## Slide 1: Rotor Hub And Pitch System
Week number : 02
Date: 07/10/2025
Supervisor: Prof. Peter Quell
Group Members :
Dhruvin Kakdiya
Adharsh Pappinisseri Veedu
Muthu Thirunavukarasu
Syed Mohammed Sikandar

## Slide 2: Agenda
07/10/2025 Dhruvin kakdiya Rotor Hub and Pitch System/Optimus syria
Comparison of Hub shape
Weighted evaluation of a pitch system
Selection of Inner or Outer ring Rotating

## Slide 3: Rotor Hub Shape Comparison
07/10/2025 Dhruvin kakdiya Rotor Hub and Pitch System/Optimus syria
Category | Star hub | Sphere hub
Aerodynamic Efficiecy | 2 | 3
Structural simplicity | 3 | 2
Manufacturing ease | 3 | 1
Maintenance access | 3 | 1
Fatigue resistance | 2 | 3
Weight | 3 | 2
Cost | 3 | 1
Suitability(Onshore) | 3 | 1
Sum | 22 | 14
1 = Low preferable, 2 = Medium preferable, 3 = High preferable

## Slide 4: Weighted Evaluation of Pitch Control Systems
07/10/2025 Dhruvin kakdiya Rotor Hub and Pitch System/Optimus syria
Criteria | Electrical Pitch | Hydraulic Pitch
Investment cost | 2 | 2
High torque | 3 | 1
Reliability | 3 | 3
Installation | 3 | 1
Operations at Hot climate | 3 | 1
Weight | 3 | 2
Service Friendliness | 3 | 2
Simple Design | 2 | 3
Sum | 22 | 15
1 = Low preferable, 2 = Medium preferable, 3 = High preferable

## Slide 5: Why Choose Electric over Hydraulic?
07/10/2025 Dhruvin kakdiya Rotor Hub and Pitch System/Optimus syria
No Hydraulic oil→ no leaks or contamination risk in hot, dusty environment.
Handles high ambient temperatures and dust reliably with IP-rated enclosures.

## Slide 6: Outer-ring rotating
07/10/2025 Dhruvin kakdiya Rotor Hub and Pitch System/Optimus syria
The blade is bolted to the outer ring and the inner ring is fixed to the hub

## Slide 7: Outer ring rotating
07/10/2025 Dhruvin kakdiya Rotor Hub and Pitch System/Optimus syria
More compact hub/lighter hub design
Simpler lubrication routing to an inner stationary ring
Pros
Cons
Higher risk of ring cracking / blade detachment
requires extra protective covers / spinner / teeth covers

## Slide 8: Inner-ring rotating
07/10/2025 Dhruvin kakdiya Rotor Hub and Pitch System/Optimus syria
The blade is bolted to the inner ring and the outer ring is fixed to the hub

## Slide 9: Inner ring rotating
07/10/2025 Dhruvin kakdiya Rotor Hub and Pitch System/Optimus syria
Safer from blade-detachment viewpoint
Pitch drives can be housed inside the hub ,simplifying environmental protection and maintenance access for the drives.
Can accommodate larger bearing diameter and more rolling elements
Pros
Cons
Hub may need to be larger to house internal drives and allow for the inner ring geometry
Internal packaging / integration is more complex (electrical routing, motor placement)

## Slide 10: Outer-ring and inner-ring rotating
07/10/2025 Dhruvin kakdiya Rotor Hub and Pitch System/Optimus syria
Topic | Outer-ring rotating (blade bolted to outer ring) | Inner-ring rotating (blade bolted to inner ring)
Which ring rotates | Outer ring rotates | Inner ring rotates
Typical pitch drive location | external or on ring perimeter | inside hub
Bearing diameter & element count | Often limited by external packaging | Easier to realize larger pitch
Assembly & maintenance | Blade bolts accessed externally | Blade bolts accessible from inside hub
Common damage modes | Outer ring hoop stresses and through-cracking near bolt holes reported in field cases | Lower incidence outer-ring through-cracks because outer ring is fixed and less stressed
Suitability | Requires reinforced outer ring and protective housings; higher inspection/maintenance attention | Preferred — allows larger diameter bearings, internal drives, improved reliability for high moments typical of 5 MW