## Slide 1: Weekly report: Team Gearbox, Brake, Coupling
Week number : 03
Date: 14/10/2025
Supervisor: Prof. Peter Quell
Nehang Jitendra Joshi
Group Members :Nehang Jitendra Joshi,Santo Mazumder,Md Razaul Karim Rahat
Presented by -Nehang Jitendra Joshi
14-10-2025
Gearbox, Brake, Coupling

## Slide 2: Agenda for 4th week
Nehang Jitendra Joshi
Team design
Basic overview about steps for design and calculation for the Gearbox
Svendborg brake as a choice
Overview for Coupling
Chapter | Responsible person
Introduction | All team members
Project order | All team members
Gearbox | Nehang
Rotor brake | Nehang+Rahat
Coupling | Nehang+Santo
Coordinate with internal group--
Rotor hub,Bearing,Machine bed (Mechanical Input)
Electrical Drivetrain Team (Mechanical Output)
Gearbox, Brake, Coupling
14-10-2025

## Slide 3: Steps for Gearbox Concept Design
Nehang Jitendra Joshi
Define gear ratio according to required input & output speed.
Define gearbox input torque according to WTGs power and gearbox input speed.
Design a gear stage including number of stages, gear split ratio and gear macro design.
Selection of bearing according to chosen gear stages.
Design of housing.
Efficiency check and design of lubrication/ cooling system.
Finalise gearbox concept design.
Gearbox, Brake, Coupling
14-10-2025

## Slide 4: Gearbox Design & Dimensioning
Nehang Jitendra Joshi
Number of Transmission Stages​
Shaft Arrangement​
Gear Type​
Module & Number of teeth​
Face width​
Material Selection
Gearbox, Brake, Coupling
14-10-2025

## Slide 5: Gearbox system
Nehang Jitendra Joshi
Dimensioning of the gearbox
  IEC-61400-4
Dimensioning of the gearbox components
  ISO 281
  ISO 76
  ISO 6336-1
Strength analysis
Modal analysis
Simulation
Gearbox Calculations​
Based on IEC 61400-4 standards
Stages module m selection
Good storage housing
1st stage: m = ?
2nd stage: m = ?
3rd stage: m = ?
Higher torques require higher module
Gearbox, Brake, Coupling
14-10-2025

## Slide 6: Gearbox system
Nehang Jitendra Joshi
Suppliers in the market:
Winergy
(Up to 8MW, eff. Of 96.5%, 2 stages low ratio gearbox)
Eickhoff
(Up to 4.8MW, 5 planet in one stage, 2 stages low ratio gearbox)
Wikof
(Up to 10MW, Flexible pin tech, 7 planets in one stage, 2 stages low ratio gearbox)
NGC
(Up to 8MW, 2 stages high ratio gearbox)
Moventas
(Up to 5MW, 2 stages low ratio gearbox)
Gearbox, Brake, Coupling
14-10-2025

## Slide 7: Rotor Brake
Main Objective:
Overview of brake
Installation of brake
Nehang Jitendra Joshi
Gearbox, Brake, Coupling
14-10-2025

## Slide 8: Rotor Brake
Nehang Jitendra Joshi
Energy supply methods:
  Hydraulic
  Electro-mechanic
Suppliers of locks:
  Hilma Römheld
  Svendborg Brakes
Suppliers of brakes
  Svendborg Brakes
Gearbox, Brake, Coupling
14-10-2025

## Slide 9: Rotor Brake
Nehang Jitendra Joshi
Main brake installation
2 option
Installation on the second generator shaft
possibility to mount the generator on the flange
Source: Optimus 200 XL Project
1 option
Installation on the HSS between gearbox and generator
Cons – mounting the generator on the frame, HSS coupling required
Source: https://www.svendborg-brakes.com/
Gearbox, Brake, Coupling
14-10-2025

## Slide 10: Rotor Brake
Nehang Jitendra Joshi
One brake calliper
Two brake callipers
Number of break calliper
Source: SMI Corporation
Svendborg Model BSAK 3000 caliper brake
Source: Optimus 200XL
Gearbox, Brake, Coupling
10
14-10-2025

## Slide 11: Rotor Brake
Nehang Jitendra Joshi
One brake calliper
Reaction force occurs
Possibility of torque
No balance
Source-Svendborg
Two brake callipers
No generation of bearing reaction forces
Achieve balance
Source-Svendborg
11
Gearbox, Brake, Coupling
14-10-2025

## Slide 12: Coupling
Main Objective:
Layout design of coupling
Design criteria
LSS and HSS coupling
Gearbox, Brake, Coupling
14-10-2025
Nehang Jitendra Joshi

## Slide 13: Coupling
Coupling Layout
Source: https://www.geislinger.com/en/products/product/compowind-coupling/
Gearbox, Brake, Coupling
14-10-2025
Nehang Jitendra Joshi

## Slide 14: Coupling
Torque transfer | Design criterion for a coupling is the torque and rotational speed it has to transfer during nominal operation | M_(N,lss) = (M_(N,gen) ∗i_gearbox)/η_gearboc
Permissible Elastic Vibratory Torque | nominal torque the coupling can transmit a vibratory torque | y="perm. elast vibratory torque" /"nominal torque" x="mean torque" /"nominal torque"
Torque overload protection | Limiting of torque after torque impulses due to electrical grid failures or generator short circuits | M_(breakdown ) = M_(N,lss)∗2.5
Permissible Misalignment | Axial Misalignment Radial Misalignment Angular Misalignment | From the calculations of tolerance
Loads deformation | Coupling housing has to sustain the loads of gearbox and generator which can results angular displacement | FEM and simulations with the finite element method (FEM)
Design Criteria
Gearbox, Brake, Coupling
14-10-2025
Nehang Jitendra Joshi

## Slide 15: Coupling
HSS Coupling
Source: https://www.geislinger.com/en/products/product/compowind-coupling/
LSS Coupling
Source-Flender arpex
Gearbox, Brake, Coupling
14-10-2025
Nehang Jitendra Joshi

## Slide 16: Bibliography
Gearbox
(1) Previous year Optimus projects
(2) IEC-61400-4
Brake
(1)Svendborg brake- https://svendborg-brakes.com/products/hydraulic-brakes/active-brakes/
Coupling
(1)Previous year project documents
(2)Geislinger and flender coupling
https://www.flender.com/en/cas/document/asm_coupling/ziuP--x-S4WQYPTrtKZFUQ/Datenblatt.pdf?refConfigId=ziuP--x-S4WQYPTrtKZFUQ&refMlfb=2LC0371-2BA99-0AF0
https://www.geislinger.com/cms_images/content/Coupling_18.0.pdf
Gearbox, Brake, Coupling
14-10-2025
Nehang Jitendra Joshi