## Slide 1: Weekly report: Load & Dynamics
Week number: 03
Date: 14/10/2025
Supervisor: Mr. Manjock
Group members: Md Aman, Arham Memon, Paresh Nakum
Presented By - Paresh Nakum
14/10/2025
Md Aman, Arham Memon, Paresh Nakum
Optimus Syria

## Slide 2: Agenda
Environmental Inputs (Syria-Relevant)
Simulated Loads
OpenFAST Load Simulation Inputs
TurbSim Input File (XY.inp)
OpenFAST Inflow File (XY_Inflow.dat)
Wind Time Series Variations
Conceptual Illustration
Future Plans
14/10/2025
Load & Dynamics Team/ Optimus Syria
Paresh Nakum

## Slide 3: Environmental Inputs
14/10/2025
3
Load & Dynamics Team/ Optimus Syria
Paresh Nakum
*data and research from wind farm group
Parameter | Typical Range / Note
Mean wind speed hub | 8-10 m/s
Turbulence intensity | 0.16
Shear exponent (α) | 0.10–0.25
Extreme gusts | From ERA5 or IEC EOG model
Air density | 1.25 kg/m³
Seismic hazard | Moderate–high (Dead Sea / East Anatolian faults)
Other | Dust storms, temperature swings, corrosion factors

## Slide 4: Simulated Loads
14/10/2025
4
Load & Dynamics Team/ Optimus Syria
Source: DNVGL-ST-0437:2016
Paresh Nakum
*DLC (“Design Load Case”) defines wind, wave, and control conditions to simulate.
Simulation Type | Goal | Typical IEC Case
Normal Operation | Evaluate fatigue and performance | DLC 1.1, 1.2,
Extreme Wind Conditions | Check survival loads | DLC 1.3, 6.1
Startup/ Shutdown/ Fault | Check transient response | DLC 2.1, 2.2, 2.3
Parked/ Standby | Idle or a storm survival | DLC 6.3

## Slide 5: OpenFAST Load Simulations
14/10/2025
5
Load & Dynamics Team/ Optimus Syria
Paresh Nakum
Parameter needs to be analyzed

## Slide 6: TurbSim Input File
Changes in the reference NREL TurbSim according to Optimus Syria Project
14/10/2025
6
Load & Dynamics Team/ Optimus Syria
Paresh Nakum
Parameter | NREL 5 MW (126 m) | Optimus Syria 5 MW (160 m)
Hub Height (m) | 90 | 120
Rotor Diameter (m) | 126 | 160
Mean Wind Speed, URef (m/s) | 8.0 – 11.4 | 7.5
Turbulence Intensity (TI) | 0.12 | 0.16
Shear Exponent | 0.14 | (0.12 – 0.18)
Roughness Length, Z₀ (m) | 0.1 | 0.03 (Not Fixed)
Turbulence Model | IECKAI (Kaimal) | IECKAI / Mann
Length Scale, Lᵤ (m) | 75 | (85 – 100)
Time Step, DT (s) | 0.05 | 0.05
Simulation Time (s) | 600 | 660
Grid Size (vertical × lateral) | 41 × 41 | (41 × 41 or 51 × 51)(Not Fixed)

## Slide 7: OpenFAST 3.0 Inflow File
14/10/2025
7
Load & Dynamics Team/ Optimus Syria
Paresh Nakum
Parameter | NREL 5-MW (126 m) | Optimus Syria 5-MW (160 m)
Rated Power | 5 MW | 5 MW
Rotor Diameter | 126 m | 160 m
Hub Height | 90 m | 120 m
Rated Wind Speed | 11.4 m/s | 7.5 m/s
Rated Rotor Speed | 12.1 rpm | 9–10 rpm (Not Fixed)
File Reference | Baseline | XY.inp
Flow Angle | 0 degree | 5-10 degree
Gearbox Ratio | 97:1 | ~100:1 (varies by design)
Tip Speed | 80 m/s | 80 m/s
Power Coefficient (Cₚ,max) | 0.482 | ~0.48–0.50

## Slide 8: Wind Time Series
14/10/2025
8
Load & Dynamics Team/ Optimus Syria
Paresh Nakum
Blue line: normal wind - fluctuates gently around 10 m/s, representing typical turbulence.
Red line: extreme wind - higher mean speed (≈12 m/s) with strong fluctuations and sudden gusts (spikes), representing rare or storm-like conditions.
You can clearly see how extreme wind files have both larger turbulence intensity and short-duration spikes, while normal wind remains relatively smooth.
*Image from other source

## Slide 9: Conceptual Illustration
14/10/2025
9
Load & Dynamics Team/ Optimus Syria
Paresh Nakum
Time (s) | Normal wind (m/s) | Extreme wind (m/s)
0 | 10.0 | 10.0
10 | 10.5 | 13.0
20 | 9.8 | 8.5
30 | 11.2 | 18.5 (gust)
40 | 10.3 | 12.0
50 | 9.7 | 16.5 (gust)
60 | 10.4 | 10.0
Normal wind file: looks like a slightly wavy signal around 10 m/s, with small, random fluctuations (turbulence intensity ≈ 10–15%).
Extreme wind file: shows violent spikes and sharp transitions — gusts up to +80% of the mean wind speed, with short correlation times.
Blue line (Normal Wind): smooth variations around 10 m/s - typical design conditions.
Red Line (Extreme Wind): sharp peaks & strong fluctuations representing gusts& severe turbulence events.

## Slide 10: Future Plan
In the next week We’ll
Configure OpenFast
Create Turbulent wind Field (precise data) with TurbSim
Start With Other parameters DLC
Connect with controller group for simulations
14/10/2025
10
Load & Dynamics Team/ Optimus Syria
Paresh Nakum

## Slide 11: References
Load Reports of the OPTIMUS projects
Loads and site conditions for wind turbines, DNVGL-ST-437,Edition November 2016
TurbSim, OpenFAST & NREL 5 MW
Load Simulation Seminar 2025 by Mr. Manjock
14/10/2025
11
Load & Dynamics Team/ Optimus Syria
Paresh Nakum