## Slide 1: Team 5 – Rotor Blade Structures
Presented by – Bhima Babu Masare (770246)
Team Members - Bhima B Masare, Anudeep Allanki, Dongsuk Kim, Mithun Shetty
Week No - 5
Date - 28.10.2025
Supervisor - Dr. Laurence Alhrshy

## Slide 2: Contents
Rotor Blade Structures Team Time line
Tasks planned for Project
Spar Cap Thickness and Deflection Analysis
  3.1 Aim
  3.2 Model Inputs and Material Parameters
  3.3 Thickness and Deflection Calculations
  3.4 Plots from MatLab
  3.5 Test-3 vs Test-2 Code Results
  3.6 Design Implications
  3.7 Results and Design Insights
  3.8 Conclusions
Bibliography
Bhima Babu Masare

## Slide 3
Bhima Babu Masare
1. Rotor Blade Structures Team Time line -
1.1 Team Time line for Month October -

## Slide 4
Mithun Shetty
2. Tasks planned for Project –
Material Selection
Spar Cap & Shear Web Thickness
Develop Blade Model in NuMAD
Analysis with Precomp
Iterate and refine the design

## Slide 5
Bhima Babu Masare
3. Spar Cap Thickness and Deflection Analysis –
3.1 Spar Cap Thickness and Deflection Analysis –
  Aim - Determine spar cap thickness for carbon and glass fiber considering strength and deflection limits
    Based on blade spanwise load and geometry data from loads.csv and thickness.csv
    Compare strength-based and stiffness-based designs
    Evaluate maximum deflection against allowable limit
    Task given by Prof. Previtali & Prof. Alhrshy

## Slide 6
Bhima Babu Masare
3. Spar Cap Thickness and Deflection Analysis –
3.1 Spar Cap Thickness and Deflection Analysis –
    Task given by Prof. Previtali & Prof. Alhrshy
Correction –
Carbon - E = 140 GPa,
Glass E = 43 GPa

## Slide 7
Bhima Babu Masare
3. Spar Cap Thickness and Deflection Analysis –
3.2 Model Inputs and Material Parameters –
  Input Tables –
    loads.csv: spanwise position & flapwise bending moments
    thickness.csv: blade thickness (distance between spar caps)
  Material Properties –
    Carbon Fiber: E = 140 GPa, σ_max = 1100 MPa, ρ = 1600 kg/m³, SF = 1.6
    Glass Fiber: E = 43 GPa, σ_max = 750 MPa, ρ = 1930 kg/m³, SF = 1.6

## Slide 8
Bhima Babu Masare
3. Spar Cap Thickness and Deflection Analysis –
3.3 Thickness and Deflection Calculations -
  Strength-based thickness –
  Moment of Inertia (two spar caps) –
  Deflection via curvature integration –
Comparing max deflection to limit (8 m)

## Slide 9
Bhima Babu Masare
3. Spar Cap Thickness and Deflection Analysis –
Test 2
Test 3
3.4 Plots from MatLab –

## Slide 10
Bhima Babu Masare
3. Spar Cap Thickness and Deflection Analysis –
Test 2
Test 3
3.4 Plots from MatLab –

## Slide 11
Bhima Babu Masare
3. Spar Cap Thickness and Deflection Analysis –
3.5 Test-3 vs Test-2 Code Results –
  Test-3: Based on Minimum thickness (no deflection limit) – deflection reached ≈ 9.85 m (beyond 8 m limit)
  Test-2: Includes deflection limit (8 m) – increases spar cap thickness to stay within limit
  Summary –
    Both start with strength-based sizing
    Updated code adds stiffness check and increases thickness when deflection > 8 m
    Ensures blade remains structurally safe and stiff

## Slide 12
Bhima Babu Masare
3. Spar Cap Thickness and Deflection Analysis –
3.6 Design Implications –
  Adding stiffness control ensures deflection stays within safe limit
  Thicker spar caps → stiffer & safer blade, but with added weight
  Final design governed by stiffness, not just strength
  Provides balanced structural and aerodynamic performance
  Overall: Improved safety, lower stress, and better blade reliability

## Slide 13
Bhima Babu Masare
3. Spar Cap Thickness and Deflection Analysis –
3.7 Results and Design Insights –
  Carbon –
    Final deflection ≤ 8 m
    Design driver: Strength / Stiffness (case-dependent)
  Glass –
    Requires greater thickness due to lower stiffness
  Final plots:
    Thickness distribution (Carbon vs Glass)
    Blade deflection curve

## Slide 14
Bhima Babu Masare
3. Spar Cap Thickness and Deflection Analysis –
3.8 Conclusions –
    Deflection limit can govern spar cap design
    MATLAB approach enables flexible spanwise optimization
    We can alter all above calculations for our Project and get the final output

## Slide 15: Bibliography
Bhima Babu Masare
Definition of a 5 MW/61.5m Wind Turbine Blade Reference Model by Brian R. Resor, Sandia National Laboratories, California, USA
Definition of a 5 MW Reference Wind Turbine for Offshore System Development, J. Jonkman, S. Butterfield, W. Musial, and G. Scott, National Renewable Energy Laboratory, USA
Reports from Optimus Shakthi 2024
Lecture Scripts from Prof. Dr. Francesco Previtali
Lecture Scripts from Prof. Dr. Laurence Alhrshy