## Slide 1: Weekly report: Feedback & Lidar – Assisted Controller
Week number: 13
Date: 23/12/2025
Supervisor: Prof. Dr.-Ing. David Schlipf
Group members: Mirza Dincer, Saurabh Pankaj Jha, Midhun Kanichattu Venu
Presenter:

## Slide 2: List of Contents
Rated Wind Speed
Steady States values
Torque Controller
Pitch Controller
Mirza Dincer

## Slide 3: Tasks of the Week
Retuning of feedback controller with updated blade configuration
Mirza Dincer

## Slide 4: Rated Wind Speed
Rated Wind speed can be found when all the parameters () set to rated values, then founding the wind speed where rotor acceleration (
The method to find is by using the fminbnd function in MATLAB, where it founds minimum value in a function, in this case our function is
In our turbine, rated wind speed is 10.8 m/s.

## Slide 5: Steady States Simulation
600 seconds of simulation.
Wind speeds from 1 m/s to 30 m/s, with increments of 1 m/s
Only enabled Rotor DOF and First fore-aft tower bending-mode DOF.

## Slide 6: Steady States
Rotational Speed [rpm]
Pitch Angles [deg]

## Slide 7: Steady States
Generator Torque [kNm]
Tower Top Position [m]

## Slide 8: Steady States
Static Power Curve

## Slide 9: Power Coefficient
Maximum power coefficient is 0.43 at TSR = 9.7 and 0 deg.

## Slide 10: Torque Controller
K value shows the relation between generator torque and generator speed for region 2.
To find the best k value, we optimized for highest power generated at a region 2 wind speed, in this case 6.5 m/s.
Starting point is 1.4273 Nm/(rad/s^2), which is the value obtained by max Cp point (0. 43 in theta = 0° and TSR = 97).
1.9273 Nm/(rad/s^2) gives the highest power.

## Slide 11: Simulation Settings for Step Response
300 seconds of simulation, to see settled values for both wind speeds.
Step wind speed, from 6 m/s to 7 m/s.
Only enabled Rotor DOF and First fore-aft tower bending-mode DOF.
Initial conditions of rotor speed and fore-aft tower top displacement.

## Slide 12: Torque Controller PI Controller
In step response of a wind turbine for below rated, we need a behavior of slightly damped (D = 0.7), and natural frequency of 2 -3 times slower than rated rotational speed.
Starting Kp chosen same as IEA 3.4 MW,
Kp = 961 [Nm/(rad/s)].
Ki = Kp / Ti, where Ti = 6 s.
In the figure, we compare the step response of different Kp values from 6 m/s to 7 m/s.
It is seen that as we increase the Kp, we get a better behavior.
Kp is chosen as 1400 [Nm/(rad/s)].

## Slide 13: Step Responses
Step response simulation from 6 to 7 m/s. Controller keeps the TSR constant for region 2.

## Slide 14: Step Responses
Step response simulation for 15 to 16 m/s.
Controller keeps the rotational speed constant for region 3.

## Slide 15: Simulation Settings for Pitch Optimization
660 seconds of simulation. Evaluation of values starts at t = 60 second to get settled values. Additionally, wind wraps around.
DLC 1.2 wind fields with average of 8 m/s to 24 m/s with steps with 4m/s, 3 seeds.
Enabled all DOFs.
Initial conditions of pitch angle, rotor speed and fore-aft tower position for every corresponding wind speed.
Mirza Dincer

## Slide 16: Pitch Optimization
Mirza Dincer
It is seen that the point Kp = -0.012 s and theta = 14° gives the lowest DEL, such that differences in AEP can be ignored because they are too small.

## Slide 17: Conclusion
Mirza Dincer
Feedback controller is ready for Optimus Syria
Continue and finish adjusting the Lidar-Assisted Controller