## Slide 1: Gearbox, Brake, Coupling
Week number : 02
Date: 30/09/2025
Supervisor: Prof. Peter Quell
Group Members :
Nehang Jitendra Joshi
Santo Mazumder
Md Razaul Karim Rahat
Arham Memon

## Slide 2: Agenda for 2nd week
Team Distibution
Concept of drive train choice
Basic idea about brake system
Insight about the coupling
Chapter | Responsible person
Introduction | All team members
Project order | All team members
Gearbox | Nehang + Arham
Rotor brake | Rahat
Coupling | Santo
Coordinate with internal group--
Rotor hub and Bearing Team (Mechanical Input)
Electrical Drivetrain Team (Mechanical Output)

## Slide 3: Drive train and Gearbox syestem
Main Objective:
Selection table for different drive train concept
Details of 3-Point suspension concept
Basic information about gearbox system
Source-Mechanical Drivetrains Prof. Peter Quell / University of Applied Sciences Kiel

## Slide 4: Drive train for CAPEX and OPEX
Source-Mechanical Drivetrains Prof. Peter Quell / University of Applied Sciences Kiel

## Slide 5
Criteria of drive train | 4Point suspension Modular | 3point suspension Semi-integrated | Integrated | hybrid | Direct drive | Max and Min
Low capex | 1 | 3 | 2 | 1 | 1 | 3 and 1
High serviceability | 3 | 3 | 1 | 1 | 1 | 3 and 1
Easy to assemble | 2 | 3 | 3 | 3 | 2 | 3 and 2
Availability of spear parts | 3 | 3 | 1 | 1 | 1 | 3 and 1
Light weight | 1 | 2 | 3 | 2 | 3 | 3 and 2
Transport | 3 | 3 | 1 | 1 | 2 | 3 and 1
Reliability | 1 | 2 | 2 | 2 | 3 | 3 and 1

## Slide 6: 3-Point suspension
Source-Y. Guo, National Renewable Energy Laboratory, 15013 Denver West Parkway, Golden, CO 80401.

## Slide 7: 3-Point suspension
Pros-
Most cost-effective concept, Elimination of the separated 2nd rotor bearing.
light weight
Shorter drivetrain
No risks of tensing the drivetrain during assembly
Cons-
-Rotor loads (forces and moments) are transferred through the housing of the gearbox into the machine bed. May damage the gearbox in case of poor design.
-Elastic coupling between gearbox and generator
Operational conditions
Long maintenance intervals
High dynamics (e.g. tower deflection)
Low stiffness of drive train foundation (machine bed)
Environmental conditions
Extreme temperatures
High humidity
Sand and Dust (deserts)
High number of lightning strikes
Earthquakes

## Slide 8: Gearbox system
Main Objective:
Types of gears
Pros and cons of each gear via table
Final recommendation

## Slide 9: Gearbox system
Source-IQS Directory
Source-Beval gear by KHK Manufactures
Source-Helical gear by MISUMI Manufactures
Source- Planetary System gears by SMC
Manufactures

## Slide 10: Gearbox system
Criteria of gears | Spur gear | Beval gear | Helical gear | Planetary gear
Design | 3 | 2 | 2 | 1
Manufacturing | 3 | 1 | 1 | 1
Space requirement | 1 | 2 | 2 | 3
Weight | 1 | 1 | 1 | 3
Transmission efficiency | 2 | 3 | 2 | 3
Reliable | 3 | 1 | 2 | 2
Cost | 2 | 1 | 2 | 1

## Slide 11: Rotor Brake
Main Objective:
Types of brake
Pros and cons for each brake system via table
Final recommendation
Rotor Brake
Yaw Brake
Aerodynamic Brake
Electrical Brake

## Slide 12: Rotor Brake
Criteria of rotor brake | Fixed caliper | Floating caliper
Design | 3 | 1
Manufacturing | 2 | 3
Space requirement | 2 | 3
Performance and pressure | 3 | 1
Weight | 2 | 3
Maintenance and Reliability | 3 | 2
Cost | 2 | 2

## Slide 13: Coupling
Main Objective:
Types of coupling
Pros and cons for each coupling via table
Final recommendation
Flexible Coupling
Disc Coupling
Rubber-Hydraulic Coupling
Composite Coupling

## Slide 14: Coupling
Criteria of Coupling | Disc Coupling | Rubber-Hydraulic Coupling | Composite Coupling
Design | 2 | 2 | 2
All kind of Protection | 1 | 2 | 3
Efficiency | 3 | 1 | 3
Service and Maintenance | 3 | 2 | 2
Reliability and weight | 1 | 2 | 3
Cost | 2 | 2 | 1

## Slide 15: Bibliography
https://www.twiflex.com/en/newsroom/2016/02/is-caliper-brake-solutions-for-wind-turbines
https://antec-group.com/wp-content/uploads/2021/12/Catalogo-Wind-2022.pdf
https://www.twiflex.com/en/newsroom/2016/02/is-caliper-brake-solutions-for-wind-turbines
https://www.windsourcing.com/en/spare-parts-and-repair-material/brakes/brake-calipers/
https://www.ktr.com/de/en/products/brake-systems/
https://www.zf.com/products/en/wind/home/wind.html#:~:text=Empowering%20a%20Sustainable%20Future%20Together&text=ZF%20Wind%20Power%20develops%2C%20together,future%20together%20with%20our%20partners.
https://www.flender.com/en/branchesAndApplications/winergy#:~:text=Two%20powerful%20brands%20%2D%20one%20company,wind%20for%20a%20better%20future.