## Slide 1: Weekly report: Machine Bed & Yaw System
Shoukat Abbas, Luksh Chawla, Sathishkumar Venkatachalam, Shrihari G Kadam
Week No - 8
Date: 18.11.2025
Supervisor: Prof. Peter Quell
Presented by – Shoukat Abbas

## Slide 2: Contents
Shoukat Abbas
Yaw Bearing Finalized Dimensions
Yaw Bearing CAD Model
Yaw brake disc and brake callipers
Initial CAD design assumptions (Casted part)
References

## Slide 3: Yaw Bearing Final Dimensions
Shoukat Abbas
Double-row four-point bearing with External Gears
Teeth Profile
2D drawing from own 3D part

## Slide 4: Yaw Bearing Tooth Profile
Shoukat Abbas
Tooth profile bearing
Tooth profile pinion
Pressure angle = 20°
Module m = 24

## Slide 5: Yaw Bearing 3D Model
Shoukat Abbas
Top view
Tooth profile close-up
Cross-sectioned view

## Slide 6: Brake Calipers selection and calculation
Shoukat Abbas
Our recommendations are the BSAC 120 or BSAB 120 brake from Svendborg Company. I have already contacted the company for one week, hoping to get their reply this week.
Source: Svendborg-brakes/hydraulic-brakes
Svendborg BSAC120
Svendborg BSAB120
[1], [2]
We have done the calculations of brake calipers, we are waiting for a reply from the manufacturer. We will present in next week. Including the parameters and calculation, no. of brake calipers for Optimus Syria are more or less 15.

## Slide 7: Yaw Brake Disc and Brake Calipers
Shoukat Abbas
Yaw brake Svendborg BSAC120 - Specification
Brake Pad:
Pad width: 138 mm
Pad area (organic): 58,500 mm²
Maximum pad wear (organic): 7 mm (pad thickness = 14 mm)
Nominal friction coefficient: µ = 0.4
Hydraulic Characteristics:
Total piston area (each caliper): 678.6 cm²
Hydraulic Volume:
Volume per caliper at 1 mm stroke: 67.8 cm³
Volume per caliper at 3 mm stroke: 203.5 cm³
Operating Pressure:
Maximum operating pressure: 20.5 MPa
Minimum operating pressure: 9.0 MPa
Operating Conditions
General temperature range: –20°C to +70°C
Wind turbine temperature range: –40°C to +60°C
[1], [2]

## Slide 8: Bed Casting – Start modelling (Initial phase)
Shoukat Abbas
We have started CAD modelling of the bed (casted part). We will modify according to requirements.
Placement of yaw drives is a bit technical, but we’re working on it and will come to an outcome as soon as possible.

## Slide 9: References
Shoukat Abbas
    [1]. Hydraulic brakes Svensborg brakes, https://www.svendborg-brakes.com/products/hydraulic-brakes/active-brakes/bsac-120/ (accessed: 13.11.2025)
    [2]. Hydraulic brakes Svensborg brakes, Svendborg-brakes /product-catalogue/ (accessed: 13.11.2025)