## Slide 1
Date: 25 November 2025

## Slide 2: Weekly report: Team Gearbox, Brake, Coupling
Week number : 09
Date: 25/11/2025
Supervisor: Prof. Peter Quell
Group Members :Nehang Jitendra Joshi,Santo Mazumder,Md Razaul Karim Rahat
Presented by -Nehang Jitendra Joshi
25-11-2025
Gearbox, Brake, Coupling

## Slide 3: List of Content
1.Calculation of the 1st stage of planetary gear and 2nd stage also Spur gear stage calculation updated
2.Material selection overview
3.Bearing selection overview
4.Displacements on Coupling
Gearbox, Brake, Coupling
25-11-2025

## Slide 4: Formulas for Planetary gear
Gearbox, Brake, Coupling
25-11-2025
z = No. of Teeth
n = RPM
D = Pitch Circle Diameter
i = Gear Ratio
Reference: Lecture Notes by Prof. Peter Quell
z_Ring | z_Sun +( 2 x z_Planet)
z_Planet | z_Sun - z_Ring / 2
No. of Planets | 5 and 4
D_Sun | z_Sun x Module
D_Planets | (D_Ring /2) – (D_Sun/2)
D_Ring | z_Ring x Module
Gap | (D_Sun + D_Planets) * Pi / (No. of Planets) - D_Planets
Face Width | 10 x Module
Tooth Depth | 2.25 x Module
n_Ring | 0
n_Planet Carrier | 10.12 rpm
n_Sun | (1-i_1) x n_Planet Carrier
i_Sun,Planet | z_Planet / z_Sun
n_Planet | n_Sun / i_Sun,Planet

## Slide 5: 1st Stage of planetary
Gearbox, Brake, Coupling
25-11-2025
Module mm | 15
z_Sun | 34
z_Ring | 136
z_Planet | 51
No. of Planets | 5
(z_Sun + z_Ring)/No. of Planets | 34
Tooth Depth | 33.75
D_Sun (mm) | 510
I-1 ratio | 5
Reference: Lecture Notes by Prof. Peter Quell and PSGdesign book
D_Planets (mm) | 765
D_Ring (mm) | 2040
Gap (mm) | 16.77
Face Width | 150
n_Ring (rpm) | 0
n_Planet Carrier (rpm) | 10.12
n_Sun (rpm) | 40.48
i_Sun,Planet | 1.5
n_Planet (rpm) | 26.98

## Slide 6: 2nd Stage of planetary
Gearbox, Brake, Coupling
25-11-2025
Module mm | 12
z_Sun | 37
z_Ring | 147
z_Planet | 55
No. of Planets | 4
(z_Sun + z_Ring)/No. of Planets | 46
Tooth Depth | 27
D_Sun (mm) | 444
I-2 ratio | 4.9
Reference: Lecture Notes by Prof. Peter Quell and PSGdesign book
D_Planets (mm) | 660
D_Ring (mm) | 1764
Gap (mm) | 6.73
Face Width | 120
n_Ring (rpm) | 0
n_Planet Carrier (rpm) | 40.48
n_Sun (rpm) | 473.61
i_Sun,Planet | 1.48
n_Planet (rpm) | 106.66

## Slide 7: Spur gear stage
Gearbox, Brake, Coupling
25-11-2025
I-3 ratio | 4.9
Module mm | 14
Center distance mm | 602
No of teeth on pinion | 108
No.teeth on gear | 22
Width of the gear mm | 140
Hight factor mm | 1
Tooth depth mm | 31.5
Bottom clearance | 2.25
Dia of input shaft mm | 100
Dia of output shaft mm | 185
PCD of pinion | 1512
PCD of gear | 308
Face width | 140
Input shaft rpm | 473.61
Output shaft rpm | 1200
Reference: Lecture Notes by Prof. Peter Quell and PSGdesign book

## Slide 8
Gearbox, Brake, Coupling
25-11-2025
Material selection overview
No | Components | Material
1 | Gearbox housing | Cast iron (GJS 400-18-LT)
2 | Gears | 18CrNiMo 7-6 grade steel
3 | Coupling | Cast iron (GJS 400-18-LT)
4 | Brake | Cast iron (GJS 400-18-LT)

## Slide 9
Gearbox, Brake, Coupling
25-11-2025
Gears Material Specification
Reference: Lucefin website and Optimus shakti

## Slide 10
Gearbox, Brake, Coupling
25-11-2025
Gears Material Specification
Reference: Lucefin website

## Slide 11
Gearbox, Brake, Coupling
25-11-2025
Bearing selection overview
coroll.cz website

## Slide 12
Gearbox, Brake, Coupling
25-11-2025
Bearing selection overview
SKF website

## Slide 13: Displacements on Coupling
Gearbox, Brake, Coupling
25-11-2025
For the high-speed shaft all radial, axial and angular displacements between
Gearbox and Generator.
Front Rotor Bearing.
Compensation of displacement by:
Movement between gearbox and generator
Elastic deformation
Production tolerances
Thermal expansion
Bearing clearance
Source: Quell, P.: Lecture note ‚Machinery Components

## Slide 14: Bibliography
Gearbox
(1) Previous year Optimus projects(60E,92LE,Shakti 21-11-2025
(2) Roloff Matek Maschinenelemente 21-11-2025
(3) Lecture notes – Mechanical drive train by Prof.Peter Quell.22-11-2025
(4)Shigley's mechanical engineering design and PSG data book 20-11-2025
(5)Lucefin website 22-11-2025
(6)Bearing-coroll.cz and SKF website 22-11-2025
Coupling
(1)Lecture notes-Machinery Components by Prof.Peter Quell 21-11-2025
Gearbox, Brake, Coupling
25-11-2025