## Slide 1
Date: 25 November 2025

## Slide 2
Weekly Presentation : Rotor Bearing System
Week number: 09
Date: 25 /11/2025
Supervisor: Prof. Peter Quell
Group members: Divyesh Mistry, Venkata Sreekanth .K , Sreehari Padachery, Jill Sadariya
Presenter : Sreehari Padachery

## Slide 3: Agenda
Bearing Housing.
Rotor Lock.
Rotor Lock pin Calculations.
Rotor Lock Disc Calculations.
Shaft Flange.
Task Performed up to now
Bibliography.

## Slide 4: Bearing Housing
parameter | value
OD | 2500mm
Rib radius | 1400mm
ID/Bore dia | 2240mm
Width | 630mm
Total length | 3200mm

## Slide 5: Rotor Lock
Source: ROEMHELD
The ROEMHELD rotor lock works with hydraulic or electromechanical locking mechanism and withstands side loads up to 5,500 kN.
Temperature range from – 30°C to + 70 °C.

## Slide 6: Rotor Lock pin Calculations
Allowable bending stress of the steel material = 0.66fy (As per Steel Design Indian Standard (IS) 800, American Institute of Steel Construction (AISC) ASD 9th Edition
Where Yield strength of the material 30NiCrMo16-6 , fy = 880 MPa or 880 N/mm2
Allowable bending stress of the material 30NiCrMo16-6 = 0.66* 880
=580.8 N/mm2
From DIN EN 10083-3,Table 8

## Slide 7: Rotor Lock pin Calculations
L1
L2
D2
D1
==1043930.268
D= D1 = 219.9 = 220 mm
Length of Lock pin L1+L2 = 930 mm
D2 = 220-30=190mm
L2= 15mm

## Slide 8: Rotor Lock Disc Calculations
where, Lock pin hole circle radius r = 1425mm
As per Prof. Peter Quell the load case with Maximum Torque of 2.5*MXR rated = 12800KNm
Bending Moment acting on the Lock pin , Mbpin=F*L
( From Optimus Shakti and 60 E)
Thickness =Thickness of Flange+ Width of Lock disc = 150+100= 250 mm
Thickness
Mbpin=F*L= 606314.7 KNmm
Source: Machinery Components, Prof. Peter Quell

## Slide 9: Rotor Lock Disc Calculations
pressure acting on the hole of the disk ,
The disk hole = Diameter of lock pin +3mm = 220+3= 223 mm
Pressure acting area of the hole, A=223*135=30105 mm2

## Slide 10: Shaft Flange
Description | Symbol | Value | Unit
Outer screw circle diameter | dt2 | 1900 | mm
Inner screw circle diameter | dt1 | 1740 | mm
No. of screws per bolt circle diameter | Ntotal = NICB + NOCB | 63+68=131 | 
Hole dia for M36 bolts = 39 mm (36+3mm)
Rotor lock hole circle diameter = 2850 mm (Assumed based on feed back drawing)
Flange outer dia = 2850 +50 = 2900mm
e
Source: Machinery Components, Prof. Peter Quell
Circumference C1= =5463.6 mm
Total number of Holes = = =63

## Slide 11: Task Performed up to now
Group Members | Components
Divyesh Mistry & Venkata Sreekanth.k | Rotor Shaft
Sreehari Padachery & Jill Sadariya | Spherical Roller Bearing
Sreehari Padachery& Jill Sadariya | Rotor Lock Pin
Venkata Sreekanth.k& Divyesh Mistry | Rotor Lock Disc
Sreehari Padachery | Bearing Housing

## Slide 12: Bibliography – Rotor Bearing System
SKF. (n.d.). 240/1120 CAF/W33 - Spherical roller bearings. Retrieved October 29, 2025, from https://www.skf.com/group/products/rolling-bearings/roller-bearings/spherical-roller-bearings/productid-240%2F1120 CAF%2FW33
Optimus Shakti, Optimus 60E
ITH. (n.d.). ITH Hydraulic Torque Wrenches Catalog. Retrieved November 08, 2025, from www.ITH.de/schraubwerkzeuge/hydraulische-drehmomentschrauber
Römheld GmbH Friedrichshütte. (n.d.). Rotorlock. Retrieved November 24, 2025, from https://www.rotorlock.de/en
Machinery Components, Prof. Peter Quell
DIN EN 10083-3: Steels for quenching and tempering – Part 3: Technical delivery conditions for alloy steels. Retrieved November 22, 2025, from https://studylib.net/doc/18166049/din-en-10083-steel-for-quenching-and-tempering-part-3-
American Institute of Steel Construction. (1989). Manual of Steel Construction: Allowable Stress Design (9th ed.). Chicago, IL: Author. Retrieved November 22, 2025, from Internet Archive (Manual of Steel Construction: Allowable Stress Design, 9th Edition)
Bureau of Indian Standards. (2007). IS 800: General Construction in Steel—Code of Practice (Third Revision). New Delhi: Bureau of Indian Standards. Retrieved November 22, 2025, from Internet Archive (IS 800: General Construction in Steel - Code of Practice)