## Slide 1
Date: 16 December 2025

## Slide 2: Weekly report: Team Gearbox, Brake, Coupling
Week number : 12
Date: 16/12/2025
Supervisor: Prof. Peter Quell
Group Members :Nehang Jitendra Joshi,Santo Mazumder,Md Razaul Karim Rahat
Presented by -Md Razaul Karim Rahat
16-12-2025
Gearbox, Brake, Coupling

## Slide 3: List of Content
Md Razaul Karim Rahat
Gearbox calculation and design
Brake calculation and design
Coupling calculation and design
Weight and Cost calculations
Gearbox, Brake, Coupling
16-12-2025

## Slide 4: Gearbox parameter calculation
Md Razaul Karim Rahat
Gearbox, Brake, Coupling
16-12-2025
Parameter | Value
Input torque,Mi KN m | 5,095
Output torque,Mo KN m | 41,9
Input speed, rpm | 10.15
Output speed, rpm | 1200
Parameter | Value | Unit
I gearbox | 120 | -
η gearbox | 0.97 | %
M N, Generator | 5.6169 | KNm
M N, Rotor | 411.55 | KNm

## Slide 5: Gearbox Coupling Torque calculation
Md Razaul Karim Rahat
Torque transfer
These values considered the losses of the different electrical components like generator, converter, and transformer. From this torque and the efficiency (97%) and ratio (120) of the gearbox, the nominal torque at the low-speed shaft 𝑀𝑁,𝑙𝑠𝑠 can be calculated as following
41.9 *120 / 0.97 = 5,183.50 KNm
Torque overload protection
For this, a breakdown torque of the coupling of 2.5 times the nominal torque is required by industry experience. The components behind the coupling are designed to withstand a higher torque than this breakdown torque, so that the coupling will fail first and the other components are protected in cases of overloads.
Mn,lss * 2.5 = 12,958.75 KNm - Breakdown
Gearbox, Brake, Coupling
16-12-2025

## Slide 6: Gearbox calculation
Md Razaul Karim Rahat
Gearbox, Brake, Coupling
16-12-2025
Items | Values
Power from main shaft (P), kW | 550
Rotational speed of main shaft (N), rpm | 10.15
Number of teeth on sun gear (NS) | 37
Number of teeth on ring gear (NR) | 115
Straight-line distance between torque arms (D), m | 3.2
Self-weight of the gearbox (W), kg | 11700
Torque of planet carrier (TC), Nm | 330062
Torque of sun gear (TS), Nm | 72382
Torque of ring gear (TR), Nm | 257680
Gear ratio (u) | 5
Torque arm load from the ring gear torque (PR), N | 151576
Torque arm load from the self-weight of the gearbox (PO), N | 26977
Torque arm design load (PT), N | 357107
Shear stress, tensile & bending strength of torque arm pin (τD),(σT) and (σb), Mpa | 15.7, 31.5, 8.3
Length of elastomeric bushing (L), mm | 220

## Slide 7: Gearbox elastomeric bearing calculation
Md Razaul Karim Rahat
Gearbox, Brake, Coupling
16-12-2025
Material using for Pin : EN-GJS-400-18-LT
Source: FKM Guidelines

## Slide 8: Gears geometry calculation
Md Razaul Karim Rahat
Gearbox, Brake, Coupling
16-12-2025
Parameter | Formula | 1st stage | 2nd stage | 3rd stage
Input torque |  | 5,095 | 23.8 | NA
Output torque |  | 23.8 | 41.9 | NA
Pitch diameter,d (mm) | m*zp m*zs m*zr | ds-592, dp-624 , dr-1840 | ds-490 , dp-525 , dr-1540 | 1200 and 336
Outer dia ,Do (mm) | D0=(z+2).m | Ds-642,dp-676,dr-1900 | Ds-540,dp-560,dr-1600 | NA
Addendum,a(mm) | a=m | 16 | 14 | 2
Dedendum,b(mm) | b=1.25*m | 20 | 17.5 | 11.25
Face width,(mm) | 10 * module | 160 | 140 | 120

## Slide 9
Md Razaul Karim Rahat
Gearbox, Brake, Coupling
16-12-2025
Cast iron,Mechanical Properties

## Slide 10: Force analysis, Stress, and Safety Factors (Zr-Ring gear)
Md Razaul Karim Rahat
Gearbox, Brake, Coupling
16-12-2025
Parameter | Formula | 1st stage | 2nd stage
Input torque,M (MNm) | Mi-5,095 M2=M1/i1 | 5,095 | 1.01
Tangencial force,Ft (MN) |  | 3.481 | 0.788
Radial force Fr (MN) |  | 1.567 | 0.587
Bending stress (m (MPa) |  | 137.89 | 92.67
Contact stress C,(MPa) |  | 216.57 | 170.34
Factor of safety (Bending) |  | 2.45 | 3.2
Factor of safety (Contact) |  | 1.38 | 2.11

## Slide 11
Md Razaul Karim Rahat
Gearbox, Brake, Coupling
16-12-2025
3D model Gearbox
Reference: Own design
Parameter | 
Ratio | 120
Stages | 3
Length | 1522 mm
Width | 3200 mm
Pin to pin distance | 2700 mm

## Slide 12
Md Razaul Karim Rahat
Gearbox, Brake, Coupling
16-12-2025
3D model Gearbox
Reference: Own design

## Slide 13: Gearbox elastomeric bearing
Md Razaul Karim Rahat
Gearbox, Brake, Coupling
16-12-2025
Source: ESM

## Slide 14
Md Razaul Karim Rahat
Gearbox, Brake, Coupling
16-12-2025
3D model Brake
Reference: Own design
Parameter | 
Type | Svendborg 300 dual action
Length | 220 mm
Width | 167 mm
Weight | 62 Kg

## Slide 15
Md Razaul Karim Rahat
Gearbox, Brake, Coupling
16-12-2025
Reference: Svendborg
BSAK 300 Dual-Action
Hydraulic pressure applied and spring return.
Clamping force: 0 to 55.000 N
Nominal braking force: 0 to 44.800 N
To bring a drivetrain that is operating at a reduced/idling speed to a complete stop and provides holding functionality.
Why svendborg..?
Developed a series of hydraulically-applied caliper brakes.
Provide easy maintenance and friction pad replacement.
Also feature corrosion protection, monitoring systems (on-off switch, pad wear monitor, etc.).
high thermal dissipation during dynamic braking
Selection of the brake caliper

## Slide 16: Brake calculation
Md Razaul Karim Rahat
Gearbox, Brake, Coupling
16-12-2025

## Slide 17: Brake calculation
Md Razaul Karim Rahat
Gearbox, Brake, Coupling
16-12-2025

## Slide 18
Md Razaul Karim Rahat
Gearbox, Brake, Coupling
16-12-2025
3D model Coupling
Reference: Own design
Parameter | 
Model | KTR RADEX NANA
Length | 945 mm
Disc Radius | 450 mm
Weight | 170 Kg

## Slide 19: Coupling Torque calculation
Md Razaul Karim Rahat
Coupling
Calculate the compensating torque applied to the coupling
Md=Md rotor * K = 5,095* 1.5 =7.6425 MNm
Nominal Torque = 3,979.16 Nm
Gearbox, Brake, Coupling
16-12-2025
TkN = 5,769.791667 Nm, On Considering Size Factor as 1.45
According to the Calculated Torque , The size of the High-speed shaft side could be chosen as 115mm With 6 Holes

## Slide 20: Coupling size overview
Md Razaul Karim Rahat
Gearbox, Brake, Coupling
16-12-2025
Source-KTR

## Slide 21
Md Razaul Karim Rahat
Gearbox, Brake, Coupling
16-12-2025
Weight and Cost estimation
No | Components | Weight estimation | Cost estimation
1 | Gearbox | 11700 Kg | 53000 €
2 | Elastomeric bearing | 58 Kg | 261 €
3 | Brake caliper | 62 Kg | 279 €
4 | Coupling | 170 Kg | 765 €
Total Weight | 11,990 Kg
Total cost | 55000-65000 €
Source-https://www.indexbox.io/search/cast-iron-price-per-kg

## Slide 22: Bibliography
Md Razaul Karim Rahat
Gearbox
Previous year Optimus projects(60E,92LE,Shakti 14-12-2025
Roloff Matek Maschinenelemente 14-12-2025
Lecture notes – Mechanical drive train by Prof.Peter Quell.13-12-2025
Shigley's mechanical engineering design and PSG data book 12-12-2025
DNV and IEC-61400-4 guidelines 13-12-2025
Brake
Svendborg handbook 14-12-2025
Previous year Optimus projects(60E,92LE,Shakti 13-12-2025
Coupling
KTR handbook 15-12-2025
Previous year Optimus projects(60E,92LE,Shakti 14-12-2025
Gearbox, Brake, Coupling
16-12-2025