## Slide 1
Date: 16 December 2025

## Slide 2
Weekly Presentation : Rotor Bearing System
Week number: 12
Date: 16 /12/2025
Supervisor: Prof. Peter Quell
Group members: Divyesh Mistry, Venkata Sreekanth .K , Sreehari Padachery, Jill Sadariya
Presenter : Divyesh Mistry

## Slide 3: Agenda
Bearing
Bearing Housing.
Shaft.
Rotor Lock Disc.
Rotor Lock Pin.
Lock nut
Rotor Bearing Assembly.
Lock pin calculation using new Load cases
Bibliography.
Divyesh Mistry

## Slide 4: Bearing
Divyesh Mistry
parameter | value | unit
Bore diameter | 1600 | mm
Outer diameter | 2240 | mm
Total width | 630 | mm
Rollers per row | 28 | numbers
Roller diameter | 131.60 | mm
Roller length | 249 | mm
Safety factor | 09 | 
(Own Design)

## Slide 5: Bearing Housing
Divyesh Mistry
parameter | value | unit
OD | 2500 | mm
ID/Bore dia | 2240 | mm
Width | 720 | mm
Total lenght | 3200 | mm
Rib Radius | 1400 | mm
Length of the Legs | 1000 | mm
(Own Design)

## Slide 6: Rotor Shaft
Description | Symbol | Value | Unit
Outer screw circle diameter | dt2 | 2450 | mm
Inner screw circle diameter | dt1 | 2250 | mm
No. of screws per bolt circle diameter | Ntotal = NICB + NOCB | 94+102=196 | 
Integrated rotorlock Flange outer dia | Dflange | 3190 | mm
Integrated Flange Thickness | t | 200 | mm
Gear box Side Flange
Description | Symbol | Value | Unit
screw circle diameter | dt1 | 1464 | mm
No. of screws per bolt circle diameter | Ntotal | 46 | 
Flange outer dia | Dflange | 1584 | mm
Hub Side Flange
Divyesh Mistry
(Own Design)

## Slide 7: Rotor Lock Disc
Divyesh Mistry
*Value we assigned based on our assumption
Source: LLM(Large Language Models).
Blade & Reference Angle | 1-pin Angle | 2-pin Angle
1st Blade (0∘) | 15 | 165
2nd Blade (0∘) | 255 | 45
3rd Blade (0∘) | 135 | 285
1st Blade (90∘) | 285 | 75
2nd Blade (90∘) | 165 | 315
3rd Blade (90∘) | 45 | 195
(Own Design)

## Slide 8: Rotor Lock Pin
parameter | value | unit
L1 | 280 | mm
L2 | 40 | mm
D2 | 160 | mm
D1 | 220 | mm
L1
L2
D2
D1
(Own Design)

## Slide 9: Lock Nut
Thread | Outer diameter | Width | Gap width | Thread for mounting lever
G | d3​ | B | b | G1​
Tr 1600x 8 | 1750 | 110 | 40 | M24
(Own Design)

## Slide 10: Rotor Bearing Assembly
Divyesh Mistry
(Own Design)

## Slide 11: Lock pin calculation using new Load data
where, Lock pin hole circle radius r = 1425mm
Torsional moment Mt= 24435 KN.m ( 250% * Rated Torque (9774KN.m)
Thickness of Integrated rotor lock disc = Flange thickness+thickness of disc= 200 mm
Bending Moment acting on the Lock pin ,Mbpin=F*L
Mbpin= 943105.2 KNmm
Allowable bending stress of the steel material = 0.66fy (As per Steel Design Indian Standard (IS) 800, American Institute of Steel Construction (AISC) ASD 9th Edition
pressure acting on the hole of the disk ,
Source: Optimus Shakti

## Slide 12
Material | Yield Strength | Case 1 (σ = fy) | Case 2 (σ = 0.66 fy)
30 NiC rMo16-6 | 880 MPa | 221.84 mm | 254.79 mm
42CrMo4 | 500 MPa | 267.83 mm | 307.61 mm
Difference | -380 MPa | +46 mm | +53 mm
Source: Optimus Shakti
(From DIN EN 10083-3,Table 8)
pressure acting on the hole of the disk ,
Area (A) = Hole Diameter* Thickness of flange

## Slide 13
Material | Case (Yield Strength Basis) | Pin Diameter (mm) | Hole Diameter (mm) | Area (mm²) | Pressure (N/mm²)
30 NiCrMo16-6 | Case 1 (σ=fy​) | 221.84 | 224.84 | 44,968 | 190.66
30 NiCrMo16-6 | Case 2 (σ=0.66fy​) | 254.79 | 257.79 | 51,558 | 166.29
42CrMo4 | Case 1 (σ=fy​) | 267.83 | 270.83 | 54,166 | 158.29
42CrMo4 | Case 2 (σ=0.66fy​) | 307.61 | 310.61 | 62,122 | 138.01

## Slide 14: Bibliography – Rotor Bearing System
Optimus Shakti, Optimus 60E
ITH. (n.d.). ITH Hydraulic Torque Wrenches Catalog. Retrieved November 08, 2025, from www.ITH.de/schraubwerkzeuge/hydraulische-drehmomentschrauber
DIN EN 10083-3: Steels for quenching and tempering – Part 3: Technical delivery conditions for alloy steels. Retrieved November 22, 2025, from https://studylib.net/doc/18166049/din-en-10083-steel-for-quenching-and-tempering-part-3-
American Institute of Steel Construction. (1989). Manual of Steel Construction: Allowable Stress Design (9th ed.). Chicago, IL: Author. Retrieved November 22, 2025, from Internet Archive (Manual of Steel Construction: Allowable Stress Design, 9th Edition)
LLM(Large Language Models).
Germanischer Lloyd Industrial Services GmbH, Renewables Certification. (2010). Guideline for the certification of wind turbines.
Boltport Fasteners. (n.d.). DIN 125 Flat Washers Weights Chart. Retrieved December 8, 2025, from https://boltport.com/weights/din-125/
M. Wilhelmsen A/S. (n.d.). STEEL BOLT M48X240 10.9 DIN 931. Abgerufen am 8. Dezember 2025, von https://ehandel.mw.dk/en/steel-bolts-din-931/steel-bolt-m48-109
Divyesh Mistry