## Slide 1
Date: 18 November 2025

## Slide 2: Weekly report: Team Gearbox, Brake, Coupling
Week number : 08
Date: 18/11/2025
Supervisor: Prof. Peter Quell
Group Members :Nehang Jitendra Joshi,Santo Mazumder,Md Razaul Karim Rahat
Presented by -Nehang Jitendra Joshi
18-11-2025
Gearbox, Brake, Coupling

## Slide 3: List of Content
1.Calculation of the 1st stage of planetary gear and 2nd stage also Spur gear stage calculation updated
2.Steps of Pin for Elastomeric Bearing
3.Hss coupling calculation
Gearbox, Brake, Coupling
18-11-2025

## Slide 4: Formulas for Planetary gear
Gearbox, Brake, Coupling
18-11-2025
z = No. of Teeth
n = RPM
D = Pitch Circle Diameter
i = Gear Ratio
Reference: Lecture Notes by Prof. Peter Quell
z_Ring | z_Sun +( 2 x z_Planet)
z_Planet | z_Sun - z_Ring / 2
No. of Planets | 5 and 4
D_Sun | z_Sun x Module
D_Planets | (D_Ring /2) – (D_Sun/2)
D_Ring | z_Ring x Module
Gap | (D_Sun + D_Planets) * Pi / (No. of Planets) - D_Planets
Face Width | 10 x Module
Tooth Depth | 2.25 x Module
n_Ring | 0
n_Planet Carrier | 10.12 rpm
n_Sun | (1-i_1) x n_Planet Carrier
i_Sun,Planet | z_Planet / z_Sun
n_Planet | n_Sun / i_Sun,Planet

## Slide 5: Calculation for 1st stage of planetary
Gearbox, Brake, Coupling
18-11-2025
Module mm | 16
z_Sun | 34
z_Ring | 126
z_Planet | 46
No. of Planets | 5
(z_Sun + z_Ring)/No. of Planets | 32
Tooth Depth | 36
D_Sun (mm) | 544
I-1 ratio | 5.2
Reference: Lecture Notes by Prof. Peter Quell and PSGdesign book
D_Planets (mm) | 736
D_Ring (mm) | 2016
Gap (mm) | 573.44
Face Width | 160
n_Ring (rpm) | 0
n_Planet Carrier (rpm) | 10.12
n_Sun (rpm) | 42.50
i_Sun,Planet | 1.35
n_Planet (rpm) | 31.48

## Slide 6: Calculation for 2nd stage of planetary
Gearbox, Brake, Coupling
18-11-2025
Module mm | 9
z_Sun | 40
z_Ring | 100
z_Planet | 30
No. of Planets | 4
(z_Sun + z_Ring)/No. of Planets | 35
Tooth Depth | 20.25
D_Sun (mm) | 360
I-2 ratio | 4.7
Reference: Lecture Notes by Prof. Peter Quell and PSGdesign book
D_Planets (mm) | 270
D_Ring (mm) | 900
Gap (mm) | 137.25
Face Width | 90
n_Ring (rpm) | 0
n_Planet Carrier (rpm) | 78.4
n_Sun (rpm) | 516.56
i_Sun,Planet | 0.75
n_Planet (rpm) | 688.74

## Slide 7: Spur gear stage calculation
Gearbox, Brake, Coupling
18-11-2025
I-3 ratio | 4.8
Module mm | 9
Center distance mm | 585.8
No of teeth on pinion | 108
No.teeth on gear | 22
Width of the gear mm | 90
Hight factor mm | 1
Tooth depth mm | 20.25
Bottom clearance | 2.25
Dia of input shaft mm | 50
Dia of output shaft mm | 85
PCD of pinion | 972
PCD of gear | 198
Face width | 90
Input shaft rpm | 516.56
Output shaft rpm | 1200
Reference: Lecture Notes by Prof. Peter Quell and PSGdesign book

## Slide 8
Gearbox, Brake, Coupling
18-11-2025
Overview gearbox data

## Slide 9
Gearbox, Brake, Coupling
18-11-2025
Steps of Pin for Elastomeric Bearing

## Slide 10
Gearbox, Brake, Coupling
18-11-2025

## Slide 11
Gearbox, Brake, Coupling
18-11-2025

## Slide 12
Gearbox, Brake, Coupling
18-11-2025

## Slide 13
Gearbox, Brake, Coupling
18-11-2025

## Slide 14: Torque and rotational speed calculation for Rotor and Generator
Gearbox, Brake, Coupling
18-11-2025
Rotor side | 
P rotor | 5.4 MW
nlss | 10.12 rpm
M rotor | 5,095 KN m
Generator side | 
nhss | 1200 rpm
Ratio i | 1200 /10.12 = 118.57
M generator | 41.9 KNm

## Slide 15: Hss coupling calculation
Gearbox, Brake, Coupling
18-11-2025
Hss nominal torque Mn.gen - 41.9 KNm
Breakdown fator k-2.5 T allowable 100 n/mm^2
Md.hss=MNgen*k = 41.9 KNm * 2.5 = 104.75 KNm
Minimum diameter . Dhss= 3 (16*104.75*10^6 )N.mm/ 3.14 *100 N/mm^2
Dhss = 174.73 mm

## Slide 16: Torque calculation for HSS coupling radex NANA
Gearbox, Brake, Coupling
18-11-2025
Nominal torque = P- 5.4 * 10^6 W Nhss= 1200 rpm
TN = p *60 / 2*3.14*1200
= 5.4 * 10^6 *60 / 2*3.14*1200 = 42971.835 Nm

## Slide 17
Gearbox, Brake, Coupling
18-11-2025
Medium or highspeed shaft calculation nN,mss = nNlss * I gearbox
= 10.12 rpm * 118.57 = 1199.93 rpm
Nominal low speed shaft calculation (MN,Lss)
MN,Lss = MN gen * I gearbox / n gearbox
= 41.9 KNm * 118.57 / 0.97 = 5121.74 KNm
Breakdown torque (Mbreakdown) = MN.lss * 2.5 = 12804.38 KNm
Torque calculation for HSS coupling radex NANA

## Slide 18: Bibliography
Gearbox
(1) Previous year Optimus projects(60E,92LE,Shakti 15-11-2025
(2) Roloff Matek Maschinenelemente 13-11-2025
(3) Lecture notes – Mechanical drive train by Prof.Peter Quell.14-11-2025
(4)Shigley's mechanical engineering design and PSG data book 14-11-2025
(5)thecatalystis.com website 15-11-2025
Gearbox, Brake, Coupling
18-11-2025