## Slide 1: List of contents
Benchmark Wind turbines
Commmon industry configuration for 5MW Class
Benchmarks comparsion
Other subsystems of benchmarks
Bakhtyar Karim

## Slide 2: 1. Benchmark Wind Turbines & Why it matters
Bakhtyar Karim
Benchmarking means studying existing wind turbines in the market that match our general concept .
Why benchmarks matters?
Helps us learn from proven 5 MW turbine designs used in real world environments
Supports future decisions in further details of drivetrain, tower, and control systems
Reduces risk by aligning with certifiable and manufacturable configurations
Provides technical references for all teams to start concept development
Ensures we follow industry best practices and can justify our design choices
[1], [2], [3]

## Slide 3: 2. Common industry configuration (5 MW Class)
Bakhtyar karim
Rated Power: 5–5.7 MW
Rotor Diameter: 145–163 m
Hub Heights: Typically between 100–127 m
Generator Type: Mostly DFIG
Drivetrain Concept: 3 point suspension
Target Wind Class: IEC IIIA, low to moderate wind sites
These configurations are used in modern turbines installed in Turkey, India, Spain, and the Middle East.
[1], [2], [3], [4], [5]

## Slide 4: 3. Benchmarks comparsion
Bakhtyar Karim
[1], [2], [3]
Feature | SG 5.0-145 | Nordex N163/5.X | GE Cypress 5.3-158
Rated Power | 5.0 MW | Up to 5.7 MW | 5.3 MW
Rotor Diameter | 145 m | 163 m | 158 m
Hub Height | Up to 127.5 m | 98 / 113 / 118 m | ~90–120 m
Drivetrain | 3 Point Suspension | 3 Point Suspension | 3 Point Suspension
Generator | DFIG | DFIG | DFIG / PMSG
Wind Class | IEC IIIA | IEC IIIA | IEC IIIA
Regions Used | India, Turkey | Turkey, EU, LATAM | Middle East, Asia, Europe

## Slide 5: 4. Other subsystems of benchmarks
Bakhtyar karim
[1], [2], [3], [4], [6], [7], [8]
Subsystem | Benchmark Approach | Example Turbines
Yaw System | Active yaw drives, flange mount | SG 5.0-145, Nordex N163, GE Cypress
Pitch System | Electric pitch motors | Nordex N163, GE Cypress
Nacelle Design | Modular serviceable structure | GE Cypress
Main Bearings | Journal or spherical types | SKF, ORE Catapult pilot turbines
Lidar Integration | Forward looking lidar for preview control | Siemens, Vestas (LAC systems)
Control System | ROSCO, feedforward & feedback hybrid | IEA RWTs, open source platforms
Grid Interface | DFIG with fault ride through capabilities | Nordex Delta4000, Siemens DFIG
Simulation Tools | OpenFAST, PowerFactory, Simulink | DTU, NREL, IEA Benchmark Turbines

## Slide 6: Bibliography – Managment team - PM
[1] Siemens Gamesa Renewable Energy, “SG 5.0-145 Onshore Wind Turbine,” Siemens Gamesa, [Online]. Available: https://www.siemensgamesa.com/en-int/products-and-services/onshore/wind-turbine-sg-5-0-145. [Accessed: Oct. 1, 2025].
[2] Nordex SE, “N163/5.X – Delta4000 Platform,” Nordex Group, [Online]. Available: https://www.nordex-online.com/en/technology/platforms/delta4000/. [Accessed: Oct. 1, 2025].
[3] GE Vernova, “Cypress Platform – 5.3-158 MW Onshore Wind Turbine,” GE Renewable Energy, [Online]. Available: https://www.gevernova.com/. [Accessed: Oct. 3, 2025].
[4] P. Bortolotti, J. J. Jonkman, L. Wang, and A. D. Wright, “IEA Wind TCP Task 37: Systems Engineering in Wind Energy - WP2.1 Reference Wind Turbines,” U.S. Department of Energy, Office of Scientific and Technical Information, May 2019. [Online]. Available: https://doi.org/10.2172/1529216. [Accessed: Oct. 3, 2025].
[5] National Renewable Energy Laboratory (NREL), “NREL 5 MW Reference Turbine Documentation,” [Online]. Available: https://www.nrel.gov/wind/nrel-5mw-reference-turbine.html. [Accessed: Oct. 3, 2025].
[6] NREL, “OpenFAST Documentation Portal,” [Online]. Available: https://openfast.readthedocs.io. [Accessed: Oct. 3, 2025].
[7] NREL, “ROSCO – Reference Open Source Controller,” GitHub Repository, [Online]. Available: https://github.com/NREL/ROSCO. [Accessed: Oct. 3, 2025].
[8] T. Decker, G. Jacobs, J. Röder, et al., “Experimental study on the condition monitoring of planetary journal bearings in wind turbine gearboxes using the surface acoustic wave method,” Forsch. Ingenieurwes., vol. 89, p. 112, 2025. [Online]. Available: https://doi.org/10.1007/s10010-025-00887-y. [Accessed: Oct. 3, 2025].
Bakhtyar Karim