## Slide 1: Weekly report: Feedback Controller
Week number: 04
Date: 21/10/2025
Supervisor: Prof. Dr.-Ing. David Schlipf
Group members: Mirza Dincer, Saurabh Pankaj Jha
Presenter: Mirza Dincer

## Slide 2: List of Contents
Tasks of the Week
Steady State Values
DLC 1.2 Simulations
Simulation Settings
Results
Conclusion
Mirza Dincer - 780261

## Slide 3: Tasks of the Week
Setting MATLAB script to get a steady state pitch and rotor speed values of a turbine
Setting MATLAB scripts to run a DLC 1.2 simulations
Running a DLC 1.2 simulations for IEA 3.4 MW.
Mirza Dincer - 780261

## Slide 4: Steady State Values
Steady state values ensures more stable turbine startup in simulation.
Only enabled GenDOF and First fore-aft tower bending-mode DOF.
No initial conditions.
600 second sim with constant wind speeds.
Average values of last 60 seconds to get the settled values.
Mirza Dincer - 780261
Wind Speed | Blade Pitch | Rotor Speed
4 | 0.000 | 4.645
5 | 0.000 | 5.807
6 | 0.000 | 6.967
7 | 0.000 | 8.128
8 | 0.000 | 9.288
9 | 0.294 | 10.432
10 | 3.361 | 11.634
11 | 7.107 | 11.634
12 | 9.493 | 11.634
13 | 11.456 | 11.634
14 | 13.184 | 11.634
15 | 14.763 | 11.634
16 | 16.240 | 11.634
17 | 17.639 | 11.634
18 | 18.973 | 11.634
19 | 20.234 | 11.634
20 | 21.461 | 11.634
21 | 22.649 | 11.634
22 | 23.801 | 11.634
23 | 24.910 | 11.634
24 | 25.992 | 11.634
25 | 27.046 | 11.634
26 | 28.073 | 11.634
27 | 29.074 | 11.634
28 | 30.050 | 11.634
29 | 31.003 | 11.634
30 | 31.935 | 11.634
Steady State Values of Pitch angle and Rotor speed for IEA 3.4 MW

## Slide 5: DLC 1.2 simulations
DLC 1.2 simulations are for production in normal turbulence to evaluate fatigue for the lifetime of a turbine.
As a result, table with following values are generated
Mean value of generated power
DEL values for tower base pitching moment (TwrBsMyt)
DEL values Low-speed shaft torque (RotTorq)
DEL values Flapwise moment at the blade root (RootMyb1)
Pitch travel
Max value of Electrical generator torque (GenTq)
Mirza Dincer - 780261

## Slide 6: Simulation Settings
Mirza Dincer - 780261
660 seconds of simulation. Evaluation of values starts at t = 60 second to get settled values.
DLC 1.2 wind fields with average of 4 m/s to 24 m/s with steps with 2 m/s, 6 seeds.
Only enabled Rotor DOF, First and Second fore-aft tower bending-mode DOF, First and Second side-to-side tower bending-mode DOF.
Initial conditions of pitch angle and rotor speed for every corresponding wind speed.
Running only feedback controller, no Lidar-assisted controller.

## Slide 7: Result 1
Mirza Dincer - 780261
Simulation results for IEA 3.4 MW with feedback control. 8 m/s wind field for DLC 1.2

## Slide 8: Result 2
Mirza Dincer - 780261
Simulation results for IEA 3.4 MW with feedback control. 10 m/s wind field for DLC 1.2

## Slide 9: Result 3
Mirza Dincer - 780261
Simulation results for IEA 3.4 MW with feedback control. 12 m/s wind field for DLC 1.2

## Slide 10: DLC 1.2 Result Table
Mirza Dincer - 780261
Wind Speed | GenPwr | DEL_4_TwrBsMyt | DEL_4_RotTorq | DEL_10_RootMyb1 | Overshoot_GenSpeed | Travel_BldPitch1 | max_GenTq
4 | 231.33 | 3.69E+04 | 6.69E+02 | 2.70E+03 | 77.89 | 0.00 | 8.79
6 | 804.38 | 8.21E+04 | 1.40E+03 | 5.39E+03 | 116.36 | 0.00 | 19.20
8 | 1855.78 | 1.02E+05 | 2.21E+03 | 7.68E+03 | 151.21 | 15.62 | 28.98
10 | 2969.43 | 8.80E+04 | 2.27E+03 | 9.17E+03 | 162.95 | 107.27 | 29.08
12 | 3308.06 | 8.28E+04 | 2.29E+03 | 9.83E+03 | 166.29 | 126.80 | 29.08
14 | 3308.06 | 8.28E+04 | 2.29E+03 | 9.83E+03 | 166.29 | 126.80 | 29.08
16 | 3350.12 | 1.02E+05 | 2.89E+03 | 1.18E+04 | 177.56 | 96.03 | 29.08
18 | 3354.51 | 1.10E+05 | 3.28E+03 | 1.28E+04 | 186.26 | 87.54 | 29.08
20 | 3346.44 | 1.32E+05 | 4.01E+03 | 1.40E+04 | 190.78 | 89.57 | 29.08
22 | 3346.27 | 1.37E+05 | 4.50E+03 | 1.42E+04 | 192.71 | 100.81 | 29.08
24 | 3348.98 | 1.49E+05 | 5.01E+03 | 1.51E+04 | 195.36 | 113.40 | 29.08
Result Table of DLC 1.2 simulations for IEA 3.4 MW
Original table has values for every wind field seeds, mean of seed is shown for presentation

## Slide 11: Conclusion
Script for getting steady state values of pitch angle and rotor speed of a wind turbine
Successfully run a simulation of DLC 1.2
Next week:
check step response for pitch and torque controller​
Focus on getting EOG at 12 m/s and 25 m/s better in cost by changing KP and updating KP and KI vectors in Rosco​
Mirza Dincer - 780261