## Slide 1: Weekly report: Foundations
Week number: 12
Date: 16/12/2025
Supervisor: Prof. Dr.-Ing. Torsten Faber
Group members : Jehad Albaali- Amgad Gerges - Reda Deif
presented by : Jehad Albaali

## Slide 2: List of contents
Seismic Analysis Parameters
Seismic Forces & Moments
Global Stability Verification
Soil-Structure Interaction Analysis
3D Modeling
References
Foundations team/ Optimus Syria
Jehad Albaali
16/12/2025

## Slide 3
Foundations team/ Optimus Syria
Jehad Albaali
16/12/2025
Seismic Analysis Parameters
Design Methodology
The analysis employs the Equivalent Static Force Method (Pseudo-Static approach) in accordance with Eurocode 8 standards. This simplified method is appropriate for regular structures and provides conservative results for seismic design verification.
Seismic Coefficient: a_g=0.4g
This represents a high seismic zone classification, requiring rigorous stability verification across all failure modes.
Figure : by Dr faber

## Slide 4
  Seismic Forces & Moments
Applying the seismic coefficient (0.4) to the precise structural weights yields the following demand on the structure:
Component
Weight (G)
Seismic Force
Lever Arm (H)
Nacelle
146.3 tons
58.5 tons
100.0 m
Tower
349.0 tons
139.6 tons
50.0 m
Foundation
2,856.0 tons
1,142.4 tons
1.0 m
TOTAL (Demand)
3,351.3 tons
1,340.5 tons
—
1,340
Base Shear
Total horizontal force in tons
14K
Overturning Moment
Total moment in ton·m
The seismic force calculation follows V_i = 0.4 \times G for each component, with forces applied at respective centers of gravity to determine the total base shear and overturning moment acting on the foundation.
Foundations team/ Optimus Syria
Jehad Albaali
16/12/2025

## Slide 5
Foundations team/ Optimus Syria
Jehad Albaali
16/12/2025
Global Stability Verification
Two critical stability checks ensure the foundation remains secure under seismic loading conditions. Both checks demonstrate adequate safety factors exceeding minimum code requirements.
1
Sliding Stability Check
This check verifies that horizontal seismic forces do not cause the foundation to slide across the soil interface.
Resisting Force (Friction + Cohesion): 2,372 tons (23,295 kN)
Driving Shear Force: 1,340 tons (13,158 kN)
Factor of Safety: 1.77 > 1.0 → SAFE
The resisting forces, generated through friction between the foundation base and soil plus soil cohesion, significantly exceed the applied horizontal seismic force.
2
Overturning Stability Check
This check ensures the foundation weight provides sufficient resistance against rotational failure.
Stabilizing Moment (Weight × Radius): 41,891 ton·m (315,800 kN·m)
Overturning Moment: ~13,972 ton·m (137,133 kN·m)
Factor of Safety: 2.30 > 1.0 → SAFE
The stabilizing moment from the foundation's self-weight provides more than double the resistance needed to prevent overturning.

## Slide 6
Foundations team/ Optimus Syria
Jehad Albaali
16/12/2025
Soil-Structure Interaction Analysis
Bearing Capacity Verification
The bearing pressure check ensures soil beneath the foundation can support the combined static and seismic loads without failure.
Maximum Edge Pressure (q_{max}): 356 kPa
Allowable Dynamic Bearing Capacity: > 400 kPa
The allowable capacity assumes compacted fill material with appropriate seismic increase factors per Eurocode 8 provisions.
Result: Safe against soil failure
The maximum bearing pressure remains below the soil's dynamic capacity, ensuring no bearing failure occurs during seismic loading.
Eccentricity & Gapping Analysis
Eccentricity measures how far the resultant force shifts from the foundation center, indicating potential edge uplift.
Calculated Eccentricity (e): 5.43 m
Critical Threshold: R/4 = 3.12 m
Foundation Radius (R): 12.5 m
Observation: Since e > R/4, partial gap opening occurs at the foundation edge under peak seismic loading.
Conclusion: Acceptable under ULS conditions
While edge gapping occurs, global stability is maintained with adequate safety factors. This behavior is acceptable for extreme seismic events at Ultimate Limit State.

## Slide 7
3D Modeling Wind of Turbine Foundation (Anchor cage)
Foundations team/ Optimus Syria
Jehad Albaali
Figure created by (Solidwork)
16/12/2025
3D model of anchor cage with anchor bolts

## Slide 8
3D Modeling Wind of Turbine Foundation
Foundations team/ Optimus Syria
Jehad Albaali
Figure created by the author (Solid work )
16/12/2025
3D model of wind turbine foundation and pedestal (SolidWorks)

## Slide 9
References
Foundations team/ Optimus Syria
Jehad Albaali
EN 1998-1 (Eurocode 8)Design of structures for earthquake resistance – Part 1: General rules, seismic actions and rules for buildings,
EN 1997-1 (Eurocode 7)Geotechnical design – Part 1: General rules,European Committee for Standardization (CEN).
SolidWorks Corporation.SolidWorks User Documentation – 3D Modeling and Assembly,
16/12/2025