## Slide 1: Weekly report: Foundations
Week number: 10
Date: 02/12/2025
Supervisor: Prof. Dr.-Ing. Torsten Faber
Group members : Jehad Albaali- Amgad Gerges - Reda Deif
presented by : Jehad Albaali
02/12/2025

## Slide 2: Project Data & Geometrics
Foundations team/ Optimus Syria
Group members: Jehad Albaali- Amgad Gerges - Reda Deif
L Dimensions
Hub Height: 100 m
Tower Base Diameter: 4.8 m
Pedestal Diameter: 7.0 m
Raft Diameter: 25.0 m
Middle Slab Thickness: 2.0 m
Materials {EC2)
Concrete Class: C35/45
Cylinder Strength (fck): 35 MPa
Reinforcing Steel: 8500 (fyk = 500 MPa)
Anchor Bolts: Grade 10.9 (fub = 1000 MPa)

## Slide 3
Design Action (ULS)
Foundations team/ Optimus Syria
The foundation is subjected to extreme overturning moments due to the 1OOm hub height.
02/12/2025
Jehad Albaali

## Slide 4: Why Anchor Cage Connection ?
Foundations team/ Optimus Syria
Considering the tower diameter (4.8m) and dynamic nature of loads, the Anchor Cage system was selected over the Embedded Ring for three critical reasons:
02/12/2025
Jehad Albaali

## Slide 5: Anchor Cage Design Concept
Foundations team/ Optimus Syria
A Single-Row anchor cage configuration was selected to simplify installation and concrete flow compared to double-row alternatives.
Bolt Size: M48 (Grade 10.9)
Number of Bolts: 96 Units
Circle Diameter: 4.6 m
Spacing: -150 mm c/c
02/12/2025
Jehad Albaali
Source: www.high-strength-steel.com

## Slide 6: ULS Tension Capacity Verification
Foundations team/ Optimus Syria
1. Load per Bolt
2. Bolt Resistance (Grade 10.9)
02/12/2025
Jehad Albaali

## Slide 7
Foundations team/ Optimus Syria
Critical Failure Check
Punching Shear at Pedestal
The calculation reveals that the concrete alone cannot resist the shear forces generated by the pedestal punching through the raft.
Applied Stress (vEd):
Concrete Capacity (vRd c):
I
0.53 MPa
0.41 MPa
FAILURE: VEd > VRdC
Conclusion: Shear reinforcement (studs or stirrups) is mandatory.
02/12/2025
Jehad Albaali
Source :https://structville.com/strengthening-flat-slabs-against-punching-shear

## Slide 8
Foundations team/ Optimus Syria
Shear Reinforcement Design
Sizeing : Ø16 or Ø20 studs with spacing s≤150mm
02/12/2025
Jehad Albaali
Source: Nanobanana

## Slide 9
Foundations team/ Optimus Syria
Flexural Reinforcment layout
Zone 1 : Under Pedestal ( r ≤ 7m )
  Bottom Radial : Ø25 @ 150mm
  Bottom Circumferential :Ø 20 @ 150-200 mm
Zone 2 : outer Raft ( r > 7m )
  Bottom Radial : Ø20 @ 200-250 mm
  Top Circumferential :Ø 20 ( to resist negative moments soil support )
02/12/2025
Jehad Albaali

## Slide 10
Foundations team/ Optimus Syria
Pedestal Reinforcment
Objective : Confine the concrete core against high bursting forces from the anchor cage .
Reinforcement Details :
  Vertical Main Bars : Ø32 @ 150mm ( Both Faces )
  Confinement (Hoops / Ties ) : Ø16 or Ø20 Spacing ( 80-100 mm)
  Anchorage : Must Extend Form the raft up to 1,0-1,2 above bolt level
02/12/2025
Jehad Albaali

## Slide 11
Foundations team/ Optimus Syria
Load Transfer Mechanism
1-Tension ForceAction:. Wind loads Uplift
Resistance: 96 x M48 Anchor bolts transfer into concrete
Design Load: 588 KN per Bolt
2-Compression Force Action: moment + dead load
Resistance: The concrete core (C35/45)
3-Bursting Forces Action: High concentrated. Anchorage Forces
Resistance: Resisted by the dense confinement hoops.
02/12/2025
Jehad Albaali

## Slide 12
Foundations team/ Optimus Syria
Jehad Albaali
Structural Detailing Overview
https://www.youtube.com/watch?v=znEKJ4Jxhmo

## Slide 13
Foundations team/ Optimus Syria
Summary
Conclusions:
  The proposed 96 x M48 anchor cage is adequate for the overturning moment .
  Punching shear reinforcement is mandatory at the pedestal interface .
  A 2.0m slab thickness provides favorable effective depth for shear and bending .
02/12/2025
Jehad Albaali
https://www.youtube.com/watch?v=fpmd_br6loI

## Slide 14
02/12/2025
Jehad Albaali
References
EN 1992-1-1: Eurocode 2 — Design of Concrete Structures European Committee for Standardization (CEN).
DNV-ST-0126: Support Structures for Wind TurbinesDet Norske Veritas (DNV), Structural Design Standard, 2016.
IEC 61400-6: Wind Turbines – Part 6: Tower and Foundation Design RequirementsInternational Electrotechnical Commission (IEC).