## Slide 1: Weekly report: Team Project Development
Group members: Luis Urhahn, Ahmed Sallam, Ceren Cetin, Sohail Mansuri
Presenter: Luis Urhahn
Week number: 07
Date: 01/12/2025
Supervisor: Dr. Marina Blohm

## Slide 2: Tasks of the week
Luis Urhahn
Overall task:
 Developing the simulation in WindPro and getting the results for the AEP.
  Week 7: Update Wind Resource Data, MCP + ResGen,
  Week 8: Calculate the first AEP calculation, develop a first WF Layout, Earthquake research,
  Week 9: Define the Power Curve of the Optimus WTG, insert the turbine Data of Optimus, first calculation of the AEP of Optimus,
  Week 10: Performing the noise and shadow calculation of the single Optimus Turbine and defining the final available Windfarm area at our location.

## Slide 3: Progress: WindPro Simulation
Luis Urhahn
Update on the Wind Ressource Implementation in the WindPro model:
  Implementing of the measured data from the met mast in 2006
    Complex, due to special format for the input data in WindPro
    Developing of a new Excel format with correct values
    Lots of problems due to different format requirements in WindPro
    Transferring into a CSV-file for compliance with WindPro requirement
  Performing an MCP Analysis (Measure, Correlate, Predict)
    Comparing the long-term data with the measured data
    Checking for similarities and dissent
  Inserting the ResGen Modul
    For the generation of the Wind Energy Resource
    Now possible with the implemented measured data (MCP)
    First calculation

## Slide 4: Progress: WindPro Simulation
Luis Urhahn
Implementing of the measured data:
Figure 1: Screenshot of implementation of measured wind data [1]

## Slide 5: Progress: WindPro Simulation
Luis Urhahn
Implementing of the measured data:
Figure 2: Screenshot of implementation of measured wind data [1]

## Slide 6: Progress: WindPro Simulation
Luis Urhahn
MCP Analysis (Measure, Correlate, Predict):
Figure 3: Comparison of the Wind rose [1]
Figure 4: Comparison of the wind resource data in 2006 [1]
Figure 5: Comparison of the wind resource data in a day [1]

## Slide 7: Explanation of the wind conditions
Luis Urhahn
Why do we have such high wind speeds at our location?
Figure 6: Elevation Map QGIS [6]
Figure 7: Windrose of the measured data

## Slide 8: Progress: WindPro Simulation
Luis Urhahn
Calculation of the Wind Resource Map:
Figure 8: Screenshot of the created Wind Resource Map [1]

## Slide 9: Progress: WindPro Simulation
Luis Urhahn
Distance circle:
4.0 x Rotordiameter in main wind direction, (r = 640m)
1.8 x Rotordiameter perpendicular, (r = 288m)
Defines the minimum distance between the turbines
It will be difficult to find further options without significant restrictions in terms of noise or shadow.
Figure 9: Screenshot of the distance circle [1]

## Slide 10: Progress: WindPro Simulation
Luis Urhahn
Calculate the Power Curve of the turbine.
Inserting the Power Curve and Turbine Data in WindPro
Calculating the AEP with the help of the “PARK-Calculation” in WindPro
Power Curve Optimus Syria |  |  | 
Windspeed [m/s] | Power [kW] | c_p | pitch angle [°]
1 | 0 | 0 | 0
2 | 0 | 0 | 0
3 | 120,49 | 0,45 | 0
4 | 285,62 | 0,45 | 0
5 | 557,85 | 0,45 | 0
6 | 963,96 | 0,45 | 0
7 | 1.530,73 | 0,45 | 0
8 | 2.284,94 | 0,45 | 0
9 | 3.253,36 | 0,45 | 0
10 | 4.462,78 | 0,45 | 0
11 | 5.000,00 | 0,37 | 0
12 | 5.000,00 | 0,28 | 0
13 | 5.000,00 | 0,22 | 0
14 | 5.000,00 | 0,18 | 0
15 | 5.000,00 | 0,14 | 0
16 | 5.000,00 | 0,12 | 0
17 | 5.000,00 | 0,10 | 0
18 | 5.000,00 | 0,08 | 0
19 | 5.000,00 | 0,07 | 0
20 | 5.000,00 | 0,06 | 0
21 | 5.000,00 | 0,05 | 0
22 | 5.000,00 | 0,05 | 0
23 | 5.000,00 | 0,04 | 0
24 | 5.000,00 | 0,04 | 0
25 | 5.000,00 | 0,03 | 0
> 25 | 0 | 0 | 0
Table 1: Table of the Power Curve OSY160-5.0 MW

## Slide 11: Progress: WindPro Simulation
Luis Urhahn
Park Calculation for 1xOSY160-5.0 MW (MCP data):
Parameter | Unit | Value
Result Park (AEP) | MWh/year | 22 491.8
Capacity factor | % | 51.3
Full Load Hours (FLH) | Hours/year | 4 498
Average wind speed | m/s | 8.5
Without any curtailments/restrictions!
Table 2: Results of the PARK-Calculation for 1xOSY160-5.0 MW [1]
Notes: Shows hat the MCP Method is the better option!

## Slide 12: Progress: WindPro Simulation
Luis Urhahn
Weibull Distribution and Power Curve of the OSY160-5.0MW
Chart: Windbins [m/s]
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25
Weibull Distribution | 0.0029299 | 0.035445 | 0.069481 | 0.091418 | 0.090105 | 0.079527 | 0.072221 | 0.063793 | 0.056601 | 0.054337 | 0.052244 | 0.051198 | 0.048515 | 0.044577 | 0.0406 | 0.034836 | 0.029794 | 0.025095 | 0.02051 | 0.014326 | 0.0090752 | 0.0063165 | 0.0038812 | 0.0018264 | 0.00066589
Power Curve OSY160-5.0MW | 0 | 0 | 120.4949 | 285.6176 | 557.847 | 963.9595 | 1530.732 | 2284.9411 | 3253.3634 | 4462.7756 | 5000 | 5000 | 5000 | 5000 | 5000 | 5000 | 5000 | 5000 | 5000 | 5000 | 5000 | 5000 | 5000 | 5000 | 5000
Figure 10: Graph of the Power Curve OSY160-5.0 MW and Weibull distribution
Notes: Shows hat the MCP Method is the better option!

## Slide 13: Progress: WindPro Simulation
Luis Urhahn
Does the turbine have to regulate down at a certain wind speed to protect the blades and the tower?
Chart: Power Curve of the OSY160-5.0 MW
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 25
 | 0 | 0 | 120.4949 | 285.6176 | 557.847 | 963.9595 | 1530.732 | 2284.9411 | 3253.3634 | 4462.7756 | 5000 | 5000 | 5000 | 5000 | 5000 | 5000 | 5000 | 5000 | 5000 | 5000 | 5000 | 5000 | 5000 | 5000 | 5000 | 0
Figure 11: Power Curve OSY160-5.0 MW
Figure 12: Power Curve of the SG5.0-145 (HH102) for Comparison [1]
Notes: Same Power Output…

## Slide 14: Progress: WindPro Simulation
Luis Urhahn
Does the turbine have to regulate down at a certain wind speed to protect the blades and the tower?
Figure 13: Power Curve of the Vestas V162-6.0MW for Comparison [1]
Notes: Same Rotordiameter…

## Slide 15: Progress: WindPro Simulation
Luis Urhahn
Finalization of the Windfarm area with the help of the “white map” of QGIS
Figure 14: White Map of QGIS (considering all restrictions) [6]
Figure 15: Final WTG area in WindPro [1]

## Slide 16: Progress: WindPro Simulation
Luis Urhahn
Location | Demand [dB(A)] | Sound level [dB(A)] | Demand fulfilled?
A | 45 | 38.8 | Yes
B | 45 | 36.0 | Yes
C | 55 | 34.2 | Yes
D | 60 | 45.7 | Yes
E | 60 | 38.6 | Yes
F | 45 | 32.2 | Yes
G | 45 | 30.3 | Yes
H | 45 | 31.2 | Yes
I | 45 | 26.2 | Yes
A
B
C
F
H
G
D
E
I
A
B
C
F
H
G
Remember the noise restriction: 45 dB(A) for rural villages, 60 dB(A) for industry
Figure 15: Noise calculation of our location [1]
Notes: Shows hat the MCP Method is the better option!

## Slide 17: Progress: WindPro Simulation
Luis Urhahn
Location | Shadow [h/year] | Shadow [h/day] | Critical?
A | 55:42 | 0:47 | Yes
B | 50:56 | 0:49 | Yes
C | 20:54 | 0:37 | Yes
D | 0:00 | 0:00 | No
E | 0:00 | 0:00 | No
F | 0:00 | 0:00 | No
G | 16:51 | 0:26 | No
H | 32:03 | 0:30 | Yes
I | 6:33 | 0:19 | No
A
B
C
F
H
G
Shadow restriction worst case: max. 30 h per year, max. 30 min per day
D
E
I
Figure 16: Shadow calculation of our location [1]
Notes: Shows hat the MCP Method is the better option!

## Slide 18: Transportation Study (Summary)
Luis Urhahn
Most of the components will be shipped to the port of Tartus
Main transportation way
Two options for the final 10 km
A few challenges along the way
Figure 17: Screenshot main transportation route [8]
Notes: Shows hat the MCP Method is the better option!

## Slide 19: Transportation Study (Summary)
Luis Urhahn
Option 1 (yellow): Shorter way, but build of a new road needed
Option 2 (blue): Longer way, few reinforcements still needed
Option 1
Option 2
Figure 18: Screenshot main transportation route [8]
Notes: Shows hat the MCP Method is the better option!

## Slide 20: Transportation Study (Summary)
Luis Urhahn
Challenges/Limitations | Number
Military Checkpoints | 8
Bridge reinforcement | 7
Block/Material removal | 7
Road improvement measures | 9
Electrical wire removal | 1
Rerouting (new road) | 2
Bridge height | 4.75 m
Road width (country road, single) | 3.75 m
Road width (Highway M1, two lines) | 7.50 m
Transport challenges from the Tartus port to the final location:
Figure 19: Pictures of road challenges [9]
Notes: Shows hat the MCP Method is the better option!

## Slide 21: Research Earthquake Situation
Luis Urhahn
Guideline or Recommended Practise: “DNV-RP-0585: Seismic design of wind power plants” [3]
Not focusing on the Richter scale
Analysis will be based on the Probabilistic Seismic Hazard Analysis (PSHA)
  Needs the input of the Peak Ground Acceleration (PGA)
Extreme scenario needs to withstand the max earthquake for 475 years
  Return period of the max earthquake
  Defined as the standard Ultimate Limit State (ULS)
For our analysis: Response Spectrum Analysis (RSA)
  A simplified, widely used method, based on PGA
The PGA for the Homs District is 0.38 to 0.40 g. [4], [5]

## Slide 22: Clarification of the cost analysis
Luis Urhahn
We will summarise the total cost of the turbine
We will calculate the transportation cost to our location
We will calculate the LCOE of the single turbine and a possible windfarm
But therefore…
You need to give us the total cost (final) of your components AND
You need to tell us where you will produce or buy the component!
 If you need any help or guidance for the cost analysis, please let us know!
Our task
Your task

## Slide 23: Next Steps
Luis Urhahn
The next steps for our Team:
Transportation cost analysis
Meeting with experts regarding the permitting process in Syria
Development of a possible windfarm at our location
Cable routing to the substation
Progressing the detailed LCOE calculation
Notes: Shows hat the MCP Method is the better option!

## Slide 24: Bibliography – Project Development
Luis Urhahn
[1] WindPro, University License for WindPro [Software] (latest on 09.11.25)
[2] Google Gemini, Student License for Gemini [AI] (latest on 08.11.25)
[3] DNV, DNV-RP-0585 Seismic design of wind power plants, (latest 12.11.25)
[4] ResearchGate, Seismic Hazard Assessment of Syria, https://www.researchgate.net/profile/Raed-Ahmad-2/publication/286870802_Seismic_Hazard_Assessment_of_Syria/links/566ead0308ae430ab5003171/Seismic-Hazard-Assessment-of-Syria.pdf , (latest 12.11.25)
[5] Scientific Research, Re-Evaluation of Seismic Hazard of Syria https://www.scirp.org/pdf/ijg20120400008_81946431.pdf , (latest 12.11.25)
[6] QGIS, Public Software of QGIS [Software]
[7] Lecture notes of “Project Development“ and “Advanced Windfarm Planning“
[8] Google, Google Maps. [Online]. Available: https://maps.google.com
[9] Pictures of Road Condition Port Tartus to Homs, Document Uni Damaskus
 Simulation developed with the help of AI.