## Slide 1
Date: 09 December 2025

## Slide 2: Weekly report: Team Gearbox, Brake, Coupling
Week number : 11
Date: 09/12/2025
Supervisor: Prof. Peter Quell
Group Members :Nehang Jitendra Joshi,Santo Mazumder,Md Razaul Karim Rahat
Presented by -Santo Mazumder
9-12-2025
Gearbox, Brake, Coupling

## Slide 3: List of Content
Gears geometry calculation
Sketch of gearbox layout
3D design of all stage and housing
Force analysis and Stress calculation
Gearbox internal shaft calculation
Cost,Weight and supplier
Gearbox, Brake, Coupling
9-12-2025

## Slide 4: Gears geometry calculation
Gearbox, Brake, Coupling
9-12-2025
Parameter | Value
Input torque,Mi KN m | 5,095
Output torque,Mo KN m | 41,9
Input speed, rpm | 10.12
Output speed, rpm | 1200

## Slide 5: Gears geometry calculation
Gearbox, Brake, Coupling
9-12-2025
Parameter | 1st stage | 2nd stage | 3rd stage
Gear ratio | 5 | 4.9 | 4.9
No of Planets | 5 | 4 | NA
Module,(mm) | 16 | 14 | 9
Pressure angle | 20 | 20 | NA
Helix angle | 20 | 20 | NA
Input speed,rpm | 10.12 | 133.79 | 401.48
Output speed,rpm | 133.79 | 401.48 | 1200

## Slide 6: Gears geometry calculation
Gearbox, Brake, Coupling
9-12-2025
Parameter | Formula | 1st stage | 2nd stage | 3rd stage
Input torque |  | 5,095 | 23.8 | NA
Output torque |  | 23.8 | 41.9 | NA
Pitch diameter,d (mm) | m*zp m*zs m*zr | ds-592, dp-624 , dr-1840 | ds-490 , dp-525 , dr-1540 | 900 and 198
Outer dia ,Do (mm) | D0=(z+2).m | Ds-642,dp-676,dr-1900 | Ds-540,dp-560,dr-1600 | 
Addendum,a(mm) | a=m | 16 | 14 | 9
Dedendum,b(mm) | b=1.25*m | 20 | 17.5 | 11.25
Face width,(mm) | 10 * module | 160 | 140 | 90

## Slide 7: Sketch of the Gear box Layout
Gearbox, Brake, Coupling
9-12-2025
Reference: Own sketch

## Slide 8: Sketch of the Gear box Layout
Gearbox, Brake, Coupling
9-12-2025
Reference: Own sketch

## Slide 9
Gearbox, Brake, Coupling
9-12-2025
3D model gearbox housing
Reference: Own design

## Slide 10
Gearbox, Brake, Coupling
9-12-2025
3D model design of all stages
Reference: Own design

## Slide 11
Gearbox, Brake, Coupling
9-12-2025
3D model design of all stages
Reference: Own design

## Slide 12
Gearbox, Brake, Coupling
9-12-2025
Cast iron,Mechanical Properties

## Slide 13: Force analysis, Stress, and Safety Factors (Zr-Ring gear)
Gearbox, Brake, Coupling
9-12-2025
Parameter | Formula | 1st stage | 2nd stage
Input torque,M (MNm) | Mi-5,095 M2=M1/i1 | 5,095 | 1.01
Tangencial force,Ft (MN) |  | 3.481 | 0.788
Radial force Fr (MN) |  | 1.567 | 0.587
Bending stress (m (MPa) |  | 137.89 | 92.67
Contact stress C,(MPa) |  | 216.57 | 170.34
Factor of safety (Bending) |  | 2.45 | 3.2
Factor of safety (Contact) |  | 1.38 | 2.11

## Slide 14: Force analysis, Stress calculation
Gearbox, Brake, Coupling
9-12-2025
Reference: AGMA 2101-DO4 Standard and Optimus shakti

## Slide 15: Force analysis and Stress
Gearbox, Brake, Coupling
9-12-2025
Reference: AGMA 2101-DO4 Standard and Optimus shakti

## Slide 16: Force analysis and Stress
Gearbox, Brake, Coupling
9-12-2025
Reference: AGMA 2101-DO4 Standard and Optimus shakti
σb: Bending stress in the gear teeth
Wt: Transmitted tangential load (force) at the pitch line
Ko: Overload factor, accounting for unexpected loads
Kv: Dynamic factor, accounting for dynamic effects due to speed
Ks: Size factor, adjusting for differences in gear size
Km: Load distribution factor, accounting for uneven load across the gear face
J: Geometry factor for bending strength, which depends on the gear geometry

## Slide 17: Force analysis and Stress
Gearbox, Brake, Coupling
9-12-2025
Reference: AGMA 2101-DO4 Standard and Optimus shakti
σc: Contact stress in the gear teeth
Wt: Transmitted tangential load (force) on the gear teeth
Ko: Overload factor (accounting for any unexpected loads)
Kv: Dynamic factor (accounts for dynamic effects due to speed)
Ks: Size factor (adjusts for size differences in gears)
Km: Load distribution factor (adjusts for uneven load across the gear face)
KBK_BKB: Rim thickness factor (related to the gear blank design)
Cp: Elastic coefficient, which depends on the materials used for the pinion and gear
I: Geometry factor for pitting resistance, which depends on the gear geometry

## Slide 18
Gearbox, Brake, Coupling
9-12-2025
Gearbox internal shafts calculations
Stage | Gear type and Face width,mm | Shaft diameter | Length (mm) | Width (mm) | Hight (mm) and depth(mm)
 |  |  | L=min(1.5*d,b) | W=D/4 | T=D/6 K.d=T/2
1st stage | Sun gear-160mm | 160 | 160 | 40 | 26.66 13.33
1st stage | Planet gear-160mm | 110 | 160 | 27.5 | 18.33 9.16
2nd stage | Sun gear-140mm | 138 | 140 | 34.5 | 23 11.5
2nd stage | Planet gear-140mm | 80 | 140 | 20 | 13.33 6.66

## Slide 19
Gearbox, Brake, Coupling
9-12-2025
Weight and Cost estimation
No | Components | Weight estimation | Cost estimation
1 | Gearbox Housing * 1 | 8000-9000 Kg | 16200 €
2 | Gears | 7000-7500 Kg | 34000 €
3 | Bearings | 1100 Kg | 2100 €
4 | Brake * 1 | 150 Kg | 5000 €
5 | Coupling *1 | 200 Kg | 1200 €
6 | Internal shaft | 3000 Kg | 13000 €
Total Weight | 24,400 Kg
Total cost | 90,000 – 1,35,000 €
Source-https://www.indexbox.io/search/cast-iron-price-per-kg

## Slide 20
Gearbox, Brake, Coupling
9-12-2025
Weight and Cost estimation Bolted flange connection
Weight and Cost | 4500 Kg and 32,500 €
Material | EN-GJS-400-18-LT
Bolts | M48
Source-https://www.indexbox.io/search/cast-iron-price-per-kg

## Slide 21: Next Steps
Gearbox, Brake, Coupling
9-12-2025
Bearing calculation
Coupling design and calculation
Brake caliper design and calculation

## Slide 22: Bibliography
Gearbox
Previous year Optimus projects(60E,92LE,Shakti 6-12-2025
Roloff Matek Maschinenelemente 7-12-2025
Lecture notes – Mechanical drive train by Prof.Peter Quell.6-12-2025
Shigley's mechanical engineering design and PSG data book 6-12-2025
DNV and IEC-61400-4 guidelines 6-12-2025
Gearbox, Brake, Coupling
9-12-2025