## Slide 1
2nd week – 3rd Presentation

## Slide 2: Weekly report: management team
Week number: 2
Date: 7th/09/2025
Supervisor: Prof. Peter Quell
Group members: Bakhtyar Karim, Federico De Mita, Josef Remberger

## Slide 3: List of contents
Benchmark Wind turbines
Commmon industry configuration for 5MW Class
Benchmarks comparsion
Other subsystems of benchmarks
Bakhtyar Karim

## Slide 4: 1. Benchmark Wind Turbines & Why it matters
Bakhtyar Karim
Benchmarking means studying existing wind turbines in the market that match our general concept .
Why benchmarks matters?
Helps us learn from proven 5 MW turbine designs used in real world environments
Supports future decisions in further details of drivetrain, tower, and control systems
Reduces risk by aligning with certifiable and manufacturable configurations
Provides technical references for all teams to start concept development
Ensures we follow industry best practices and can justify our design choices
[1], [2], [3]

## Slide 5: 2. Common industry configuration (5 MW Class)
Bakhtyar karim
Rated Power: 5–5.7 MW
Rotor Diameter: 145–163 m
Hub Heights: Typically between 100–127 m
Generator Type: Mostly DFIG
Drivetrain Concept: 3 point suspension
Target Wind Class: IEC IIIA, low to moderate wind sites
These configurations are used in modern turbines installed in Turkey, India, Spain, and the Middle East.
[1], [2], [3], [4], [5]

## Slide 6: 3. Benchmarks comparsion
Bakhtyar Karim
[1], [2], [3]
Feature | SG 5.0-145 | Nordex N163/5.X | GE Cypress 5.3-158
Rated Power | 5.0 MW | Up to 5.7 MW | 5.3 MW
Rotor Diameter | 145 m | 163 m | 158 m
Hub Height | Up to 127.5 m | 98 / 113 / 118 m | ~90–120 m
Drivetrain | 3 Point Suspension | 3 Point Suspension | 3 Point Suspension
Generator | DFIG | DFIG | DFIG / PMSG
Wind Class | IEC IIIA | IEC IIIA | IEC IIIA
Regions Used | India, Turkey | Turkey, EU, LATAM | Middle East, Asia, Europe

## Slide 7: 4. Other subsystems of benchmarks
Bakhtyar karim
[1], [2], [3], [4], [6], [7], [8]
Subsystem | Benchmark Approach | Example Turbines
Yaw System | Active yaw drives, flange mount | SG 5.0-145, Nordex N163, GE Cypress
Pitch System | Electric pitch motors | Nordex N163, GE Cypress
Nacelle Design | Modular serviceable structure | GE Cypress
Main Bearings | Journal or spherical types | SKF, ORE Catapult pilot turbines
Lidar Integration | Forward looking lidar for preview control | Siemens, Vestas (LAC systems)
Control System | ROSCO, feedforward & feedback hybrid | IEA RWTs, open source platforms
Grid Interface | DFIG with fault ride through capabilities | Nordex Delta4000, Siemens DFIG
Simulation Tools | OpenFAST, PowerFactory, Simulink | DTU, NREL, IEA Benchmark Turbines

## Slide 8: Bibliography – Managment team - PM
[1] Siemens Gamesa Renewable Energy, “SG 5.0-145 Onshore Wind Turbine,” Siemens Gamesa, [Online]. Available: https://www.siemensgamesa.com/en-int/products-and-services/onshore/wind-turbine-sg-5-0-145. [Accessed: Oct. 1, 2025].
[2] Nordex SE, “N163/5.X – Delta4000 Platform,” Nordex Group, [Online]. Available: https://www.nordex-online.com/en/technology/platforms/delta4000/. [Accessed: Oct. 1, 2025].
[3] GE Vernova, “Cypress Platform – 5.3-158 MW Onshore Wind Turbine,” GE Renewable Energy, [Online]. Available: https://www.gevernova.com/. [Accessed: Oct. 3, 2025].
[4] P. Bortolotti, J. J. Jonkman, L. Wang, and A. D. Wright, “IEA Wind TCP Task 37: Systems Engineering in Wind Energy - WP2.1 Reference Wind Turbines,” U.S. Department of Energy, Office of Scientific and Technical Information, May 2019. [Online]. Available: https://doi.org/10.2172/1529216. [Accessed: Oct. 3, 2025].
[5] National Renewable Energy Laboratory (NREL), “NREL 5 MW Reference Turbine Documentation,” [Online]. Available: https://www.nrel.gov/wind/nrel-5mw-reference-turbine.html. [Accessed: Oct. 3, 2025].
[6] NREL, “OpenFAST Documentation Portal,” [Online]. Available: https://openfast.readthedocs.io. [Accessed: Oct. 3, 2025].
[7] NREL, “ROSCO – Reference Open Source Controller,” GitHub Repository, [Online]. Available: https://github.com/NREL/ROSCO. [Accessed: Oct. 3, 2025].
[8] T. Decker, G. Jacobs, J. Röder, et al., “Experimental study on the condition monitoring of planetary journal bearings in wind turbine gearboxes using the surface acoustic wave method,” Forsch. Ingenieurwes., vol. 89, p. 112, 2025. [Online]. Available: https://doi.org/10.1007/s10010-025-00887-y. [Accessed: Oct. 3, 2025].
Bakhtyar Karim

## Slide 9: List of contents
Result file
Rotor diameter choice
  Why 250 W/m^2

## Slide 10: 1. Result file
Federico De Mita
New file created for interfaces between the mechanical groups!!!!

## Slide 11: 1. Result file
Federico De Mita
It allows teams to:
Make a record of all their components
Write down and update all the components parameters
Check the situation of other groups
THE FILE WILL BE CONTINOUSLY UPDATED!!!

## Slide 12: 2. Rotor Diameter choice
[1]
Federico De Mita
Rotor Loading
(or Specific Power)
Market trends

## Slide 13: 2. Rotor Diameter choice
Why L must be low
Higher capacity factors
High AEP
Low LCOE
Federico De Mita

## Slide 14: 2. Rotor Diameter choice
Chosen value for Rotor Loading:
If the rated power is fixed at 5 MW, then:
Final diameter choice: 160 m
Blade length: 80 m
Federico De Mita

## Slide 15: 2.i why 250 W/m^2?
[2]
Market trends:
Federico De Mita

## Slide 16: 2.i why 250 W/m^2?
Dependance on the site
[3]
Site conditions chosen:
Low wind speed conditions
To have a high AEP and a low LCOE: low Rotor Loading and relatively large diameter
Federico De Mita

## Slide 17
[1] J. Serrano-González and R. Lacal-Arántegui, “Technological evolution of onshore wind turbines—a market-based analysis,” Wind Energy, vol. 19, no. 12, pp. 2171–2187, Dec. 2016, doi: 10.1002/WE.1974.
[2] “Top Trends in Wind Technology | Department of Energy.” Accessed: Oct. 06, 2025. [Online]. Available: https://www.energy.gov/eere/wind/articles/top-trends-wind-technology
[3] S. Roach, S. M. Park, E. Gaertner, J. Manwell, and M. Lackner, “Application of the New IEC International Design Standard for Offshore Wind Turbines to a Reference Site in the Massachusetts Offshore Wind Energy Area,” J Phys Conf Ser, vol. 1452, no. 1, Mar. 2020, doi: 10.1088/1742-6596/1452/1/012038.
Federico De Mita

## Slide 18: Weekly report: Team Project Development
Group members: Luis Urhahn, Ahmed Sallam, Ceren Cetin, Sohail Mansuri
Week number: 02
Date: 07/10/2025
Supervisor: Dr. Marina Blohm

## Slide 19: List of content
Task of this week
Update on soil condition
Distance anaylsis on the sides (Um Aledam vs. Qattinah
Luis Urhahn

## Slide 20: 1. Tasks of the week
Research on the distances (Luis)
Clarifying the situation regarding the soil (Luis)
Interpolating the measured data to the HH (Ahmed)
Preparing the presentation (Ahmed)
Research on further wind data (measured data) (Sohail + Ceren)
Research on exsitng 5 MW DFIG turbines (Sohail + Ceren)
Luis Urhahn

## Slide 21: 2. Update Soil Conditions – Homs District
Hard to find any soil data in the area…
Most reasonable data by SOIL Grids [1]:
After a discussion with the Foundation-Team:
Both locations possible, but they need improvements!
  Site of Qattinah more, due do lots of water in the area (assumption)
Additional costs need to be considered
Luis Urhahn
Depth [m] | Dataset | Clay [%] | Sand [%] | Silt [%]
0-18 | US-NCSS | 58.4 | 17.3 | 24.3
18-45 | US-NCSS | 58.4 | 15.2 | 26.4
45-80 | US-NCSS | 59.8 | 14.4 | 25.8
80-100 | US-NCSS | 59.5 | 13.8 | 26.7
100-130 | US-NCSS | 55.1 | 12.7 | 32.2
Table 1: Soil Condition in Talbiseh (north of Homs), 20 km from sites [1]
Figure 1: Showing the distance from measuring point (yellow) to locations (red) [2]
Notes: After the meeting with the Foundation-Team we came to the conclusion that both locations in the area of Homs will be suitable for a wind turbine with the size of 5 MW.
But the soil will need improvements, which could be cost intensive in the end.
The shown data in the graph is measuredin Talbiseh, which is not directly at the location (20 km distance).
In general it is really hard to find good and real measured data for the soil in the area…

## Slide 22: 3.1 Distance Analysis– Um Aledam
Final Turbine Location: 34°41'49.6"N
36°30'30.0"E
Building | Distance [m]
Building A | 515 m
Building B | 671 m
Building C | 567 m
Building D | 704 m
Building E | 1 002 m
Building F | 1 671 m
Building G | 1 083 m
Building H | 837 m
A
B
C
D
E
F
G
H
Figure 2: Distances in Um Aledam [3] & [4]
Luis Urhahn
Notes: Shows the distances to the surrounding buildings.
The critical point is with Building H because it is close to the limit of 800 m in (sometimes) wind direction. Building A-D is not relevant because they are located upwinds. Building C-D could be crucial for shadow flicker! But everything is managable.
Still a good site!
Turbine needs to be regulated when wind from north-west direction (315°)

## Slide 23: 3.2 Distance Analysis– Qattinah
Luis Urhahn
Final Turbine Location: 34°40'25"N
36°35'44"E
D
E
G
H
Qattinah Turbine Location
Figure 3: Windfarm location in Qattinah [5]
Notes: Shows the location of the possible wind turbine location / wind farm location…
We would also consider this location.
Shows also the longer distance to the substation, but it is definitely manageable!

## Slide 24: 3.2 Distance Analysis– Qattinah
Luis Urhahn
Final Turbine Location: 34°40'25"N
36°35'44"E
Building | Distance [m]
Building A | 440 m
(Building B)* | 1 041 m
Building C | 1 724 m
Building D | 1 845 m
Building E | 577 m
Building F | 603 m
(Building G)* | 428 m
(Building H)* | 321 m
C
A
D
B
E
F
G
H
* Not sure about the building
Figure 4: Distances in Qattinah [3] & [4]
Notes: Shows the distances to the surrounding buildings.
In general the distance is longer to the surrounding buildings, especially in the main wind dirction, which is cruicual!
Regarding the buildings A, the shaddow flicker will be a problem, but only in the morning ours.
With the buildings F-H, I am not sure if they are in use. I assume its for farmers or so.
In my opinion its the better side now. Only the amount of water resources could be a major problem, but according to the soil analysis it will not be a problem!

## Slide 25: 3.3 Distance Analysis– Summary
Distances for both locations in main wind direction are out of the critical distance (> 800 m),
A few buildings will limit the turbines performance in some wind directions (North to North-West),
Critical distances in the Qattinah location have a higher value (> 1 500 m)
 Our suggestion regarding the distance: Qattinah Site
Luis Urhahn

## Slide 26: Bibliography – Project Development
[1] Soil Grids, [Online]. Available: https://soilgrids.org/?utm
[2] Google, Google Maps. [Online]. Available: https://maps.google.com
[3] Google, Google Earth. [Online]. Available: https://earth.google.com/web/search/34%c2%b041%2749.6%22N+36%c2%b030%2730.0%22E/@34.67531382,36.5980701,506.39690821a,3513.70885844d,35y,360h,0t,0r/data=CiwiJgokCTkQ2iOXWkFAEQndzvkBWEFAGYw3RwMnREJAIQJ6D_SHPUJAQgIIAUICCABKCAjMjOyYBRAA
[4] Global Wind Atlas, Global Wind Atlas. [Online]. Available: https://globalwindatlas.info/en/
Luis Urhahn

## Slide 27: Weekly report: Load & Dynamics
Week number: 02
Date: 07/10/2025
Supervisor: Mr. Manjock
Group members: Md Aman
07/10/2025
Md Aman
Optimus Syria

## Slide 28: Agenda
Concept behind DLC* 1.3 & 6.1 according to DNVGL-ST-0437:2016 / IEC 61400-1:2019
ETM & Normal Calculation
TurbSim
Estimated Loads for Optimus Syria based on statistics.
Connected Group & Future Plan
* DLC = Design Load Case
07/10/2025
Md Aman
Load & Dynamics Team/ Optimus Syria

## Slide 29: DLC 1.3 & DLC 6.1
Design Load Case 1.3 from the DNVGL-ST-0437 / IEC 61400 wind turbine standard, which typically covers normal operation in extreme turbulent wind conditions.
Design Load Case 6.1 from the DNVGL-ST-0437 / IEC 61400 wind turbine standard, about parked turbine loads (when the turbine is not running).
Specifically: Extreme Wind Model (EWM) when the rotor is parked or idling.
Feature | DLC 1.3 | DLC 6.1
Turbine state | Operating, spinning, active control | Parked or idling, minimal control
Turbulence model | ETM (extreme turbulence) | EWM / ETM variant for park condition
Purpose | Extreme loads during operation | Extreme loads when not operating / safety in storm
Loads driven by | Mean + turbulence + dynamic response | Mostly high wind speeds and static pressure + wind excitation
07/10/2025
29
Load & Dynamics Team/ Optimus Syria

## Slide 30: Load cases according to DNV-ST0437 load standard
07/10/2025
30
Load & Dynamics Team/ Optimus Syria
Simulated load cases planned for this project
Source: DNVGL-ST-0437:2016

## Slide 31: ETM & Normal Operation
ETM Calculation at 7.5m/s
For V_hub = 7.5 m/s
5.625
…
ETM Calculation at 16m/s
For V_hub = 16.0 m/s
2.816 m/s
Extreme Turbulence Model (ETM) in the standards is a prescription for a (10-minute standard deviation) of the longitudinal wind speed that represents an extreme turbulence level (the ETM is defined with a 50-year return period).
(Practical IEC Implementation) A commonly used form (the same formula used by many tools that implement DNVGL / IEC ETM) for the longitudinal 10-min standard deviation, [m/s], is:
(For IIIA)
07/10/2025
31
Load & Dynamics Team/ Optimus Syria

## Slide 32: TurbSim
Turb Sim ( Turbulence Simulation )
TurbSim is a stochastic (random) wind field simulator developed by the National Renewable Energy Laboratory (NREL). It generates time-series of three-dimensional wind velocity fields that represent realistic atmospheric turbulence.
Allows to input mean wind speed, turbulence intensity, turbulence length scale, etc. into OpenFAST simulations.
07/10/2025
32
Load & Dynamics Team/ Optimus Syria

## Slide 33: Estimated Extreme Loads for Optimus Syria
07/10/2025
33
Load & Dynamics Team/ Optimus Syria

## Slide 34: Estimated Extreme Loads for Optimus Syria
07/10/2025
34
Load & Dynamics Team/ Optimus Syria

## Slide 35: Estimated Extreme Loads for Optimus Syria
 | Blade Edge moment | Blade Flap moment | Rotor thrust | Yaw Bearing Tilt moment | Rotor torque | Tower-bottom | Diameter | Tower height | Rated Power
 | kNm | kNm | kNm | kNm | kNm | kNm | m | m | KW
Optimus150 WS15 | 30,103 | 26,341 | 1,535 | 18,793 | 6,941 | 256,308 | 150 |  | 3,500
Optimus150 WS16 | 12,413 | 26,770 | 1,737 | 20,817 | 7,925 | 284,580 | 150 | 140 | 3,500
Optimus200 WS17 | 39,052 | 100,649 | 4,503 | 57,713 | 27,729 | 681,780 | 200 | 143 | 10,000
Optimus Oceanus | 52,998 | 116,570 | 4,872 | 103,990 | 49,073 | 1,189,800 | 255 | 150 | 17,000
Optimus92LE WS19 | 3,074 | 8,184 | 630 | 5,082 | 3,194 | 64,590 | 92 | 80 | 2,000
Optimus92LE WS20 | 4,070 | 7,495 | 764 | 8,432 | 2,471 | 86,020 | 92 | 80 | 2,000
Optimus60E WS21 | 2,204 | 1,872 | 304 | 1,708 | 2,005 | 28,567 | 60 | 70 | 750
Optimus Shakti | 18,358 | 42,563 | 2,376 | 29,331 | 12,496 | 376,242 | 178 | 140 | 5,000
Optimus Syria | 18,732 | 35,830 | 2,095 | 32,786 | 8,500 | 284,186 | 160 | 120 | 5,000
All values represent extreme loads (ULS) and already include the corresponding partial safety factors (γF).
07/10/2025
35
Load & Dynamics Team/ Optimus Syria

## Slide 36: Connected Group & Future Plan
Feedback Control
Talked with them for Wind field
Simulation result with MatLab Simulink
Rotor Blade Design & Structure
Provided them the needed parameter for load simulations
In the next week I’ll
contact with Tower Structure team
Configure OpenFast
Create Turbulent wind Field with TurbSim
Start With Other DLC
07/10/2025
36
Load & Dynamics Team/ Optimus Syria

## Slide 37: References
Load Reports of the OPTIMUS projects
Loads and site conditions for wind turbines, DNVGL-ST-437,Edition November 2016
NREL 5 MW
Load Simulation Seminar 2025 by Mr. Manjock
07/10/2025
37
Load & Dynamics Team/ Optimus Syria

## Slide 38: Weekly report: Feedback Controller
Week number: 02
Date: 07/10/2025
Supervisor: Prof. Dr.-Ing. David Schlipf
Group members: Mirza Dincer, Saurabh Pankaj Jha
Presenter: Mirza Dincer

## Slide 39: List of Contents
Tasks of the Week
Why IEA 3.4 MW?
ROSCO Workflow
Simulation Settings
Results
Conclusion
Mirza Dincer - 780261

## Slide 40: Tasks of the Week
Migrate files of IEA 3.4-MW model to OpenFAST v3.0 and ROSCO v2.6.0 due to them being compatible for Lidar applications
Run Simulation of the IEA 3.4-MW with feedback-only control without Lidar-Assisted controller.
Mirza Dincer - 780261

## Slide 41: Why IEA 3.4 MW ?
Mirza Dincer - 780261
[1]
Rated power capacity: 3.4 MW, designed for utility-scale wind energy generation.
Supports advanced control strategies such as individual pitch control and yaw optimization.
ROSCO implementation allows research-driven improvements and customization for specific turbine control requirements.
Facilitates simulation and testing through OpenFAST.
Clean and well documented example to start.

## Slide 42: ROSCO Workflow
DLL (Dynamic Link Library)
Linked via ServoDyn.
Manages I/O between OpenFAST and control logic.
IN (Controller Input)
Parameter file for the DLL.
Holds feature flags, modes, gains.
Mirza Dincer - 780261
[2]
Standard ROSCO workflow showing controller structure and interaction between OpenFAST and ROSCO.

## Slide 43: Simulation settings
30 seconds of simulation.
Wind speed with 12 m/s, ‘Mexican Hat’ shaped gust up to 15 m/s.
Only enabled Rotor DOF and First fore-aft tower bending-mode DOF.
Set initial conditions of rotor speed, pitch angle, tower top positions. So that turbine starts in steady state.
Running only feedback controller, no Lidar-assisted controller.
Mirza Dincer - 780261

## Slide 44: Results
Mirza Dincer - 780261
Simulation results for IEA 3.4 MW with feedback control.

## Slide 45: Conclusion
Learned how to couple ROSCO and OpenFAST.
Learned how to update OpenFAST files and ROSCO.
Should discuss with load and dynamics team for OpenFAST version for the project.
Will be updating GitHub simulation files.
Mirza Dincer - 780261

## Slide 46: Bibliography – Feedback Controller
[1] P. Bortolotti et al., “IEA Wind TCP Task 37: Systems Engineering in Wind Energy - WP2.1 Reference Wind Turbines,” OSTI OAI (U.S. Department of Energy Office of Scientific and Technical Information), May 2019, doi: https://doi.org/10.2172/1529216.
[2] N. J. Abbas, D. S. Zalkind, L. Pao, and A. Wright, “A reference open-source controller for fixed and floating offshore wind turbines,” Wind Energy Science, vol. 7, no. 1, pp. 53–73, Jan. 2022, doi: https://doi.org/10.5194/wes-7-53-2022.

## Slide 47: Report: Lidar Assisted Controller
Date: 05/10/2025
Supervisor: Prof. David Schlipf
Group members: Annika Gathje, Hesham Mahmoud, Midhun Kanichattu Venu

## Slide 48: New functions in the simulator OpenFAST
Envolving turbulence
 previous assumption: Taylor‘s frozen turbulence (wind remains constant during transport)
 new: integration of evoTurb (stochastic wind field)
 wind development reduces correlation between measured and actual wind speed
 realistic prediction of Lidar data
Blade blockage effect = Lidar beams can be blocked by rotor blades
 algorithm detects blockage through geometric modelling of the leaves
 important for signal availability and data processing
Adjustable data availability = Lidar data is dependent on CNR (carrier to noise ratio)
 modelling via spectral analysis: realistic simulation of data gaps

## Slide 49: Frozen turbulence
8

## Slide 50: New functions in the simulator OpenFAST
Envolving turbulence = integration of evoTurb (stochastic wind field)
 wind development reduces correlation between measured and actual wind speed
 realistic prediction of Lidar data
Blade blockage effect = Lidar beams can be blocked by rotor blades
 algorithm detects blockage through geometric modelling of the leaves
 important for signal availability and data processing
Adjustable data availability = Lidar data is dependent on CNR (carrier to noise ratio)
 modelling via spectral analysis: realistic simulation of data gaps

## Slide 51: Method and Implementation
EvoTurb integration
 simulate wind fields for rotor and Lidar separately
Blade blockage detection
 simplified geometry and Ray Triangle interaction algorithm
CNR modelling
 empirical spectrum and white noise comparison

## Slide 52: Setup & Tuning (OpenFAST v3.0 • ROSCO v2.6 • IEA 3.4 MW)
 | Feedback(baseline) | FF(feedforward)
DLL_FileName | ROSCO.DLL | WRAPPER.dll
DLL_InFile | IEA-3.4-130 RWT_DISCON.IN | WRAPPER.IN
ProcName | DISCON | DISCON
FFP tuning: LPF=0.5 rad/s, buffer=3 s, curve ↓ • KPIs: t>12 s, GenSpeed std & Pitch-rate std).

## Slide 53: IEA 3.4 MW — LiDAR-Assisted Feedforward (FF) on OpenFAST v3.0

## Slide 54: Results: FB vs FF (Same Wind, t = 10–30 s)
FB vs FF same wind (t=10–30 s), KPIs on t>12 s: GenSpeed std & Pitch-rate std.

## Slide 55: Conclusion and Outlook
Realistic Lidar simulation is crucial for controller development
The three new features significantly improve model fidelity
 Indispensable for interpreting data correctly
Adaptation to local atmospheric conditions necessary
controller must be able to deal with data gaps e.g. buffer storage, interpolation, adaptive control strategies
- position and orientation of the control system must be strategically chosen to minimise blockage

## Slide 56: Reference
[1] Matthew L Aitken, Michael E Rhodes, and Julie K Lundquist.
Performance of a wind-profiling lidar in the region of wind turbine rotor disks.
Journal of Atmospheric and Oceanic Technology, 29(3):347–355, 2012.
[2]Matthieu Boquet, Philippe Royer, Jean-Pierre Cariou, Mehdi Machta, and Matthieu Valla.
Simulation of doppler lidar measurement range and data availability.
Journal of Atmospheric and Oceanic Technology, 33(5):977–987, 2016
[3]David Schlipf. Lidar-Assisted Control Concepts for Wind Turbines.
Dissertation, University of Stuttgart, 2015.
[4] David Schlipf, Feng Guo, and Steffen Raach. Lidar-based estimation of turbulence
intensity for controller scheduling. Journal of Physics: Conference Series, 1618:032053, sep 2020.
[5] David Schlipf, Steffen Raach, and Florian Haizmann. Control system for controlling a turbine,
method for controlling a turbine, and wind turbine, Patent EP3717770B1, 2018

## Slide 57: Rotor Blade and Aerodynamics
Week: 3
Date: 07/10/2025
Supervisor: Prof. Dr. rer.nat. Alois Schaffarczyk
Harsh Panchal, Jay Pandya, Kandarp Pathak, Daniyal Sikander

## Slide 58: List of contents
  Flow Chart
  Selected Airfoils
  Airfoil Analysis Graphs
Harsh Panchal Matriculation Number 770278

## Slide 59: 1. Flow Chart
Reynolds number
Airfoil selection according to thickness
Airfoil analysis (Cl/Cd vs AOA),(Cl vs AOA),(Cd vs AOA)
360 degree Polar Generation
Blade Design
Chord , Twist, Bezier Curve( For smooth blade design)
Harsh Panchal Matriculation Number 770278

## Slide 60: 2. Selected Airfoils
Harsh Panchal Matriculation Number 770278
Circular Foil 6. DU40
DU21 7. NACA64
DU25
DU30
DU35

## Slide 61: Graphs
Harsh Panchal Matriculation Number 770278

## Slide 62: Bibliography
http://airfoiltools.com/search/index?m%5Bgrp%5D=naca4d&m%5Bsort%5D=1
https://qblade.org/
Harsh Panchal Matriculations Number 770278

## Slide 63: Team 5 – Rotor Blade Structures
Bhima B Masare, Anudeep Allanki, Dongsuk Kim, Mithun Shetty
Week number: 2
Date: 07.10.2025
Supervisor: Dr. Laurence Alhrshy

## Slide 64: List of contents
Anudeep Allanki
Sample Blade Geometry by Aero Team
Positioning the Airfoils (will be provided by Aero Team)
Calculating Blade Structural properties
Bibliography

## Slide 65
Anudeep Allanki
Sample Blade Geometry by Aero Team
Circular Foil
DU21
DU25
DU30
DU35
DU40
NACA64

## Slide 66
Anudeep Allanki
Rearrange the Airfoils positions on Blade span (correction)
From Root to tip of Blade the order follows –
  Circular Foil1
  Circular Foil 2
  DU40
  DU35
  DU30
  DU25
  DU21
  NACA64
Note –
NACA 0060 can be added followed by circular foils as per observations from WEC Optimus Shakti 2024
Sample Blade Geometry by Aero Team

## Slide 67
Anudeep Allanki
Rearrange the Airfoils positions on Blade span (correction)
From Root to tip of Blade the order follows –
  Circular Foil1
  Circular Foil 2
  DU40
  DU35
  DU30
  DU25
  DU21
  NACA64
Note –
NACA 0060 can be added followed by circular foils as per observations from WEC Optimus Shakti 2024
Sample Blade Geometry by Aero Team

## Slide 68
Anudeep Allanki
Data needed to proceed further
 | Data required from Aero Team
 | Data calculated by Structure Team

## Slide 69: Bibliography
Definition of a 5 MW/61.5m Wind Turbine Blade Reference Model by Brian R. Resor, Sandia National Laboratories, California, USA
Definition of a 5 MW Reference Wind Turbine for Offshore System Development, J. Jonkman, S. Butterfield, W. Musial, and G. Scott, National Renewable Energy Laboratory, USA
Q Blade Design from Blade Aerodynamics Team

## Slide 70
Weekly report: Electrical Drivetrain
Week number: 3
Date: 07/10/2025
Supervisor: Prof. Dr.-Ing. Saiju
Group members: Aiswarya Vijayan, Vishranti Shivajirao Patil , Girish Mahadeo Padalkar, Cristina Milene Vergara Hernandez
Presented By : Girish Padalkar

## Slide 71: List of contents
  DFIG Working Principle
  Converter Rating
  Local Partner & Market Strategy
  Physical and Cost Parameters
  Conclusion & Next Steps
Presented By : Girish Padalkar
Electrical Drive Train/ Optimus Syria

## Slide 72: 1. DFIG Working Principle
Presented By : Girish Padalkar
[1]
[2]
Rotor connected via slip rings to partial converter
Stator directly connected to grid
Enables variable-speed operation
Power flow
Active Power : Supplied via stator and rotor.
Reactive Power : Controlled by rotor-side converter.
Bidirectional flow : Converter enables flexible grid support.

## Slide 73: 2. Converter Rating
Partial converter : ~25 -30% of generator capacity.
For 5MW DFIG : ~1.2 MW to 1.5 MW .
Lower cost and losses vs. full-scale converters.
Parameter | Value/Range
Outer Diameter (Stator) | 2.0 – 2.5 m
Axial length | 2.0 – 2.5 m
Air Gap length | 1.0- 3.0 m
Rotational speed | 1,500 – 2,000 rpm
Generator mass | 20 – 30 tons
Physical Parameters (5MW DFIG )
Presented By : Girish Padalkar

## Slide 74: 3. Local Partner & Market Strategy
Manufacturer / Supplier | Relevant Model / Platform | Generator Type (DFIG) | Approx. Generator Weight (Component Only) | Estimated | Manufacturer / Supplier
WDRVM (Syria) | 3.X MW to 10.X MW Platforms | Geared DFIG / PMSG | N/A (Local Assembly) | Negotiable (Local Content Priority) | Initial priority for local content and support specific to Syrian grid.
Siemens Gamesa | SG 5.0-145 (2.0) Onshore | Geared DFIG | 20 to 30 Tons | $1.2 M to $1.6 M | Confirmed commercial 5.0 MW product, acts as primary European technical benchmark.
SANY | SI-16050 SE16050 (5.0 MW) | Geared DFIG | 20 to 30 Tons | $1.0 M to $1.3 M | High-volume Asian supplier; provides aggressive cost and delivery benchmark.
GE Vernova | 4.8 MW to 6.1 MW Platforms | DFIG | 20 to 30 Tons | $1.2 M to $1.6 M | Active development in this capacity range, offering competitive U.S./Global technology.
ABB / WEG | Components Only | Standalone DFIG / PMSG | 20 to 30 Tons | N/A (Component Cost) | Critical component suppliers for local WDRVM assembly or repair/maintenance.
Presented By : Girish Padalkar

## Slide 75: 4. Physical and Cost Parameter
Presented By : Girish Padalkar
[2]
Generator Specifications (Estimated for a 5 MW Geared DFIG)
Table below: Specific dimensions and air gap are proprietary data. The figures below are typical industry estimates for a high-speed, geared DFIG rated at 5 MW (50 Hz grid).
Parameter | Estimated Value / Range | Unit | Implication for Project
Rated Power | 5,000 | kW | Project Requirement
Rated Voltage | 690 | V | Standard low-voltage output for large turbines (steps up via transformer).
Maximum Speed | 1,500 to 2,000 | rpm | Requires high-ratio gearbox (typically 1:80 to 1:100).
Air Gap Length | 1.0 to 3.0 | mm | Critical for efficiency and magnetic coupling. Small air gap minimizes reactive power needs.
Outer Diameter (Stator) | 2.0 to 2.5 | m | Determines nacelle size and logistical requirements.
Axial Length (L) | 2.0 to 2.5 | m | Compact size relative to Direct Drive generators.
Generator Mass (Weight) | 20,000 to 30,000 | kg (20 to 30 Tons) | Lighter than PMSG, reducing tower top load and crane requirements.

## Slide 76: 4. Physical and Cost Parameter
Presented By : Girish Padalkar
Total Installed Wind Farm Cost: USD 1,800 to USD 2,200/kW (Onshore).
  5 MW Farm Cost: ∼USD 9 Million to USD 11 Million (Total project).
Turbine System (Generator + Nacelle + Rotor): Typically, 65% to 75% of the total farm cost.
Generator & Converter System Cost: Estimated at 15% to 20% of the total Turbine System Cost.
Cost Item | Estimated Range | Notes
DFIG Generator Unit (5 MW) | USD 550,000 to USD 800,000 | Estimate for the generator machine only.
Power Converter (2 MW Rated) | USD 600,000 to USD 900,000 | Estimate for the back-to-back converter system (partial rating).
Total DFIG Electrical Drive | USD 1.15 Million to USD 1.7 Million | This cost advantage is why DFIG is popular in the 5 MW range.

## Slide 77: 5. Next Step
Planning:
align our milestone planning with the other teams
Technical:
Generator: more detailed estimation of dimensions (size & rotational speed), Cost.
Converter: first research and collect the data of converter.
Presented By : Girish Padalkar

## Slide 78: Bibliography
text{https://en.wind-turbine-models.com/turbines/2465-sany-si-16050-se16050} [1]
https://www.pengky.cn/zz-horizontal-axis-turbine/13-doubly-fed-wind-turbine-principle/doubly-fed-wind-turbine-principle.html [2]
https://www.siemensgamesa.com/global/en/home/products-and-services/onshore/wind-turbine-sg-5-0-145.html
DFIG Market Status and Reliability: Is Using DFIG in Wind Turbines an Obsolete Technology? (Industry Article)
DFIG Product Offering (ABB): ABB Doubly-fed Generators
DFIG Turbine Platform (Siemens Gamesa): Siemens Gamesa SG 5.0-145 (2.0) Wind Turbine
Presented By : Girish Padalkar

## Slide 79
Weekly report: Grid Code Development
Week number: 2
Date: 7/10/2025
Supervisor: Prof. Ing. Saiju
Presented by: Josef Remberger / Vijay Simha Reddy Bogala

## Slide 80: List of contents
Grid operation states
  Emergency / extreme fault conditions
  Restorative / Black Start
Special connection conditions
  Withstanding LVRT capability
  Reactive Range & Voltage Control
Outlook for the coming week
Bibliography

## Slide 81: 1-i. Emergency / extreme fault conditions
Definition: That actual condition of the Power System when, due to the occurrence of one or more incidents, a part or the whole of the Power System has experienced excessive frequency deviations or Transmission voltage deviations
Frequency: 47.5 ≤ X ≥ 51.5 Hz
Voltage:
  59.5 < X > 72.5 kV
  207.0 < X > 241.5 kV
[1]

## Slide 82: 1-ii. Restorative / Black Start
Definition: The procedure necessary for a System recovery from a Total Blackout or Partial Blackout
Wind turbines are not entitled for Black Start
[1]

## Slide 83: 2-i. Withstanding LVRT capability
Wind generators must remain connected during voltage sags (e.g. cleared short circuits)
They shall withstand voltage disturbances even under second-level protection actions
[1]
Voltage Profile Recovery of Wind Generators During and After a voltage sag; [1]; (04/10/2025)

## Slide 84: 2-i. Withstanding LVRT capability
Wind generators must withstand a 0.5 s voltage dips down to 20% voltage p.u.
Voltage should recover to ≥ 80 % voltage p.u. within 1 s and ≥ 90 % voltage p.u. within 15 s after fault clearance
Wind generators must remain connected during voltage dips of similar or lower severity
They shall recover at least 90 % of pre-fault output within 1 minute
[1]

## Slide 85: 2-ii. Reactive Range & Voltage Control
Dead band of 5 % of nominal voltage is defined for normal operational conditions, with two different allowed operative conditions
  Constant Power factor
  Participate in Voltage Control
[1]
Minimum requirements for a non-synchronous machine in
voltage control; [1]; (04/10/2025)

## Slide 86: 2-ii. Reactive Range & Voltage Control
Outside the dead band ability to participate for recovery of voltage
Two different expectations according with the design of non-synchronous machines
  Voltage-controlling units: Provide full reactive current (≈ nominal current) for voltages ≤ 50 %; response < 1 s.
  Non-voltage-controlling units: Provide up to 25 % capacity (half of nominal to reactive current) via external equipment; response < 1 s
Wind generators must stay connected and stable for voltage variations between 90–110 % of nominal Voltage at the connection point
[1]

## Slide 87: 3. Outlook for the coming week

## Slide 88: Bibliography – Grid Code Development
[1] SYRRIAN ARAB REPUBLIC / Ministry of Electricity / PETE / Transmission Grid Code, 2014 (accessed Sept. 27, 2025)

## Slide 89: Rotor Hub And Pitch System
Week number : 02
Date: 07/10/2025
Supervisor: Prof. Peter Quell
Group Members :
Dhruvin Kakdiya
Adharsh Pappinisseri Veedu
Muthu Thirunavukarasu
Syed Mohammed Sikandar

## Slide 90: Agenda
07/10/2025 Dhruvin kakdiya Rotor Hub and Pitch System/Optimus syria
Comparison of Hub shape
Weighted evaluation of a pitch system
Selection of Inner or Outer ring Rotating

## Slide 91: Rotor Hub Shape Comparison
07/10/2025 Dhruvin kakdiya Rotor Hub and Pitch System/Optimus syria
Category | Star hub | Sphere hub
Aerodynamic Efficiecy | 2 | 3
Structural simplicity | 3 | 2
Manufacturing ease | 3 | 1
Maintenance access | 3 | 1
Fatigue resistance | 2 | 3
Weight | 3 | 2
Cost | 3 | 1
Suitability(Onshore) | 3 | 1
Sum | 22 | 14
1 = Low preferable, 2 = Medium preferable, 3 = High preferable

## Slide 92: Weighted Evaluation of Pitch Control Systems
07/10/2025 Dhruvin kakdiya Rotor Hub and Pitch System/Optimus syria
Criteria | Electrical Pitch | Hydraulic Pitch
Investment cost | 2 | 2
High torque | 3 | 1
Reliability | 3 | 3
Installation | 3 | 1
Operations at Hot climate | 3 | 1
Weight | 3 | 2
Service Friendliness | 3 | 2
Simple Design | 2 | 3
Sum | 22 | 15
1 = Low preferable, 2 = Medium preferable, 3 = High preferable

## Slide 93: Why Choose Electric over Hydraulic?
07/10/2025 Dhruvin kakdiya Rotor Hub and Pitch System/Optimus syria
No Hydraulic oil→ no leaks or contamination risk in hot, dusty environment.
Handles high ambient temperatures and dust reliably with IP-rated enclosures.

## Slide 94: Outer-ring rotating
07/10/2025 Dhruvin kakdiya Rotor Hub and Pitch System/Optimus syria
The blade is bolted to the outer ring and the inner ring is fixed to the hub

## Slide 95: Outer ring rotating
07/10/2025 Dhruvin kakdiya Rotor Hub and Pitch System/Optimus syria
More compact hub/lighter hub design
Simpler lubrication routing to an inner stationary ring
Pros
Cons
Higher risk of ring cracking / blade detachment
requires extra protective covers / spinner / teeth covers

## Slide 96: Inner-ring rotating
07/10/2025 Dhruvin kakdiya Rotor Hub and Pitch System/Optimus syria
The blade is bolted to the inner ring and the outer ring is fixed to the hub

## Slide 97: Inner ring rotating
07/10/2025 Dhruvin kakdiya Rotor Hub and Pitch System/Optimus syria
Safer from blade-detachment viewpoint
Pitch drives can be housed inside the hub ,simplifying environmental protection and maintenance access for the drives.
Can accommodate larger bearing diameter and more rolling elements
Pros
Cons
Hub may need to be larger to house internal drives and allow for the inner ring geometry
Internal packaging / integration is more complex (electrical routing, motor placement)

## Slide 98: Outer-ring and inner-ring rotating
07/10/2025 Dhruvin kakdiya Rotor Hub and Pitch System/Optimus syria
Topic | Outer-ring rotating (blade bolted to outer ring) | Inner-ring rotating (blade bolted to inner ring)
Which ring rotates | Outer ring rotates | Inner ring rotates
Typical pitch drive location | external or on ring perimeter | inside hub
Bearing diameter & element count | Often limited by external packaging | Easier to realize larger pitch
Assembly & maintenance | Blade bolts accessed externally | Blade bolts accessible from inside hub
Common damage modes | Outer ring hoop stresses and through-cracking near bolt holes reported in field cases | Lower incidence outer-ring through-cracks because outer ring is fixed and less stressed
Suitability | Requires reinforced outer ring and protective housings; higher inspection/maintenance attention | Preferred — allows larger diameter bearings, internal drives, improved reliability for high moments typical of 5 MW

## Slide 99: Weekly Presentation: Rotor Bearing System
Week number: 02
Date: 07/10/2025
Supervisor: Prof. Quell
Group members: Divyesh Mistry, Venkata Sreekanth .K , Sreehari Padachery, Jill Sadariya
Presenter : Venkata Sreekanth .K
Rotor Bearing System / Optimus Syria

## Slide 100: Agenda
Task of the week
Individual responsibility of components
Hydrodynamic vs Hydrostatic
Suggestion for Hydrodynamic bearing
Manufacturing of Shaft
Rotorlocking System
Approached companies & experts
Venkata Sreekanth .K
Rotor Bearing System / Optimus Syria

## Slide 101: Task of the week
Divided individual responsibilities of components among team members.
Contacted couple of bearing manufactures and some experts regarding spherical journal bearing suited for 5MW.
Conducted research about the components like rotor lock ,shaft and type of journal bearing.
Venkata Sreekanth .K

## Slide 102: Individual responsibility of components
Group Members | Components
Divyesh Mistry & Venkata Sreekanth.k | Rotor Shaft
Jill Sadariya & Sreehari Padachery | Journal Bearing
Jill Sadariya | Rotor Lock
Sreehari Padachery | Bearing Housing
Venkata Sreekanth.k | Coupling
Divyesh Mistry | Flanges
Venkata Sreekanth .K

## Slide 103: Hydrodynamic vs Hydrostatic Journal bearing
Venkata Sreekanth .K
Feature | Hydrodynamic Bearing | Hydrostatic Bearing
Startup & Low-Speed Operation | High friction | Virtually zero startup friction
Load Carrying Capacity & Stiffness | Depends on rotational speed | Independent of rotational speed.
Maintenance & System Complexity | Mechanically simpler system with fewer components. | More complex system requiring an external pump, filters, piping, and controls
Damping & Vibration Control | Good damping characteristics from the oil film. | Superior damping characteristics, leading to smoother operation and better absorption of vibrations from wind gusts and rotor imbalance.
Cost-Benefit Analysis | Low CAPEX High OPEX | High CAPEX Low OPEX

## Slide 104: Suggestion for Hydrodynamic bearing
We contacted Howatech Bearings in Germany, and they recommended using a hydrodynamic bearing for the low-speed shaft. For more detailed information, they advised us to get in touch with RENK.
General trend in the wind industry is that Hydrodynamic Journal bearing is used.
Venkata Sreekanth .K

## Slide 105: Manufacturing of the Shaft
Venkata Sreekanth .K
Forged | Casted
Suitable for cyclic loading, better fatigue behaviour in low-cycle fatigue. | Different cast iron types offer a wide range of property combinations.
Minimizes pores, cavities, and microstructural defects | Volume reduction in low-stress areas can save material, reducing component weight.
Higher strength | can be more brittle
Restricts the shaping of components, limiting design adaptations for specific loading conditions | Suitable for complex shapes and customizations, adaptable to individual loading situations.
Requires higher energy during smelting | Requires less energy for cast iron smelting
Tooling and setup costs can be significant, especially for small production quantities | High damping capacity against vibrations
Material generally used: 42CrMo4 | Material generally used: ductile cast iron EN GJS-400-18-LT and EN GJS-350-22-LT
High Cost of Manufacturing | Low Cost of Manufacturing

## Slide 106: Shaft Dimension
Rotor diameter of the shaft :
Optimus | Rotor diameter | Rotor shaft diameter
Shakti | 178m | 1.4m
60E | 60m | .440m
Syria | 160m | 1.6m
Rotor shaft diameter : +/- 1 or 1.5% of Rotor diameter
By doing some research we assume that the distance between the lever and main bearing should be between 2-3m.
Venkata Sreekanth .K
Rotor Bearing System / Optimus Syria

## Slide 107: Rotor Locking System
Venkata Sreekanth .K
Feature | Hydraulic Caliper Brake with Lock Pin | Purely Mechanical Pin/Ratchet Lock | Gearbox-Integrated Lock
Locking Torque | Very High | Extremely High | High
System Complexity | Moderate to High | Low to Moderate | High
Reliability | Very good | Excellent | Good
Maintenance | Regular inspection required | Simpler maintenance | Difficult
Safety & Redundancy | Excellent | Excellent | Good
Cost | Moderate | Low to Moderate | High

## Slide 108: Recommended Rotor Locking System
Venkata Sreekanth .K
For a modern 5MW wind turbine, especially in an offshore application, the best and most widely adopted method is the fail-safe Hydraulic Caliper Brake System with an integrated Mechanical Lock Pin.
Reasoning:
Safety through Redundancy: This system provides two crucial functions. The fail-safe brakes can safely stop the rotor in an emergency and hold it, while the mechanical pin offers a secondary, energy-free lock that is essential for ensuring the safety of maintenance crews.
Proven Technology: This approach is mature, well-understood, and has a long track record of reliability in the field.
High Performance: It meets the extreme torque requirements of multi-megawatt turbines and offers powerful dynamic braking, which a purely mechanical lock cannot provide

## Slide 109: Approached companies & experts
Waiting for reply from the following companies
Venkata Sreekanth .K
Bearing specialist from Vestas clearly told they cannot share any information regarding Journal bearing due to competion and confidentiality.
Waiting for reply from Fraunhofer IWES and CSC Bearing Europe GmbH.

## Slide 110: Gearbox, Brake, Coupling
Week number : 03
Date: 07/10/2025
Supervisor: Prof. Peter Quell
Group Members :
Nehang Jitendra Joshi
Santo Mazumder
Md Razaul Karim Rahat
Arham Memon

## Slide 111: Agenda for 3rd week
Team design
Concept of drive train choice
Basic idea about brake system
Insight about the coupling
Chapter | Responsible person
Introduction | All team members
Project order | All team members
Gearbox | Nehang + Arham
Rotor brake | Rahat+Nehang
Coupling | Santo+Nehang
Coordinate with internal group--
Rotor hub,Bearing,Machine bed (Mechanical Input)
Electrical Drivetrain Team (Mechanical Output)

## Slide 112: Drive train system
Main Objective:
Break down analysis of 3-Point suspension concept for each criteria of selection
Source-https://www.researchgate.net/

## Slide 113: 3-Point suspension
Criteria of drive train | 4Point suspension Modular | 3point suspension Semi-integrated | Integrated | hybrid | Direct drive
Low capex | 1 | 3 | 2 | 1 | 1
High serviceability | 3 | 3 | 1 | 1 | 1
Easy to assemble | 2 | 3 | 3 | 3 | 2
Availability of spear parts | 3 | 3 | 1 | 1 | 1
Light weight | 1 | 2 | 3 | 2 | 3
Transport | 3 | 3 | 1 | 1 | 2
Reliability | 1 | 2 | 2 | 2 | 3
Paired comparison analysis for drive train
Total Points
4Point suspension Modular --- 14
3point suspension Semi-integrated-- 19
Integrated-- 13
Hybrid-- 11
Direct drive-- 13

## Slide 114
Criteria of drive train | 4Point suspension Modular | 3point suspension Semi-integrated | Integrated | hybrid | Direct drive
Low capex | High cost due to complexity, additional materials. | fewer components and simpler geometry | omplex design, tooling, and manufacturing | depends on how the hybrid is implemented. Can reduce cost through smart design | precision motor design and electronics needed.
High serviceability | More moving parts mean more maintenance | due to simplicity and fewer joints | difficult to access internal components without specialized tools | some parts are easy to fix, others not | fewer moving parts, but harder to repair motor if it fails
Easy to assemble | Requires precise alignment and more components to mount | often DIY-friendly | often assembled in factory only | custom instructions, especially if parts are not standardized | no chain or transmission
Availability of spear parts | especially in mainstream markets | due to standardization | harder to source and replace | some parts standard, others proprietary | specially if proprietary motor is used.
Light weight | due to extra linkages and hardware | design is a major benefit | helps reduce external mounts and improves aerodynamics | depending on materials and structure. | due to fewer mechanical parts
Transport | may require partial disassembly for shipping | better for packaging or folding designs | more fragile due to enclosed systems | some parts may be detachable, others fixed. | fewer parts means easier logistics
Reliability | especially in demanding terrain or under load. Built for durability | but may not perform well under heavy stress or rough terrain | components are protected from the elements. Risky if one part fails | if well-engineered – benefits from best of both worlds | no wear on chains/gears, fewer failure points.

## Slide 115: Gearbox system
Main Objective:
Break down analysis of planetary gearbox concept for each criteria of selection.
Criteria Key Points for Planetary Gearbox.

## Slide 116: Gearbox system
Source- Planetary System gears by SMC
Manufactures

## Slide 117: Gearbox system
Criteria Key Points for Planetary Gearbox
Design -Compact, multiple gear ratios, load sharing, low backlash possible
Manufacturing-Precision machining, heat treatment, quality materials, tight tolerances
Space Requirement-Very compact for torque output; coaxial design saves space
Weight- High torque-to-weight ratio; lightweight options available
Efficiency- High (95–98%), optimized by quality gears and lubrication
Reliability -Excellent with proper design and maintenance; robust against heavy-duty use

## Slide 118: Rotor Brake
Main Objective:
Break down analysis of Rotor brake.
Criteria Disc Brake System.

## Slide 119: Rotor Brake
Source- KTG AUTO

## Slide 120: Rotor Brake
Source- KTG AUTO

## Slide 121: Rotor Brake
Criteria Disc Brake System-
Design-Simple, open design with rotor, caliper, and pads. Good for cooling and modularity.
Manufacturing- Mature process; rotor and caliper materials vary with performance level.
Space Requirement-Compact design, but performance setups need larger wheels and calipers.
Performance & Pressure-Excellent braking, quick heat dissipation, linear pressure response.
Weight- Moderate; lighter than drums at high end, but heavier at low cost.
Maintenance & Reliability- Easy access, frequent pad changes, prone to corrosion/warping.
Cost- Affordable for mass production; premium for high-performance materials.

## Slide 122: Coupling
Main Objective:
Break down analysis of Coupling
Criteria Coupling

## Slide 123: Coupling

## Slide 124: Coupling
Criteria Disc Brake System-
Design-Compact, torsionally rigid, high misalignment capability
Protection-Requires external guards; corrosion-resistant options available
Efficiency--Very high (>99%), no backlash, no lubrication needed
Service & Maintenance- Low; visual inspection and alignment checks sufficient
Reliability & Weight-Very reliable, lightweight, fatigue-resistant
Cost-High upfront cost, low over time due to durability

## Slide 125: Bibliography
https://www.twiflex.com/en/newsroom/2016/02/is-caliper-brake-solutions-for-wind-turbines
https://antec-group.com/wp-content/uploads/2021/12/Catalogo-Wind-2022.pdf
https://www.twiflex.com/en/newsroom/2016/02/is-caliper-brake-solutions-for-wind-turbines
https://www.windsourcing.com/en/spare-parts-and-repair-material/brakes/brake-calipers/
https://www.ktr.com/de/en/products/brake-systems/
https://www.zf.com/products/en/wind/home/wind.html#:~:text=Empowering%20a%20Sustainable%20Future%20Together&text=ZF%20Wind%20Power%20develops%2C%20together,future%20together%20with%20our%20partners.
https://www.flender.com/en/branchesAndApplications/winergy#:~:text=Two%20powerful%20brands%20%2D%20one%20company,wind%20for%20a%20better%20future.

## Slide 126: Weekly report: Machine Bed & Yaw System
Week # 2
Date: 07/10/2025
Supervisor: Prof. Quell Peter
Group members: Shoukat Abbas, Luksh Chawla, Sathishkumar Venkatachalam, Shrihari Kadam
Flensburg University of Applied Sciences

## Slide 127: Contents
Reference Models For Bed plate - 5MW with 4-point support
Reference Models For Bed plate - 5MW with Separated Bed plate
Reference Models from Optimus Sakthi
Coordinate system & load definitions (IEC)
Axial Load and Radial load Comparison
About NGC Group
Reference
Shoukat Abbas, Luksh Chawla, Sathishkumar Venkatachalam, Shrihari Kadam

## Slide 128: Reference Models For Bed plate - 5MW with 4 point support
Credits: Norwegian University of Science and Technology - Dr. Jason Jonkman, Prof. Erin Bachynski-polic Source: [2]
Shoukat Abbas, Luksh Chawla, Sathishkumar Venkatachalam, Shrihari Kadam

## Slide 129: Reference Models For Bed plate - 5MW with 4 point support
1. Models are Same, Changes in Design
2. Design Changes in Tail Area, Addition of casting material.
3. Ribs and Cost cuttings are Added - For stability and reduction of Material Weight & cost.
Shoukat Abbas, Luksh Chawla, Sathishkumar Venkatachalam, Shrihari Kadam

## Slide 130: Reference Models For Bed plate - 5MW with Seperated Bed plate
Source : https://www.mdpi.com/1996-1073/14/12/3581?utm_source [3]
Shoukat Abbas, Luksh Chawla, Sathishkumar Venkatachalam, Shrihari Kadam

## Slide 131: Reference Models from Optimus Sakthi
Shoukat Abbas, Luksh Chawla, Sathishkumar Venkatachalam, Shrihari Kadam

## Slide 132
For Optimus Syria - What do we decide at the moment to go for in Design?
Bed type:
  Go for Casting
Material:
  Grey Cast Iron (EN-GJL-250 (GG25)
  Price as per market - 2.8 to 3.2 Euro / Kg
Max. Weight of a Machine Bed:
  15 to 22 tons ( For 5MW turbine)
Single frame Design, may be changed into separate in the future (If needed)
Shoukat Abbas, Luksh Chawla, Sathishkumar Venkatachalam, Shrihari Kadam

## Slide 133: Coordinate system & load definitions (IEC)
133
Fig: Global blade coordinate system [1]
Blade-root coordinates:
  X = Thrust (along shaft)
  Y = vertical radial / flapwise (along y)
  Z = lateral / side to side (along z)
Hub / Nacelle coordinates:
  Fx = axial force, Mx is rotor torque moment (about x)
  Fy = radial (vertical), My = tilting moment (about y)
  Fz = lateral force, Mz = yaw moment (about z)

## Slide 134: Axial Load and Radial load Comparison
134
Formula:
Shakti diameter: 174 m
Syria diameter: 160 m
Scaling factor = (160 / 174)² ≈ 0.845
Case 1: Shakti axial = 700 kN → Syria axial ≈ 700 × 0.845 = 592 kN
Case 2: Shakti axial = 900 kN → Syria axial ≈ 900 × 0.845 = 761 kN
Case 1: Shakti radial = 800 kN → Syria radial ≈ 800 × 0.845 = 676 kN
Case 2: Shakti lateral = 2000 kN → Syria lateral ≈ 2000 × 0.845 = 1690 kN

## Slide 135
135
Multi-megawatt pitch gearboxes and yaw drives wind turbines.
With more than 20 years of experience in the wind energy field
Product Features
    Torque: 10 kNm - 250 kNm
    Wind turbine power: 1x MW - 15 MW
    High bearing capacity
    High reliability and efficiency
    Compact design
Applications
    Onshore & offshore
    Low & high-altitude areas (> 1000 m)
    Low & high temperature environments (-40 °C to + 50 °C)
    Low wind speeds
Nanjing High Accurate Drive Equipment Mfg Group Co., Ltd. (NGC Group)

## Slide 136: References
136
[1] P. N. Castelos, “On the impact of multi-axial stress states on trailing edge bondlines in wind turbine rotor blades,” https://www.researchgate.net, Oct. 2016. https://www.researchgate.net/publication/308793459_On_the_impact_of_multi-axial_stress_states_on_trailing_edge_bondlines_in_wind_turbine_rotor_blades
[2] V. Liverud, J. Jonkman, and Bachynski-Polić, “Drivetrain structural flexibility in OpenFAST.” Accessed: Oct. 06, 2025. [Online]. Available: https://www.sintef.no/globalassets/project/eera-deepwind-2023/presentasjoner/substructures_krathe.pdf?utm_source
[3] A. S. Pehlivan, M. F. Aksit, and K. Erbatur, “Fatigue Analysis Design Approach, Manufacturing and Implementation of a 500 kW Wind Turbine Main Load Frame,” Energies, vol. 14, no. 12, p. 3581, Jun. 2021, doi: https://doi.org/10.3390/en14123581.

## Slide 137: Weekly report: Tower structure
Week number: 02
Date: 06/10/2025
Supervisor: Prof. Faber
Group members: Ibrahim Mostafa, Mohammed Eldemerdash, Kirolls Ghaly
Speaker: Ibrahim Mostafa(770134)

## Slide 138: List of contents
Selecting Suitable Dimensions for the Tower
Tower structure team/ Optimus Syria
Group members: Ibrahim Mostafa, Mohammed Eldemerdash, Kirolls Ghaly

## Slide 139
1-Tubular Steel tower system primary design
Tubular steel tower for Siemens
Tower structure team/ Optimus Syria
Group members: Ibrahim Mostafa, Mohammed Eldemerdash, Kirolls Ghaly

## Slide 140
Loads calculations and stress analysis
Fig 9: how the different loads and moments affect the wind turbine
Tower structure team/ Optimus Syria
Group members: Ibrahim Mostafa, Mohammed Eldemerdash, Kirolls Ghaly

## Slide 141
Assumptions
𝜌air=1.225 kg/m3
𝜌steel=7850 kg/m3
(Wind class III) 𝑉=37.5 m/s
𝑔=10 m/s2
𝐷rotor=160 m, 𝐷𝑜=6.0 m, 𝑡=0.027 m
⇒ 𝐷𝑖=5.946
𝐻tower=98 m
ℎhub=100 m
𝐶𝑇=0.5
𝐶𝐷=1 ​
𝑚rotor=110,000 kg
𝑚nacelle=240,000 kg
𝑚RNA=350,000 kg
𝑀nacelle=4200 kN
Loads calculations and stress analysis
Tower structure team/ Optimus Syria
Group members: Ibrahim Mostafa, Mohammed Eldemerdash, Kirolls Ghaly
Reference to data assumptions:
https://www.nrel.gov/wind/data-tools

## Slide 142
Loads calculations and stress analysis
Tower structure team/ Optimus Syria
Group members: Ibrahim Mostafa, Mohammed Eldemerdash, Kirolls Ghaly

## Slide 143
Loads calculations and stress analysis
Tower structure team/ Optimus Syria
Group members: Ibrahim Mostafa, Mohammed Eldemerdash, Kirolls Ghaly

## Slide 144
2. Tubular steel tower with tie system, primary design.
Tower structure team/ Optimus Syria
Group members: Ibrahim Mostafa, Mohammed Eldemerdash, Kirolls Ghaly
Assumptions
𝜌air=1.225 kg/m3
𝜌steel=7850 kg/m3
(Wind class III) 𝑉=37.5 m/s
𝑔=10 m/s2
𝐷rotor=160 m, 𝐷𝑜=9.0 m, 𝑡=0.027 m
⇒ 𝐷𝑖=8.946
𝐻tower=98 m
ℎhub=100 m

## Slide 145
2. Tubular steel tower with tie system, primary design.
Tower structure team/ Optimus Syria
Group members: Ibrahim Mostafa, Mohammed Eldemerdash, Kirolls Ghaly

## Slide 146
2. Tubular steel tower with tie system, primary design.
Tower structure team/ Optimus Syria
Group members: Ibrahim Mostafa, Mohammed Eldemerdash, Kirolls Ghaly

## Slide 147
2. Tubular steel tower with tie system, primary design.
Tower structure team/ Optimus Syria
Group members: Ibrahim Mostafa, Mohammed Eldemerdash, Kirolls Ghaly

## Slide 148
2. Tubular steel tower with tie system, primary design.
Tower structure team/ Optimus Syria
Group members: Ibrahim Mostafa, Mohammed Eldemerdash, Kirolls Ghaly

## Slide 149
Loads calculations and stress analysis
Tower structure team/ Optimus Syria
Group members: Ibrahim Mostafa, Mohammed Eldemerdash, Kirolls Ghaly

## Slide 150
Loads calculations and stress analysis
Tower structure team/ Optimus Syria
Group members: Ibrahim Mostafa, Mohammed Eldemerdash, Kirolls Ghaly

## Slide 151
Loads calculations and stress analysis
Fig : Original handwritten calculations
Tower structure team/ Optimus Syria
Group members: Ibrahim Mostafa, Mohammed Eldemerdash, Kirolls Ghaly

## Slide 152: work distribution
Mohammed Eldemerdash:
Searching for the wind loads in IEC 61400-1 code .
Ibrahim Mostafa:
Load calculations and primary design.
Kirollos Ghaly:
- no input
Tower structure team/ Optimus Syria
Group members: Ibrahim Mostafa, Mohammed Eldemerdash, Kirolls Ghaly

## Slide 153: Weekly report: Foundations
Week number: 03
Date: 07/10/2025
Supervisor: Prof. Dr.-Ing. Torsten Faber
Group members : Jehad Albaali- Amgad Gerges - Reda Deif
presented by : Amgad Gerges

## Slide 154: List of contents
Soil Profile for Qattinah .
Soil Properties for Qattinah
`Choose Type of Foundations .
Foundations team/ Optimus Syria
Group members: Jehad Albaali- Amgad Gerges - Reda Deif

## Slide 155
Soil Profile for Qattinah
Foundations team/ Optimus Syria
Group members: Jehad Albaali- Amgad Gerges - Reda Deif
https://soilgrids.org/?utm
https://earth.google.com/web/search/34%c2%b041%2749.6%22N+36%c2%b030%2730.0%22E/@34.67531382,36.5 980701,506.39690821a,3513.70885844d,35y,360h,0t,0r/data=CiwiJgokCTkQ2iOXWkFAEQndzvkBWEFAGYw3RwMnRE JAIQJ6D_SHPUJAQgIIAUICCABKCAjMjOyYBRAA

## Slide 156: Soil Properties for Qattinah
Foundations team/ Optimus Syria
Group members: Jehad Albaali- Amgad Gerges - Reda Deif
Depth | Soil Type | Moduls of Elasticity | Friction Angle | Cohesion | Density | Poisson Ratio
(m) |  | KN/m2 | [°] | KN/m2 | KN/m3 | 
0 - 18 | Soft to medium clay (CL / CL–OL) | 7000 | 20o | 15 | 18 | 0.45
18 - 45 | Medium cohesive clay | 11,000 | 22o | 20 | 19 | 0.45
45 – 80 | Stiff to very stiff clay (CL–CH) | 20,000 | 24o | 25 | 20 | 0.45
80 – 100 | Very stiff clay | 25,000 | 26o | 30 | 21 | 0.40
https://soilgrids.org/?utm

## Slide 157
Foundations team/ Optimus Syria
Group members: Jehad Albaali- Amgad Gerges - Reda Deif
Choose Type of Foundations
The estimated type of foundation for our turbine will be shallow foundation type (mat with round shape)
Reasons for estimated shallow foundation type
More effective cost than deep foundation
Simple and Fast to Construct
we don’t need specialized equipment , which reduces construction time and cost
ground water is at depth 74.5 m so it will not be affected by ground water.
Reasons for estimated round shape type
Uniform Load and Moment Distribution
Smaller Perimeter for the Same Area ( amount of concrete and steel Rebar decrease )
: http://ggis.un-igrac.org/

## Slide 158
Foundations team/ Optimus Syria
Group members: Jehad Albaali- Amgad Gerges - Reda Deif
Next Task
Estimation of Concrete Dimensions depending on estimations loads
Estimation Weight of foundation

## Slide 159: Weekly report: Storage System
Week number: 02
Date: 07/010/2025
Supervisor: Dr. Laurence Alhrshy
Group members: Mohamed Ahmed

## Slide 160: Battery Technologies for Large-Scale Energy Storage
Content
Introduction
Lithium-Ion Batteries
Sodium-Sulfur Batteries
Flow Batteries
Comparative Summary Table
Technology Selection for Our Project
Conclusion

## Slide 161: Introduction
Energy storage lies at the core of the renewable energy revolution. As the world shifts toward clean and sustainable power, batteries have become essential for balancing supply and demand.
In this presentation, we will explore the main battery technologies used for large-scale energy storage, highlighting their advantages, disadvantages, costs, and leading manufacturers. Finally, based on our analysis, we will identify the most suitable battery type for our project.

## Slide 162: Lithium-Ion Batteries Lithium-Ion Batteries: Pros & Cons
Cons | Pros
High Cost: More expensive upfront compared to other battery types | High Energy Density: Stores a large amount of energy in a compact, lightweight form (150–200 Wh/kg).
Limited Lifespan: Capacity gradually decreases (~20% loss after 500 cycles) | Long Cycle Life: Can last several years with over 1,000 charge–discharge cycles.
Safety Risks: Risk of thermal runaway, requiring careful handling. | Fast Charging: Allows quick recharge with new fast-charging technologies.
Environmental Impact: Mining and disposal affect sustainability. | Low Self-Discharge: Retains charge well (only 2–3% loss per month).
Temperature Sensitivity: Performance drops in extreme temperature. | Variety of Sizes and Shapes: Flexible design for multiple applications.

## Slide 163: Sodium-Sulfur Batteries
Sodium-Sulfur Batteries: Pros & Cons
Disadvantages | Advantages
Operates at high temperatures (300–350°C) | High energy density (~150 Wh/kg)
Safety risks due to molten sodium and sulfur | Long cycle life (1000–2000 cycles)
Large size and heavy weight | High charge/discharge efficiency (89–92%)
Shuttle effect can reduce capacity and performance | Relatively low cost per unit energy
Poor performance at room temperature | Compatible with renewable energy storage

## Slide 164: Flow Batteries
Flow Battery Technologies: RFBs have been investigated and produced during the past few decades using various chemistries. Among them the commercialized deployment of all vanadium RFB began in the 1980s.
Main types of Flow Batteries
All-Vanadium Redox Flow Battery (VRFB)
Zinc–Bromine Flow Battery (ZBFB)
Iron–Chromium Flow Battery (Fe–CrFB)
Aqueous Organic Redox Flow Battery (AORFB)
Metal–Air Flow Battery (MAFB)
Semi-Solid Flow Battery (SSFB)
Solar Redox Flow Battery (SRFB)
Solid-Mediated Flow Battery (SMFB)

## Slide 165: Flow Batteries
Flow Batteries: Pros & Cons
Disadvantages | Advantages
Low energy/power density | Very low stand-by loss (almost no self-discharge)
High capital cost, especially membranes ($200–600/m²; new membranes ~$50/m²) | Stable performance regardless of power demand
Requires technological improvements for industrial applications | Long cycle life (≥2000 cycles on average; some >10,000)
Need for optimized cell design to reduce ohmic and activation losses | Electrodes remain chemically and physically stable
Complex system structure (separate tanks, flow fields) | High safety and recyclability

## Slide 166: Costs & Leading Manufacturers
Leading Manufacturers | Costs | Types
China-based CATL and BYD, South Korean companies ,like LG and Samsung SDI, and Japan-based Panasonic. Other notable players are the US-based Tesla Gigafactories and several prominent companies in China, such as Tianneng Group and Microvast. | about $151 per kWh | Lithium-Ion Batteries
Infinite Energy Systems (UK) Sumitomo Electric Industries, Ltd. (Japan) VRB Energy (Canada) Enerox GmbH (Austria) Elestor (The Netherlands) ESS Tech, Inc. (US) Largo Inc. (Canada) Lockheed Martin Corporation (US) Primus Power (US) | $260–$500 per kWh (The price varies depending on the type) | Flow Batteries
NGK Insulators Ltd.,EaglePicher Technologies LLC,GE Energy Storage,BYD Company Limited,Furukawa Battery Co., Ltd.,Amara Raja Batteries Ltd.,Samsung SDI Co., Ltd. EnerVault Corporation,Ceramatec, Inc.,Sieyuan Electric Co., Ltd. | $300–$450 per kWh | Sodium-Sulfur Batteries

## Slide 167: Technology Selection for Our Project
Project Conditions:
The wind turbine is IEC Class 3A with a 160 m rotor diameter, indicating high capacity and variable generation.
The system requires medium to long-term energy storage (several hours) to balance wind fluctuations.
Project space is not highly constrained, allowing installation of a large-scale Flow Battery system.
Safety and long lifespan are prioritized over high energy density.
Final Selection: Vanadium Redox Flow Battery is Most suitable for large-scale wind applications, providing long-duration storage, stable performance, and extended operational lifetime.
Hybrid Energy Storage System (HESS): Flow Battery: For long-duration energy storage (hours). Li-ion Battery: For fast response and frequency regulation.

## Slide 168: Technology Selection for Our Project
Enerox / CellCube (Austria / The CellCube family) Why?
European manufacturing — high quality and reliable production standards.
Geographical proximity (Europe → Middle East) — easier logistics and shorter delivery times.
Proven operational track record — numerous successful systems deployed across Europe.
Strong commercial experience — established projects and long-term clients
Easy communication and support — accessible and responsive European supplier

## Slide 169: References
https://www.battery.associates/post/state-of-art-of-flow-batteries-a-brief-overview
https://bslbatt.com/blogs/lithium-battery-price-2025-current-costs-trends-and-changes/
https://www.sciencedirect.com/science/article/pii/S0306261924003374
https://www.skyquestt.com/report/sodium-sulfur-battery-market/companies
https://www.sciencedirect.com/topics/engineering/sodium-sulfur-battery#:~:text=Sodium%E2%80%93sulfur%20batteries%20offer%20long%20battery%20lifetime%20(up,its%20explosiveness%20have%20constrained%20its%20wide%2Dscale%20implementation.