## Slide 1: Weekly report: Team Project Development
Group members: Luis Urhahn, Ahmed Sallam, Ceren Cetin, Sohail Mansuri
Presenter: Luis Urhahn
Week number: 05
Date: 26/10/2025
Supervisor: Dr. Marina Blohm

## Slide 2: List of content
Task of this week
Further update on wind analysis – Weibull-Distribution
Overview sub-tasks
Progress of the tasks
  Detailed Site Analysis
  WindPro Simulation
  Economic calculation (LCOE)
Updated timeline
Questions and Requests
Luis Urhahn

## Slide 3: 1. Tasks of the week
Optimizing/Updating the Weibull-Distribution
Working and progressing the sub-tasks
  Detailed site analysis
  WindPro Simulation
  Economic calculation (LCOE)
Luis Urhahn

## Slide 4: 2. Update on wind analysis (HH = 100m)
Luis Urhahn
Wind range [m/s] | Windbins [m/s] | Absolute Frequency (n_i) | Cumulative Distribution Function F(v) | Probability Density Function f(v)
0 - 1 | 0.5 | 154 | 0.00293 | 0.022910994
1 - 2 | 1.5 | 1863 | 0.03544 | 0.047745282
2 - 3 | 2.5 | 3652 | 0.06948 | 0.06430642
3 - 4 | 3.5 | 4805 | 0.09142 | 0.075101365
4 - 5 | 4.5 | 4736 | 0.09010 | 0.081127619
5 - 6 | 5.5 | 4180 | 0.07953 | 0.08316111
6 - 7 | 6.5 | 3796 | 0.07222 | 0.08194524
7 - 8 | 7.5 | 3353 | 0.06379 | 0.078210087
8 - 9 | 8.5 | 2975 | 0.05660 | 0.072651867
9 - 10 | 9.5 | 2856 | 0.05434 | 0.065906216
10 - 11 | 10.5 | 2746 | 0.05224 | 0.0585264
11 - 12 | 11.5 | 2691 | 0.05120 | 0.050970001
12 - 13 | 12.5 | 2550 | 0.04852 | 0.043594435
13 - 14 | 13.5 | 2343 | 0.04458 | 0.036660096
14 - 15 | 14.5 | 2134 | 0.04060 | 0.030339248
15 - 16 | 15.5 | 1831 | 0.03484 | 0.024728617
16 - 17 | 16.5 | 1566 | 0.02979 | 0.019863793
17 - 18 | 17.5 | 1319 | 0.02509 | 0.015733853
18 - 19 | 18.5 | 1078 | 0.02051 | 0.012295033
19 - 20 | 19.5 | 753 | 0.01433 | 0.009482683
20 - 21 | 20.5 | 477 | 0.00908 | 0.007221106
21 - 22 | 21.5 | 332 | 0.00632 | 0.005431172
22 - 23 | 22.5 | 204 | 0.00388 | 0.004035826
23 - 24 | 23.5 | 96 | 0.00183 | 0.002963737
24 - 25 | 24.5 | 35 | 0.00067 | 0.002151412
25 - 26 | 25.5 | 28 | 0.00053 | 0.00154413
26 - 27 | 26.5 | 8 | 0.00015 | 0.001096003
27 - 28 | 27.5 | 0 | 0.00000 | 0.00076947
28 - 29 | 28.5 | 0 | 0.00000 | 0.000534444
29 - 30 | 29.5 | 0 | 0.00000 | 0.000367296
30 - 31 | 30.5 | 0 | 0.00000 | 0.000249806
Parameter | Unit | Number
Number of Measurements | / | 52560
Mean value (v_bar) | m/s | 8.49
standard deviation (sigma_v) | m/s | 5.1399
Ratio | / | 0.6054
Form Parameter (k) | / | 1.7246
Gamma-Argument | / | 1.5798
Gamma-Value | / | 0.8914
Scale Parameter (A) | m/s | 9.52
Form Parameter:
Scale Parameter:
[5] [6] [7]

## Slide 5: 2. Weibull-Distribution
Luis Urhahn
Chart: Weibull-Distribution [Shape Parameter k = 1.72, Scale Parameter A = 9.52 m/s]
Cumulative Distribution Function F(v) | 0.0029299 | 0.035445 | 0.069481 | 0.091418 | 0.090105 | 0.079527 | 0.072221 | 0.063793 | 0.056601 | 0.054337 | 0.052244 | 0.051198 | 0.048515 | 0.044577 | 0.0406 | 0.034836 | 0.029794 | 0.025095 | 0.02051 | 0.014326 | 0.0090752 | 0.0063165 | 0.0038812 | 0.0018264 | 0.00066589 | 0.00053271 | 0.0001522 | 0 | 0 | 0 | 0
Probability Density Function f(v) | 0.021269 | 0.045526 | 0.062185 | 0.073376 | 0.079933 | 0.082526 | 0.08183 | 0.078532 | 0.073306 | 0.066784 | 0.059526 | 0.052005 | 0.044599 | 0.037585 | 0.031157 | 0.025425 | 0.020437 | 0.016191 | 0.012648 | 0.0097474 | 0.0074133 | 0.0055659 | 0.0041266 | 0.0030221 | 0.0021867 | 0.0015637 | 0.0011052 | 0.00077228 | 0.00053361 | 0.00036464 | 0.00024647
[5] [6] [7]

## Slide 6: 3. Overview of the sub-tasks
Luis Urhahn
Detailed Site-Analysis
Legal framework
QGIS Analysis
WindPro Simulation
Project setup
Wind Resource Implementation
Economic Calculation (LCOE)
Tool setup
Environmental Impact Assessment (EIA)
Transportation study
Grid connection plan
(Land leasing)
(Conflict of Interests)
Layout Design
Compliance Optimization
Final Calculation
Collecting all the input parameters (component costs)
Including the AEP
Calculating the LCOE

## Slide 7: 4.i Progress: Detailed Site Analysis
Luis Urhahn
Figure 1: Overview of the QGIS “White Mapping” Progress [9]

## Slide 8: 4.ii Progress: WindPro Simulation
Luis Urhahn
Set-up of the WindPro model:
  Set-up of site location
  Creating the WTG area
  Defining the Orography
  Defining the Roughness
Figure 2: Screenshot from the WindPro Simulation [8]

## Slide 9: 4.iii Progress: Economic Calculation (LCOE)
Luis Urhahn
Interest rate
Possible incentives
12 cent and 30 cent per kWh or higher depend on actual gas price market .
Actual electricty price in syria
Work plan for LCOE
Wind Electricity Purchase Price (Tariff)
BOQ (Bill of Quantity)from all teams
Discount rate determination
Setting a target value for LCOE
Calculating the NPV (net present Value )
Make a sensitivity analysis
Determine our cost drivers
Prepare a full calculated excel sheet for cost analysis year by year
Pay back period
Equity to dept ratio
Worldwide LCOE for Wind turbine

## Slide 10: 5. Timeline – Project Development Team
 | Milestone Plan of Team "Project Development" |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Description | OCT |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | NOV |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | Dec |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | Jan |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30 | 31 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30 | 31 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30 | 31
1. genral site analysis + Wind ressource analysis |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
1. Legal Framework Analysis |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
2. QGIS Analysis |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
3. Environmental Impact Assessment |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
4. Land Leasing Agreements |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
5. Transportation Study |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
6. Grid Connection Plan |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
7. Conflict of Interests |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
1. Project Setup |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
2. Wind Resource Data |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
3. Layout Design |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
4. Compliance Optimization |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
5. Final Calculation |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
1. Setup of the calculation tool |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
2. Collecting all the input parameters |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
3. Collecting all the cost of the components |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
4. Simulating the AEP |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
5. Calculating the LCOE |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
6. Final Economic Assessment |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Buffer |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Buffer |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Buffer |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Luis Urhahn
Final presentation
Figure 3: Screenshot of the timeline – Project Development

## Slide 11: 6. Questions and Requests
Luis Urhahn
Questions:
Should we consider the possibility of a Wind Farm for our area?
  Especially regarding the WindPro simulation and LCOE calculation
Should we consider also Development Expenditures (DevEx) in the calculations?
  Maybe an approximation of every team's development costs?
Requests:
Every component team, please provide the costs of the component as soon as possible!
  We will discuss the costs over the next weeks to make sure we will get a cost-efficient WTG.
  You need to add the costs in the results file!

## Slide 12: 6. Questions and Requests
Luis Urhahn
You will find the list here: result file.xlsx
Figure 4: Screenshot of the result file in excel

## Slide 13: Bibliography – Project Development
Luis Urhahn
[1] Google, Google Maps. [Online]. Available: https://maps.google.com
[2] Google, Google Earth. [Online]. Available: https://earth.google.com/web/search/34%c2%b041%2749.6%22N+36%c2%b030%2730.0%22E/@34.67531382,36.5980701,506.39690821a,3513.70885844d,35y,360h,0t,0r/data=CiwiJgokCTkQ2iOXWkFAEQndzvkBWEFAGYw3RwMnREJAIQJ6D_SHPUJAQgIIAUICCABKCAjMjOyYBRAA
[3] Global Wind Atlas, Global Wind Atlas. [Online]. Available: https://globalwindatlas.info/en/.
[4] Open Infrastructure Map, OpenInfraMap. [Online]. Available: https://openinframap.org/#10.04/33.2058/36.2058.
[5] Shared files from the contact of Laurence Alhrshy. [Documets]
[6] Weibull distribution function and wind power statistics, ResearchGate. [Online]. Available: https://www.researchgate.net/publication/234452780_The_Weibull_distribution_function_and_wind_power_statistics
[7] „Introduction to wind turbine aerodynamics“, Alois Peter Schaffarczyk [online book].
[8] WindPro, University License for WindPro [Software]
[9] QGIS, Public Software of QGIS [Software]