## Slide 1: Weekly report: Team Project Development
Group members: Luis Urhahn, Ahmed Sallam, Ceren Cetin, Sohail Mansuri
Presenter:Sila Ceren Cetin
Week number: 06
Date: 03/11/2025
Supervisor: Dr. Marina Blohm

## Slide 2: Tasks of the week
Sila Ceren Cetin
Update on the electricity prices/LCOE in Syria
Progress: WindPro Simulation
Logistics
QGIS

## Slide 3: Update electricity prices Syria
Sila Ceren Cetin
Research on the current electricity prices in Syria:
  Households: 1.6 €Cents/kWh
  Industry: 4.6 €Cent/kWh
The Syrian Pound has a volatile and variable exchange rate, making a precise conversion unreliable.
[2] Source: Syria energy prices | GlobalPetrolPrices.com
Worldwide LCOE for Wind turbine (onshore, 2024):
  LCOE: 4.3 – 9.2 €Cents/kWh
[3] Source: https://www.ise.fraunhofer.de/content/dam/ise/en/documents/publications/studies/EN2024_ISE_Study_Levelized_Cost_of_Electricity_Renewable_Energy_Technologies.pdf
Shows that our turbine needs to be very cost-efficient!

## Slide 4
Sila Ceren Cetin
Rough estimation of wind turbine Price
Project development lecture
Determining the true price of a 5 MW wind turbine is challenging due to differences between manufacturers.
Initial cost estimation for calculations is set at 6.5 million euros.
Price range for 5 MW turbines from different manufacturers is 5.5 to 7 million euros.

## Slide 5
Sila Ceren Cetin
The initial assumptions and inputs for our Excel sheet
Electricity price based on Syria’s Electricity Law No. 32 (2010): guaranteed at 8 cent€/kWh for first 2 years
If annual production exceeds 2500 hours, price adjusted by formula; otherwise, remains at 8 cent€/kWh
European O&M cost reference: 1.2–1.5 cent€/kWh (Germany, Spain, UK, Denmark)
[4]
Cost breakdown: 55% investment (CAPEX), 45% operational expenses (OPEX), maintenance = 25% of OPEX
Own source

## Slide 6
Sila Ceren Cetin
The main structure and the calculations of NPV and discount rate
Own source

## Slide 7: Progress: WindPro Simulation
Sila Ceren Cetin
Wind Ressource Implementation in the WindPro model:
  Long Term Data – ERA5 (Gaussian Grid)
    1995 up to 2025, 30 years
    Different from measured data (lower)
    8 km from location
  Lonf Term Data – ERA5(T) (Rectangular Grid)
    30 years, very similar to first LTD, 13 km
  Trying to include the measured data
    Failed so far, need to review again
  Including StatGen
    For the generation of Wind Statistics
  Including ResGen
    For the generation of Wind Energy Resources
    Need to try again with measured data
  Setup of WTG
    Starting with 5 MW turbine (SG 5.0-145 @ HH102m, for assumption)
    Will be echanged when final turbine data available
Figure 1: Screenshot of the wind rose at 100m in WindPro [8]
Figure 2: Screenshot of the Weibull distribution at 100m in WindPro [8]

## Slide 8: Progress: WindPro Simulation
Sila Ceren Cetin
Figure 3: Screenshot of the Optimus Turbine location [8]
Critical to build a larger Wind Farm
  Close to the buildings
  Close to the powerline

## Slide 9: Wind Turbine Cost Distribution in Turkey
[8]

## Slide 10: Transportation: Tartus Port-Homs City
Military checking point should be removed: 8
Bridge has to be supported: 7
Concrete/block/material/stockpile removal: 7
Road/bypass/turn/exits/layout intervention: 8
Electric wires and Telephone cable should be moved up: 1
Road leveling is needed: 1
[7]

## Slide 11: Progress : Detaile Site Analysis (QGIS)
Sila Ceren Cetin
[9]]

## Slide 12: Bibliography – Project Development
[1] WindPro, University License for WindPro [Software] (latest on 30.10.25)
[2] Syrian Energy Prices, GlobalPetrolPrices. [Online]. Available: Syria energy prices | GlobalPetrolPrices.com (latest on 28.10.25)
[3] Study Levelized Cost of Electricity Renewable Energy Technologies, ISE-Fraunhofer [Document]. https://www.ise.fraunhofer.de/content/dam/ise/en/documents/publications/studies/EN2024_ISE_Study_Levelized_Cost_of_Electricity_Renewable_Energy_Technologies.pdf (latest on 28.10.25)
[4] https://www.wind-energy-the-facts.org/operation-and-maintenance-costs-of-wind-generated-power.html
[5] https://english.enabbaladi.net/archives/2025/09/loans-starting-at-e50-million-offered-for-renewable-energy-projects-in-syria/ [6] Damacus university shared files IRENA_Power_Generation_Costs_2021_pdf
[7] Inspection road between Tatous and dier Ali power plant, unpublished report, 2025.
[8] Wind Turbine Prices, Cost Analysis, and 1 MW Turbine Profit - Comprehensive Guide," Aldatmaz Global, [Online]. Available: https://aldatmazglobal.com/ruzgar-turbini-fiyatlari-maliyet-analizi-ve-1-mw-turbin-kazanci-kapsamli-rehber/. [Accessed: 30- Oct- 2025]
[9] QGIS, Public Software [Software]
Sila Ceren Cetin