## Slide 1: Team 5 – Rotor Blade Structures
Presented by – Dongsuk Kim(770143)
Team Members - Bhima B Masare, Anudeep Allanki, Dongsuk Kim, Mithun Shetty
Week No - 6
Date - 04.11.2025
Supervisor - Dr. Laurence Alhrshy

## Slide 2: Contents
Rotor Blade Structures Team Time line
Team Responsibilities and Output Flow
Temporary Structural Design limits for 80m Blade
Material selection for 80m Blade
4.1 Design limit and comparison
4.2 Main Blade Materials and Cost
4.3 Cost Reduction Strategies
Bibliography
Dongsuk Kim

## Slide 3
1. Rotor Blade Structures Team Time line
1.1 From Oct to Nov
Dongsuk Kim

## Slide 4
Dongsuk Kim
2. Tem responsibilities and Output Flow–
Rotor Blade Design Team
Output
Rotor Blade Structure Team
Load & Dynamics Team
Airfoil sequence
Chord length(m)
Relative thickness(t/c)
Twist distribution(deg)
Design Tip Speed Ratio(TSR)
Power coefficient(cp)
Radial positions(m)
Yes
Yes
No
No
Deflection, δ(r) / δ_tipChord
Spar Cap Thickness, t_spar(r)
Elastic Modulus, E_L
Mass Distribution
Static Load Cases
Dynamic Load Cases, DLC
Natural Frequencies
RD 160m
HH 120m
Fixed
Optimus
WTG 5MW
Fixed
BEM
EB Theory
SLC,DLC
Fixed

## Slide 5
Dongsuk Kim
3. Temporary Structural Design limits for 80m Blade –
No. | Parameter | NREL 5 MW (61.5 m Blade) | Scaling (Calculation Method) | Optimus Syria 5MW (80 m Blade) | Remark
1. | Tip Deflection Limit (δ_tip,max) | 8 m (≈ 0.13 · R) | Proportional to Blade Length (R₈₀/R₆₁.₅ = 1.30) | ≈ 10 m (0.125 · R) | Structural limit for stiffness design
2. | First Aerodynamic Profile Location (r/R) | 0.08 – 0.10 | Non-dimensional (no scaling) | 0.10 (allowable 0.08 – 0.12) | 0 – 0.10 R = structural root (Non-dimensional ratio,)
3. | Maximum Chord (C(max)) | 4.65 m | Manufacturing / transport limited; not strictly ∝ R | ≤ 5.0 m (recommended 4.9–5.0 m) | 5 m is practical for mold and road transport width limits.
4. | Maximum Twist Angle (θ(max)) | ~14.5° | Manufacturing limit (mold and laminate lay-up complexity) | ≤ 18° (recommended 16–18°) | Twist > 20° causes tooling issues; limit gradient ≈ ≤ 2° per 5 % span.
5. | Blade Mass (per Blade) | ≈ 18 t @ 61.5 m | Mass ∝ (R₈₀/R₆₁.₅)³ = (1.30)³ ≈ 2.2 × m₆₁.₅ | ≈ 35 – 40 t | Weight scaling estimate
6. | Tip Clearance Guide | ≈ 4 m | Scaled by R ratio (×1.3) | ≥ 5 m | To avoid tower strike under load
7. | Manufacturing Guide for Spar Cap Thickness | t_tip ≥ 2 mm, t_root ≤ 60 mm | Scaled by R ratio (×1.3) | t_tip ≥ 3 mm, t_root ≤ 80 mm | Manufacturing envelope
8. | Estimated Spar Cap (h_cap) | h_cap ≈ 0.6 · (t/c) · chord | Empirical relation maintained | h_cap ≈ 0.6 · (t/c) · chord | To be confirmed after geometry fix
※ All scaled values are based on geometric similarity: geometry ∝ R, mass ∝ R³, loads ∝ R³, Keeping t_spar ∝ R maintains similar stress and deflection behavior so the new limits (e.g., δ_tip ≈ 10 m) are physically consistent with the NREL 5 MW reference

## Slide 6
Dongsuk Kim
4. Material selection for 80m Blade–
4.1 Design limit and comparison –
Source: https://doi.org/10.1016/j.marstruc.2020.102858
Airfoil Structure | Blade Region | NREL 5 MW (61.5 m) | Optimus 5NW (80.0m) | Reason
 | Spar Cap | Hybrid Carbon + Glass UD (0°) | Full Carbon UD (0°) | - Higher bending moment. - Increase EI and reduce tip deflection & mass.
 | Shell (Suction/Pressure) | Glass Triax (±45/0/90) Lay-up: [±45 / 0 / 90 / ±45 / 0]ₛ | Glass Triax (±45 dominant) Lay-up: [±45 / 0 / ±45 / 90 / ±45 / 0 / ±45]ₛ | - More ±45° plies increase torsional stiffness (GJ) - shear resistance for longer, flexible blades.
 | Shear Webs | Glass ±45 + thin foam core Lay-up: [±45/G] + Core + [±45/G] | Glass ±45 + thicker foam core (50 → 80 mm) Lay-up: [±45/G] + Core(↑t) + [±45/G] | - Shear load ↑ → thicker core improves shear stiffness & buckling resistance.
 | Core (in Shell) | PVC / Balsa Foam (ρ ≈ 60 kg/m³) | High-density PVC or PET Foam (ρ ≈ 80–100 kg/m³) Thickness tapered along span | - Prevent shear failure & skin buckling under higher spanwise loads.
 | Trailing Edge (TE) | Glass + thin foam core Lay-up: [±45 / 0]ₛ + core | Glass + thicker foam + reinforcement patch Lay-up: [±45 / 0 / ±45]ₛ + core | Local buckling risk ↑; reinforced TE prevents opening, improves fatigue resistance.
 | Leading Edge (LE) | Glass + solid insert | Glass + Carbon Hybrid (optional) | - Improve impact, erosion resistance in longer blades.
 | Root Region | Thick Glass + Adhesive Joint | Glass + Carbon Hybrid (optional) | - Increase root strength and reduce weight for bolt interface.

## Slide 7
Dongsuk Kim
4. Material selection for 80m Blade –
4.2 Main Blade Materials and Cost –
E-glass fiber
Carbon fiber
Epoxy resin
Material | Main Features | Where Used | Unit Cost (€/kg) | Est. Weight of NREL5MW (kg) | Subtotal | Share
E-glass fiber | Strong, Low cost, Heavy | Shell skin, shear web, root reinforcements | 1.8 | ~13,000 | € 23,400 | 38%
Carbon fiber | High stiffness/strength, lightweight | Spar caps (load-carrying beam) | 25 | ~500 | € 12,500 | 20%
Epoxy resin | Excellent bonding, heat/chem. resistance | Matrix for all composites (fiber wet-out) | 4 | ~5,000 | € 20,000 | 33%
Core (PET/PVC/Balsa) | Lightweight sandwich material | Shell and shear web core panels | 4 | ~1,200 | € 4,800 | 8%
Adhesive & gel coat | Bonding, sealing, surface finish | Bond lines, LE/TE joints, outer surface | 10 | ~100 | € 1,000 | 1%
Total Material Cost (55%) |  |  |  | 19,800 | ≈ € 61,700 | 100%
+ Manufacturing (35%) |  |  |  |  | ≈ € 39,200 | 
+ Quality & Process (10%) |  |  |  |  | ≈ € 11,200 | 
= Total Production Cost (100%) |  |  |  |  | ≈ € 112,000 / blade | 
Source: Wind Turbine Reliability: A Database and Analysis Approach

## Slide 8
Dongsuk Kim
4. Material selection for 80m Blade –
4.3 Cost Reduction Strategies –
€ 112,000 * (1.3)³ =
Max € 246,000
€ 246,000 * 3 ea =
Min € 600,000 ~ Max € 738,000
Ⅰ. Material Optimization
- Less Carbon ↓
- More Glass ↑
- Replace PVC↔PET
Ⅱ. Geometric Simplification
- Reduce number of unique molds
Ⅲ. Manufacturing Process Efficiency
- High-speed infusion
- 3D Printing Automation
- Reuse of existing molds/platforms

## Slide 9: Bibliography
Dongsuk Kim
Definition of a 5 MW/61.5m Wind Turbine Blade Reference Model by Brian R. Resor, Sandia National Laboratories, California, USA
Definition of a 5 MW Reference Wind Turbine for Offshore System Development, J. Jonkman, S. Butterfield, W. Musial, and G. Scott, National Renewable Energy Laboratory, USA
Reports from Optimus Shakthi 2024
Lecture Scripts from Prof. Dr. Francesco Previtali
Lecture Scripts from Prof. Dr. Laurence Alhrshy
Structural analysis of an offshore vertical axis wind turbine composite blade experiencing an extreme wind load,Brian P, Hand, university College Cork, 09. 2020
Sandia National Laboratories Wind Turbine Blade Manufacturing Cost Studies (SAND2006-1100)