## Slide 1: List of contents
Bakhtyar Karim
Optimus effeciancy
  System effeciancy
  Final overall effeciancy
  Efficiency beyond the numbers
Detailed logistic strategy
  Syrian Permiting path
Power flow
  Necessary actions

## Slide 2
1. Optimus efficiency
Efficiency isn't just one number, it's a chain of events. Every time energy moves from one part to another, we lose a part of the energy we captured from wind
We calculate total efficiency by multiplying the efficiency of the Rotor (how well we catch the wind) by the efficiency of the Drivetrain (how well we convert it).
Rotor: Aerodynamic Capture ( Power Coefficient )
Drivetrain: Mechanical & Electrical Conversion
Bakhtyar Karim
[1] [2]

## Slide 3
1.i. System efficiency from rotor to grid
Tracing the power path through our specific components. Every step represents a conversion from kinetic to mechanical to electrical energy.
Key Insight: The Drivetrain (Gearbox + Gen + Elec) is 90.8% efficient. The main factor is the aerodynamic limit (Cp).
AERODYNAMIC
Rotor
Capture
Cp = 0.45
MECHANICAL
Gearbox
Speed Step up
η = 97.5%
ELECTRICAL
Generator
DFIG
η = 98.0%
GRID SIDE
Conv+Trans
Conditioning
η ≈ 97% & η ≈ 98%
FINAL OUTPUT
GRID
Delivery
Total = ?
Bakhtyar Karim
[1] [2]
ELECTRICAL

## Slide 4
1.ii. Final overall efficiency
Multiplying our Rotor efficiency ( Cp = 0.45 ) by our Drivetrain Efficiency (0.908):
40.9%
For every 100 kW of wind power that hits our rotor,
we deliver 40.9 kW of clean electricity to the Syrian grid.
Impact: This directly drives our Annual Energy Production (AEP) and lowers our LCOE.
Bakhtyar Karim
[1] [2]

## Slide 5
1.iii. Efficiency beyond the numbers
Efficiency isn't just about power conversion, it's about reliability and cost saving over 20 years. Here is how our "Smart Design" choices pay off.
Structural Efficiency
Lidar Assisted control
By "seeing" wind gusts before they arrive, we reduce structural stress by up to 50%. This means lighter blades and towers.
Thermal Efficiency
Custom cooling system
Designed specifically for Syrian heat. Keeps the gearbox and generator in their optimal efficiency range, preventing burnout.
Operational Efficiency
Automatic lubrication
Keeps the hub and pitch bearings healthy without stopping the turbine, reduces downtime, increasing total energy sold.
Bakhtyar Karim
[1] [2]

## Slide 6
Part 2: Critical project gaps
We have verified the efficiency, but we have major gaps in the Development Strategy.
Focus area: Project Development Team (PDT)
Bakhtyar Karim

## Slide 7
2. Detailed Logistics Strategy
We know the distance (85 km), but we lack the detailed plan for moving our 5MW wind turbine components.
Current Gaps
Route Survey: No detailed report on road quality, corners, or bridge load capacities between Tartus and Qattinah.
Costing: Missing precise transport costs for "Heavy Lift" operations.
Project Development team:
Provide a detailed Logistics Study & Cost Report by as soon as possible.
Bakhtyar Karim
[1] [2]

## Slide 8
2.i. The Syrian Permitting Path
We know what to build (IEC Standards), but the PDT has not defined how to get permission to build it in Syria.
License to Operate
What is the exact application process with the Ministry of Electricity?
Grid Connection
What are the terms for the PETDE Interconnection Agreement?
Local EIA
We have the map, but what is the official Syrian Environmental Impact Assessment procedure?
Bakhtyar Karim
[1] [2]

## Slide 9
Part 3: Electrical integration
Connecting the components: The Hardware (EDT) vs. The Brain(GCD).
Focus Area: EDT & GCD
Bakhtyar Karim

## Slide 10
3.i. Power flow
The missing link is the detailed definition of this interaction.
Storage
Managed by GCD Logic
Bakhtyar Karim
[1] [2]

## Slide 11
3.ii. Necessary actions: EDT & GCD
To close this gap, we need specific outputs from both teams by Week 10.
EDT Team (Hardware)
GCD Team (Logic)
Cable Sizing: Finalize calculations for the DC/AC Link cables and Grid Connection cables.
Physical Layout: Where do the cables go, especially in the nacelle?
Switchgear: Select the specific protection devices.
EMS Logic: Define the "If/Then" rules for the battery.
Simulink Model: Prove the logic works in simulation.
Connection Agreement: What does PETDE require at the connection point?
Bakhtyar Karim
[1] [2]

## Slide 12: Bibliography / Managment Team / PM
[1] All previous weeks presentations
[2] Final result file shared across all teams
Bakhtyar Karim