## Slide 1: Weekly report: Feedback Controller
Week number: 02
Date: 07/10/2025
Supervisor: Prof. Dr.-Ing. David Schlipf
Group members: Mirza Dincer, Saurabh Pankaj Jha
Presenter: Mirza Dincer

## Slide 2: List of Contents
Tasks of the Week
Why IEA 3.4 MW?
ROSCO Workflow
Simulation Settings
Results
Conclusion
Mirza Dincer - 780261

## Slide 3: Tasks of the Week
Migrate files of IEA 3.4-MW model to OpenFAST v3.0 and ROSCO v2.6.0 due to them being compatible for Lidar applications
Run Simulation of the IEA 3.4-MW with feedback-only control without Lidar-Assisted controller.
Mirza Dincer - 780261

## Slide 4: Why IEA 3.4 MW ?
Mirza Dincer - 780261
[1]
Rated power capacity: 3.4 MW, designed for utility-scale wind energy generation.
Supports advanced control strategies such as individual pitch control and yaw optimization.
ROSCO implementation allows research-driven improvements and customization for specific turbine control requirements.
Facilitates simulation and testing through OpenFAST.
Clean and well documented example to start.

## Slide 5: ROSCO Workflow
DLL (Dynamic Link Library)
Linked via ServoDyn.
Manages I/O between OpenFAST and control logic.
IN (Controller Input)
Parameter file for the DLL.
Holds feature flags, modes, gains.
Mirza Dincer - 780261
[2]
Standard ROSCO workflow showing controller structure and interaction between OpenFAST and ROSCO.

## Slide 6: Simulation settings
30 seconds of simulation.
Wind speed with 12 m/s, ‘Mexican Hat’ shaped gust up to 15 m/s.
Only enabled Rotor DOF and First fore-aft tower bending-mode DOF.
Set initial conditions of rotor speed, pitch angle, tower top positions. So that turbine starts in steady state.
Running only feedback controller, no Lidar-assisted controller.
Mirza Dincer - 780261

## Slide 7: Results
Mirza Dincer - 780261
Simulation results for IEA 3.4 MW with feedback control.

## Slide 8: Conclusion
Learned how to couple ROSCO and OpenFAST.
Learned how to update OpenFAST files and ROSCO.
Should discuss with load and dynamics team for OpenFAST version for the project.
Will be updating GitHub simulation files.
Mirza Dincer - 780261

## Slide 9: Bibliography – Feedback Controller
[1] P. Bortolotti et al., “IEA Wind TCP Task 37: Systems Engineering in Wind Energy - WP2.1 Reference Wind Turbines,” OSTI OAI (U.S. Department of Energy Office of Scientific and Technical Information), May 2019, doi: https://doi.org/10.2172/1529216.
[2] N. J. Abbas, D. S. Zalkind, L. Pao, and A. Wright, “A reference open-source controller for fixed and floating offshore wind turbines,” Wind Energy Science, vol. 7, no. 1, pp. 53–73, Jan. 2022, doi: https://doi.org/10.5194/wes-7-53-2022.