## Slide 1: Weekly report: Machine Bed & Yaw System
Shoukat Abbas, Luksh Chawla, Sathishkumar Venkatachalam, Shrihari G Kadam
Week No - 6
Date: 04.11.2025
Supervisor: Prof. Peter Quell
Presented by – Luksh Chawla

## Slide 2: Contents
Luksh Chawla
Number of Yaw Drives Calculation
Number of Yaw Drives – Syria
Yaw Bearing type
Machine Bed 2D sketching with proper Dimensions
References

## Slide 3: Number of Yaw Drives Calculation
Luksh Chawla
Bonfiglioli 716 T4 drive (suggestion).
Assumptions:
Pitch circle diameter of yaw bearing PCD Bearing(Syria) =3800 𝑚𝑚
Nominal torque: 90 kNm
Pitch circle diameter of pinion PCD Pinion=288 𝑚𝑚
Operational yaw moment Mz,op(Syria)= 7164 kNm
Pinion module= 24
Pinion teeth number = PCDpin/Pinion module=288/24=12

## Slide 4: Number of Yaw Drives – Syria
Luksh Chawla
Bearing teeth number =(PCDbearing)/ Bearing module =3800/24 = 158.33
rounded to 158.
The external gear ratio (iex) PCD Bearing = Bearing module × Bearing teeth number = 24 × 158 = 3792mm iex = PCDBearing /PCDPinion=3792/288 = 13.16
The number of yaw drives (N) is determined using the following formula: N=Total yaw moment/Each drive nominal torque × iex N =7164/90 × 13.16 = 6.04 rounded up to 6 no of yaw drives
Source: Bonfiglioli 716 T4F + BE160 + DGM Inverter [1]

## Slide 5: Yaw Bearing (Double-row 4-point Bearing)
Luksh Chawla
Advantages –
Matches a larger tower-top geometry
High tilting moments for future load revisions
Sized for high loads
Conservative margin & system integration
Disadvantages –
Approximate and needs vendor verification
Higher cost/lead time and potential custom work
Upscaling by section modulus is approximate
Thyssenkrupp Double-row four-point yaw bearings (Series 09) [2]

## Slide 6: Double row 4 - Point Bearing (External Gearing)
Luksh Chawla
Why does this choice fit Optimus Syria?
Tower-top diameter is 3.8 m (very close to Shakti’s final ~4.0 m PCD choice).
Similar interface and allows standard gear teeth dimensions/pinion geometry
Tilting moments are likely closer to Shakti’s loads
Double row four-point slewing bearing with external gearing (ThyssenKrupp style)
Sized close to the tower top / pitch-circle diameter (PCD)

## Slide 7: Bed Casting - 2D Dimension Defined
Luksh Chawla
Note: For Defining of Dimension, we utilize Optimus 92LE Concept 2D drawing. [3]

## Slide 8: Bed Casting - Updation
Luksh Chawla
1. Shaft Dimension - Looking for the proper dim. values of a shaft to fix the total length of the bed.
2. Yaw drives & Bearing - As per the calculation, we are going to use 6 yaw drives. Bed design update in progress.
3. Main Bearing and Gearbox Fixing Details Needed.
4. 3D Model on process - Reference Senvion MM92

## Slide 9: References
Luksh Chawla
[1]. Bonfiglioli (accessed 19 Oct 2025). Solutions for Wind. https://www.bonfiglioli.com/_default_upload_bucket/TR_CAT_WIND_STD_ENG_R05_0.pdf
[2]. WEC Development Project: Optimus Shakti 5.0 Machine Bed and Yaw System Final Report.
[3]. Master Wind Engineering Project Optimus 92LE Machine Bed and Yaw System