## Slide 1: Weekly report: Foundations
Week number: 11
Date: 09/12/2025
Supervisor: Prof. Dr.-Ing. Torsten Faber
Group members : Jehad Albaali- Amgad Gerges - Reda Deif
presented by : Jehad Albaali

## Slide 2: List of contents
Reasons for Design Pedestal
Bolt Tension Verification
Reinforcement Details
Complete Foundation Cost Breakdown
References
Foundations team/ Optimus Syria
Jehad Albaali

## Slide 3
Concrete Dimensions
Foundations team/ Optimus Syria
Diameter of Base Plate (BP) = 25 m
Diameter of Pedestal = 7 m
Height Pedestal = 1.5 m
Height of Middle slab = 2 m
Height of Frustum (HF) = 1.5 m
Height of Edge slab (HE) = 0.5 m
Jehad Albaali

## Slide 4
Reasons for Design Pedestal
Foundations team/ Optimus Syria
Improved load transfer from the tower to the foundation
Strengthening the critical upper concrete zone and enhancing cone-shear resistance
Better bending-moment distribution and reduced structural deformations
Higher pull-out capacity and confinement for anchor bolts
Enhancing anchor-cage performance and increasing its structural safety margin
High-precision tower alignment (±2 mm per IEC).
Safe and efficient installation workspace for anchor cage & bolt tensioning.
Jehad Albaali

## Slide 5
Bolt Tension Verification
Foundations team/ Optimus Syria
Jehad Albaali

## Slide 6
Reinforcement Details
Foundations team/ Optimus Syria
Jehad Albaali
Figure created by the author (AutoCAD, 2025)

## Slide 7
Reinforcement Details
Foundations team/ Optimus Syria
Jehad Albaali
Figure created by the author (AutoCAD, 2025)

## Slide 8
Reinforcement Details
Foundations team/ Optimus Syria
Jehad Albaali
Figure created by the author (AutoCAD, 2025)

## Slide 9
Reinforcement Details
Foundations team/ Optimus Syria
Jehad Albaali
Figure created by the author (AutoCAD, 2025)

## Slide 10
Reinforcement Details
Foundations team/ Optimus Syria
Jehad Albaali
Figure created by the author (AutoCAD, 2025)

## Slide 11
Foundations team/ Optimus Syria
Jehad Albaali
Complete Foundation Cost Breakdown
Foundation Specifications
Concrete volume: 1,121 m³
Reinforcement steel: 49.4 tons
Anchor bolt cage: 4.0 tons
Grout volume: 0.54 m³
Total foundation area: 491 m²
Unit Pricing Structure
Concrete + labor + formwork: €182/m²
Reinforcement steel: €595/ton
Anchor bolts: €2,273/ton
Grout materials: €727/m³
Detailed Cost Calculations
Concrete & Labor
Includes all concrete materials, labor costs, and formwork installation for the 491 m² foundation area.
Reinforcement Steel
Total cost for 49.4 tons of reinforcement steel required for structural integrity.
Anchor Bolt Cage
Specialized anchor system weighing 4.0 tons to secure the turbine tower to the foundation.
Grout Materials
High-strength grout for final anchor bolt installation and load distribution.
€128,240
Total Foundation Cost
Complete construction cost including all materials and labor
€261
Cost per Square Meter
Average cost per m² of foundation area (128,240 ÷ 491)

## Slide 12
References
Foundations team/ Optimus Syria
Jehad Albaali
IEC 61400-6: Wind Turbines – Tower and Foundation Design Requirements, IEC (2020).
EN 1992-1-1: Eurocode 2 – Design of Concrete Structures, CEN.
EN 1993-1-8: Eurocode 3 – Design of Steel Structures, CEN.
Bautabellen für Ingenieure ( mit Berechnungshinweisen und Beispielen )