## Slide 1: Weekly report: Machine Bed & Yaw System
Shoukat Abbas, Luksh Chawla, Sathishkumar Venkatachalam, Shrihari G Kadam
Week No - 11
Date: 09.12.2025
Supervisor: Prof. Peter Quell
Presented by – Shrihari G Kadam

## Slide 2: Contents
Shrihari G Kadam
Calculation of Brake Caliper
Calculation of Braking Torque
No. of Brake calipers
Yaw Brake Disk Modification
Yaw System Finalization
Machine Bed Modification and Rear bed (welded part) concept design
References

## Slide 3: Calculation of Brake Calipers & Braking Torque
Shrihari G Kadam
Clamping Force Determination
Clamping force taken from manufacturer’s performance graph (Svendborg BSAB-120).
Operating pressure: 16 MPa.
At 16 MPa and μ = 0.35, the graph gives a clamping force of: FC ≈ 543 kN Calculation of Braking Force (FB) Formula (manufacturer catalogue): FB = 2 × μ × FC
Where:
μ = coefficient of friction = 0.35
FC = Clamping force = 543 kN
FB = Braking force = 380.1 kN
[1]

## Slide 4: Calculation of Brake Calipers & Braking Torque
Shrihari G Kadam
source : Svendborg Brakes [1]

## Slide 5: Calculation of Brake Calipers & Braking Torque
Shrihari G Kadam
Calculation of Braking Torque (MB, caliper)
Manufacturer formula:
MB = FB × (Do − 0.136) / 2
Where:
FB = 380.1 kN
Do = brake disc outer diameter = 3.8 m
Substitution: MB = 696.16 kNm per caliper
Summary
Clamping force: 543 kN
Braking force: 380.1 kN
Braking moment: 696.16 kNm
[1]

## Slide 6: Calculation of Brake Calipers & Braking Torque
Shrihari G Kadam
Calculation of no. of brake calipers
    DLC 5.1 Normal Turbulence mode @25 m/s (cut-out speed)
Source: Load and Dynamics team Optimus Syria

## Slide 7: Calculation of Brake Calipers & Braking Torque
Shrihari G Kadam
Calculation of no. of brake calipers
  DLC 5.1 Normal Turbulence mode @25 m/s (cut-out speed)
    From the graph:
      Mz, yaw brake ≈ 10000 kNm
      a = no of brake calipers = Mz, yaw brake / MB
        = 1000 kNm / 696.16 kNm = 14.36
So, the number of brake calipers are 14 in Optimus Syria. Finalized numbers will be taken after confirmation from the Prof.
Source: Load and Dynamics team Optimus Syria

## Slide 8: Yaw Brake – Modification Diff.
Shrihari G Kadam
Modified New Brake
Old Model – With Extra Boss
Yaw brake disk

## Slide 9: Yaw system Finalization
Shrihari G Kadam
Yaw brake disk - 3D
Removed extra
Gears portions
Modified Design

## Slide 10: Machine Bed – Modification Diff.
Shrihari G Kadam
Machine Bed - 3D
We have clear gap now!!
Modified Drive
flange

## Slide 11: Rear Machine Bed – Concept
Shrihari G Kadam
* Optimus model- Modified dimension according to our casted bed - Concept Design

## Slide 12: Updated Machine Bed & Yaw System Ass.
Shrihari G Kadam

## Slide 13: References
Shrihari G Kadam
    [1]. Hydraulic brakes Svensborg brakes, https://www.svendborg-brakes.com/products/hydraulic-brakes/active-brakes/bsab-120/ (accessed: 13.11.2025)